## Slide 1: Caveability
Fundamentals of Block Caving Geomechanics
June 21-25 2010
Notes: <number>

## Slide 2: Outline
Conceptual model of a cave
Terminology
How rock masses cave (basics of caving mechanics)
Factors affecting caving (stress, strength, undercutting…)
Tools for prediction
Risks associated with high caveability
Risks associated with low caveability
Case studies

## Slide 3: Conceptual Model
Notes: <number>

## Slide 4: Conceptual Model of a Cave
Notes: <number>

## Slide 5: Conceptual Model
These zones are defined by differences in:
  Rock mass conditions
  Stress conditions
Notes: <number>

## Slide 6: Conceptual Model
Zone 1: Elastic Zone
  Rock mass conditions:
    Rock mass is still elastic and undisturbed.
  Stress conditions:
    Stresses in this zone lie below the damage threshold and are generally close to in situ values
Notes: <number>

## Slide 7: Conceptual Model
Zone 2: Seismogenic Zone
  Rock mass conditions:
    Rock is being damaged/disturbed through (1) slip on pre-existing joints and faults and (2) growth of new fractures, resulting in microseismic activity.
  Stress conditions:
    Stresses in this zone lie above the damage threshold and are generally high
Notes: <number>

## Slide 8: Conceptual Model
Zone 3: Yielded Zone
  Rock mass conditions
    Rock mass has experienced significant damage and has lost some or all of its cohesive and/or tensile strength as a result.
  Stress conditions
    Stresses in this region have exceeded peak strength and are generally low because the rock mass is at or near residual strength.
Notes: <number>

## Slide 9: Conceptual Model
Zone 4: Air Gap
  An air gap may only exist if the rock mass in the yielded zone still has some tensile/cohesive strength (i.e. not yet at residual strength).
Notes: <number>

## Slide 10: Conceptual Model
Zone 5: Mobilized Zone
  Rock mass conditions:
    Rock mass has lost all cohesive and tensile strength
    Rock blocks are moving toward the drawpoints in response to draw
    As the blocks move, they rotate relative to one another, leading to bulking.
  Stress conditions:
    Stresses are generally low inside the caved zone but can vary significantly depending on location relative to active draw.
Notes: <number>

## Slide 11: Terminology
Notes: <number>

## Slide 12: Bulking
Bulking – the increase in volume of a mass of rock when it has caved or been otherwise broken and removed from its in situ state
Bulking factor – the proportional increase in the volume of a mass of in situ rock when it has caved or bulked, usually represented by the symbol, B, so that an in situ volume, V, becomes a volume of V(1+B) on bulking.
in situ volume=V
caved volume=V(1+B)
caved porosity=n
bulking factor=B=n/(1-n)
swell factor=(1+B)=1+n/(1-n)
Notes: <number>

## Slide 13: Rock Mass Behavior (Pre-Peak)
Damage threshold – the stress limit (below the peak strength envelope) at which rock masses generally begin to experience joint slip and crack formation:
  Sigma1=Sigma3+(0.3 to 0.4)*UCSintact
Peak strength envelope – the limit of stress that the rock mass can carry, most simply defined by the Mohr-Coulomb criterion and a tensile strength:
  Sigma1=2c*(cos)/(1-sin)+Sigma3*(1+sin)/(1-sin)
  where c=cohesion and =friction angle
Notes: <number>

## Slide 14: Rock Mass Behavior (Pre-Peak)
Damage Threshold
Peak Strength
Envelope
Sigma 1-Sigma 3 plot of simulated rock mass test showing damage threshold and peak strength envelope
Stress path
Notes: <number>

## Slide 15: Rock Mass Behavior (Post-Peak)
Cohesion/tension-weakening (also known as strain-softening) – the loss of cohesive/tensile strength that accompanies shear/tensile yielding
Dilation – the bulking that accompanies shear yielding
Frictional-strengthening – the increase in frictional strength that accompanies dilation/bulking
Modulus softening – the decrease in modulus that accompanies dilation/bulking
Notes: <number>

## Slide 16: Basic Mechanics
Notes: <number>

## Slide 17: Basic Mechanics
Undercutting causes an increase in the horizontal stress (sh) above and below the undercut:
sh
sh’
Undercut
Notes: <number>

## Slide 18: Basic Mechanics
Undercutting also causes a decrease in the vertical stress (sv) above and below the undercut:
sv
sv’
Notes: <number>

## Slide 19: Basic Mechanics
sh’
sv’
Yielding and
weakening
If the difference between the two new stresses (sh’-sv’) is large enough, the rock mass will yield and weaken:
Notes: <number>

## Slide 20: Basic Mechanics
How does a rock mass yield and weaken under these conditions?
How does it turn from a cohesive rock mass to a disintegrated assembly of blocks?
We can simulate compression of a rock mass using PFC (Particle Flow Code). The intact rock is represented by bonded particles and the joints by low strength planar inclusions. A simple example….
Notes: <number>

## Slide 21: Basic Mechanics
sh’
sv’
Notes: <number>

## Slide 22: Basic Mechanics
Because the rock in the yielded zone has been completely weakened, it is capable of flowing and can be drawn out from the extraction level.
Caved (Mobilized)
Yielded
Extraction
level
Notes: <number>

## Slide 23: Basic Mechanics
If (sh’-sv’) remains sufficiently large, the yielded and caved zones will expand upward with continued draw: stress caving
Caved (Mobilized)
Yielded
sh’
sv’
Notes: <number>

## Slide 24: Basic Mechanics
If (sh’-sv’) is too small, an air gap will develop with continued draw:
sh’
Caved (Mobilized)
Air Gap
Notes: <number>

## Slide 25: Basic Mechanics
It is often possible in such cases for caving to continue via tensile failure in the back: gravity caving
Air Gap
Tension due to gravity
Caved (Mobilized)
Notes: <number>

## Slide 26: Basic Mechanics
If tension due to gravity is insufficient to cause collapse, a stable arch may form, even under significant drawdown:
Air Gap
Stable arch
Caved (Mobilized)
Notes: <number>

## Slide 27: Controlling Factors
Notes: <number>

## Slide 28: Factors Affecting Caving
Intact strength & modulus
Joint network geometry
Joint strength & stiffness
These factors impact rock mass strength
These factors impact induced stresses
Often not considered
Geology
Faults, dykes, etc.
In situ stress
Undercut size, shape and direction
Draw strategy
Adjacent mining
Water
Time dependence
Preconditioning strategies
Stochastic variations
Major structures
Spatial variations
Notes: <number>

## Slide 29: Tools for Prediction
Notes: <number>

## Slide 30: Tools
The following tools are commonly used to assist with caving prediction:
  Empirical models:
    Laubscher’s Caving Charts
    Extended Mathew Stability Graph
  Elastic numerical models, e.g.:
    Examine2D (Rocscience)
    MAP3D
  Inelastic numerical models, e.g.:
    FLAC2D/3D,UDEC/3DEC, PFC2D/3D (Itasca)
    Phases (Rocscience)
    Abaqus
Notes: <number>

## Slide 31: Laubscher Chart 1
Hydraulic Radius
=area/perimeter
Modified Rock Mass Rating (MRMR)
Considers:
Laubscher RMR, which is based on
Intact strength
RQD
Joint spacing
Joint condition
Plus adjustments for:
induced stress
joint orientation
Notes: <number>

## Slide 32: Laubscher Chart
Advantages
  Since the 1980s, Laubscher’s caving chart has been the major method used internationally to predict caveability in block and panel caving mines.
  It has been particularly successful when applied to the weaker and larger orebodies for which it was first developed.
Disadvantages
  Relatively small number of case histories
  It may not always provide satisfactory results for stronger, smaller and isolated or constrained blocks or orebodies.
  There may be insufficient guidelines available for the inexperienced user seeking to establish values of the adjustment factors to be applied to the RMR.
Notes: <number>

## Slide 33: Extended Mathews Method
Stability Number, N
N= Q’*A *B *C
Considers:
NGI Q’, which is based on
RQD
Number of joint sets
Joint roughness
Joint alteration
Plus adjustments for:
induced stress
joint orientation
gravity
Hydraulic Radius
=area/perimeter
Mawdesley (2002)
Notes: <number>

## Slide 34: Extended Mathews Method
(UCS)/
(induced stress)
Estimate induced stresses in cave back using elastic model or analytical solutions
Notes: <number>

## Slide 35: Extended Mathews Method
Advantages
  Larger number of case histories in higher quality rock.
  Provides detailed guidelines for the determination of the adjustment factors used.
Disadvantages
  Relatively new technique for caving prediction.
  More caving and transitional caving data are required to increase confidence in the use of this technique for predicting caveability
Notes: <number>

## Slide 36: Elastic Models
Features
  Represents rock mass as an elastic material
  Techniques can sometimes be used to approximate rock mass failure
Uses in caving prediction
  Analysis of pre-caving process from elastic to seismogenic
Advantages
  Relatively easy to use
  Very large problems can be modeled quickly
Disadvantages
  Cannot model the entire caving process (e.g. from seismogenic, to yielded, to caved)
Notes: <number>

## Slide 37: Elastic Models
Examine2D Elastic model of stresses around yielded zone
Notes: <number>

## Slide 38: Inelastic Models
Features
  Represents rock mass as an elastic-plastic material that can yield, weaken and flow
Uses in caving prediction
  Analysis of complete caving process from elastic, to seismogenic, to yielded, to caved
Advantages
  Provides much more information than elastic models, including expected shape and extent of all five zones
Disadvantages
  Requires skilled user and specialized algorithms
  Difficult/time-consuming to model very large problems
Notes: <number>

## Slide 39: Inelastic Models
Dots=Seismogenic zone
Blue=Yielded zone
White=Caved zone
Grey=Undercut
FLAC3D Inelastic
model of caving
Notes: <number>

## Slide 40
Example of a cave-scale predictive model (FLAC3D). This model of Northparkes Lift 2 incorporates rock mass properties derived from Synthetic Rock Mass (SRM) testing. The predicted caved zone is shown in gray and the yielded zone in blue. The yielded zone compares favorably with observed open hole blockages (red diamonds).
Inelastic Models
Notes: <number>

## Slide 41: Inelastic Models
Critical features of inelastic model required to accurately model caving process:
  Cohesion/tension weakening: to simulate disintegration
  Frictional strengthening: to account for the fact that caved rock often has higher friction angle (~40-45 degrees) than the rock mass
  Modulus softening: to account for the fact that caved rock has a lower modulus (~2 orders of magnitude lowerthan the rock mass
  Dilation: to allow for bulking inside the cave – dilation must shut off once the caved rock reaches its expected minimum density
Notes: <number>

## Slide 42: Predictions
Notes: <number>

## Slide 43: Seismogenic Zone
What useful information do seismogenic zone predictions provide?
  Seismic hazard assessment
    Seismogenic zone limits can be used to estimate if and where microseismic activity might be centered around infrastructure.
  Microseismic monitoring system design
    By knowing the likely locations of concentrated microseismic activity, the design and layout of the MS monitoring system can be optimized
Notes: <number>

## Slide 44: Seismogenic Zone
What tools should I use?
  Laubscher/Mathews charts
    Cannot be used
  Inelastic numerical models
    Available constitutive models do not generally account for damage before peak strength
    Limits must generally be inferred from stresses in the elastic zone using an empirical damage threshold criterion
  Elastic numerical models
    Empirical damage threshold can be used to estimate the seismogenic zone limits if the yield zone shape is assumed.
Notes: <number>

## Slide 45: Yielded Zone Prediction
What useful information do yielded zone predictions provide?
  Caveability
    Thin or non-existent yielded zone in the undercut/cave back indicates high potential for cave stalling
  Hazards to infrastructure
    Yield zone shape can be used to estimate if and where the yield zone might intersect infrastructure and cause damage.
  Caving rate
    The rate of upward advance of the yield zone is known as the “caving rate”
    This will help to develop a suitable rate of draw
  Open pit-underground transition
    Open pit operations should not continue in areas impacted by the yielded zone
Notes: <number>

## Slide 46: Yielded Zone Prediction
What tools should I use?
  Caveability
    Laubscher/Mathews charts
      Best choice to get initial estimate of caveability
    Inelastic numerical models
      Often needed for more in-depth feasibility assessment, particularly under more complicated conditions, e.g. with complex induced stresses, highly variable rock mass or highly anisotropic joint fabric
    Elastic numerical models
      Cannot be used
Notes: <number>

## Slide 47: Yielded Zone Prediction
What tools should I use (cont.)?
  Hazards to infrastructure & open pit-underground transition
    Laubscher/Mathews charts
      Cannot be used
    Inelastic numerical models
      Best choice because they are able to model the complex rock mass weakening associated with the yielded zone
    Elastic numerical models
      Can be used to roughly estimate the yielded zone thickness if the cave shape is assumed.
Notes: <number>

## Slide 48: Yielded Zone Prediction
What tools should I use (cont.)?
  Caving rate
    Laubscher/Mathews
      Some charts available
    Inelastic numerical model
      Best choice because it can account for the bulking associated with yielding that is known to have a significant impact on caving rate
    Elastic model
      Cannot be used
Notes: <number>

## Slide 49: Mobilized Zone Prediction
What useful information do mobilized zone predictions provide?
  Limits of potentially recoverable ore
    Some portions of the yielded zone will never mobilize!
    The mobilized zone encompasses all parts of the yielded zone that are likely to move in response to draw and is therefore useful for defining the limits of potentially recoverable ore (and waste!).
    Can be used as input to gravity flow simulators (e.g. PC-BC, REBOP) to optimize draw control.
Notes: <number>

## Slide 50: Mobilized Zone Prediction
What tools should I use?
  Limits of potentially recoverable ore
    Laubscher/Mathews
      Cannot be used
    Inelastic numerical models
      Best choice because it is possible to outline which portions of the yielded zone area may actually move in response to draw
    Elastic numerical models
      Cannot be used.
Notes: <number>

## Slide 51: Risks
Notes: <number>

## Slide 52: Risks
Poor caveability may lead to stalling, air gap development and the potential for catastrophic collapse.
Very good caveability may result in high caving rates and could jeopardize transition mining (e.g. in overlying open pit).
Unexpected cave shape may impact ore recovery and infrastructure stability.
Notes: <number>

## Slide 53: Case Studies
Notes: <number>

## Slide 54
Northparkes E26 Lift 1
Duplancic & Brady (1999)
Yielded
Zone
Seismogenic
Zone
Stresses low relative to strength therefore small yielded zone (~10-15 meters) and poor caveability.
Cave stalled before reaching ground surface.
Crown pillar collapsed catastrophically, causing damaging air blast.
Notes: <number>

## Slide 55
Northparkes E26 Lift 2
Deeper than Lift 1 therefore higher horizontal stresses. Resulted in large yield zone and good caveability in the west.
Stronger, more ductile rock (BQM) to the southeast resulted in unexpected cave shape and ore loss.
Notes: <number>

## Slide 56
Ridgeway
Weak fault to the North resulted in good caveability and unexpected cave shape
Oct 02
May 02
Mar 02
Nov 01
July 01
N
100m
N
100m
Host
Cap rock
Near surface cap rock
Notes: <number>

## Slide 57
Palabora
Base of open pit
Glazer & Hepworth (2004)
Yielded Zone
Seismogenic Zone
High stress relative to rock mass strength resulted in large yielded zone (~60-80 meters thick) and good caveability.
Notes: <number>