## Slide 1: Spread Spectrum

## Slide 2: Advantages of Spread Spectrum
Immunity from various kinds of noise and multipath distortion
Can be used for hiding and encrypting signals
Several users can independently use the same higher bandwidth with very little interference

## Slide 3: Direct Sequence Spread Spectrum (DSSS)

## Slide 4: Code-Division Multiple Access (CDMA)
Basic Principles of CDMA
  D = rate of data signal
  Break each bit into k chips
    Chips are a user-specific fixed pattern
  Chip data rate of new channel = kD

## Slide 5: Orthogonal Codes
Orthogonal codes
  All pairwise cross correlations are zero
  Fixed- and variable-length codes used in CDMA systems
  For CDMA application, each mobile user uses one sequence in the set as a spreading code
    Provides zero cross correlation among all users
Types
  Walsh codes
  Variable-Length Orthogonal codes

## Slide 6: Walsh Codes
Set of Walsh codes of length n consists of the n rows of an n ´ n Walsh matrix:
W1 = (0)
    n = dimension of the matrix
Every row is orthogonal to every other row and to the logical not of every other row
Requires tight synchronization
  Cross correlation between different shifts of Walsh sequences is not zero