## Slide 1: GSM

## Slide 2: Contents
• GSM-Introduction
• Architecture
• Technical Specifications
• Frame Structure
• Channels
Security
Characteristics and features
Applications

## Slide 3: What is GSM ?
Global System for Mobile (GSM) is a second generation cellular standard developed to cater voice services and data delivery using digital modulation

## Slide 4: GSM: History
• Developed by Group Spéciale Mobile (founded 1982) which was an initiative of CEPT ( Conference of European Post and Telecommunication )
• Aim : to replace the incompatible analog system
• Presently the responsibility of GSM standardization resides with special mobile group under ETSI ( European telecommunication Standards Institute )
Full set of specifications phase-I became available in 1990
• Under ETSI, GSM is named as “ Global System for Mobile communication “
• Today many providers all over the world use GSM (more than 135
countries in Asia, Africa, Europe, Australia, America)
• More than 1300 million subscribers in world and 45 million subscriber in India.

## Slide 5: GSM in World

## Slide 6: GSM System Architecture
BSC
BSC
MSC
MS
MS
MS
BTS
BTS
BTS
GMSC
PSTN
ISDN
PDN
EIR
AUC
HLR
VLR

## Slide 7: GSM System Architecture-I
Mobile Station (MS)
    Mobile Equipment (ME)
    Subscriber Identity Module (SIM)
Base Station Subsystem (BSS)
    Base Transceiver Station (BTS)
    Base Station Controller (BSC)
Network Switching Subsystem(NSS)
    Mobile Switching Center (MSC)
    Home Location Register (HLR)
    Visitor Location Register (VLR)
    Authentication Center (AUC)
    Equipment Identity Register (EIR)

## Slide 8: System Architecture Mobile Station (MS)
The Mobile Station is made up of two entities:
Mobile Equipment (ME)
2. Subscriber Identity Module (SIM)

## Slide 9: System Architecture Mobile Station (MS)
Mobile Equipment
Portable,vehicle mounted, hand held device
Uniquely identified by an IMEI (International Mobile Equipment Identity)
Voice and data transmission
Monitoring power and signal quality of surrounding cells for optimum handover
Power level : 0.8W – 20 W
160 character long SMS.

## Slide 10: System Architecture Mobile Station (MS) contd.
Subscriber Identity Module (SIM)
Smart card contains the International Mobile Subscriber Identity (IMSI)
Allows user to send and receive calls and receive other subscribed services
Encoded network identification details
- Key Ki,Kc and A3,A5 and A8 algorithms
Protected by a password or PIN
Can be moved from phone to phone – contains key information to activate the phone

## Slide 11: System Architecture Base Station Subsystem (BSS)
Base Station Subsystem is composed of two parts that communicate across the standardized Abis interface allowing operation between components made by different suppliers
Base Transceiver Station (BTS)
Base Station Controller (BSC)

## Slide 12: System Architecture Base Station Subsystem (BSS)
Base Transceiver Station (BTS):
Encodes,encrypts,multiplexes,modulates and feeds the RF signals to the antenna.
Frequency hopping
Communicates with Mobile station and BSC
Consists of Transceivers (TRX) units
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: System Architecture Base Station Subsystem (BSS)
Base Station Controller (BSC)
Manages Radio resources for BTS
Assigns Frequency and time slots for all MS’s in its area
Handles call set up
Transcoding and rate adaptation functionality
Handover for each MS
Radio Power control
It communicates with MSC and BTS

## Slide 14: System Architecture Network Switching Subsystem(NSS)
Mobile Switching Center (MSC)
Heart of the network
Manages communication between GSM and other networks
Call setup function and basic switching
Call routing
Billing information and collection
Mobility management
- Registration
- Location Updating
- Inter BSS and inter MSC call handoff
MSC does gateway function while its customer roams to other network by using HLR/VLR.

## Slide 15: System Architecture Network Switching Subsystem
Home Location Registers (HLR)
    - permanent database about mobile subscribers in a large service area(generally one per GSM network operator)
    database contains IMSI,MSISDN,prepaid/postpaid,roaming restrictions,supplementary services.
Visitor Location Registers (VLR)
    Temporary database which updates whenever new MS enters its area, by HLR database
    Controls those mobiles roaming in its area
    Reduces number of queries to HLR
    Database contains IMSI,TMSI,MSISDN,MSRN,Location Area,authentication key
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16: System Architecture Network Switching Subsystem
Authentication Center (AUC)
    Protects against intruders in air interface
    Maintains authentication keys and algorithms and provides security triplets ( RAND,SRES,Kc)
    Generally associated with HLR
Equipment Identity Register (EIR)
    - Database that is used to track handsets using the IMEI (International Mobile Equipment Identity)
    Made up of three sub-classes: The White List, The Black List and the Gray List
    Only one EIR per PLMN
Notes: <number>
<footer>
<header>
<date/time>

## Slide 17: GSM Specifications-1
RF Spectrum
GSM 900
Mobile to BTS (uplink): 890-915 Mhz
BTS to Mobile(downlink):935-960 Mhz
Bandwidth : 2* 25 Mhz
GSM 1800
Mobile to BTS (uplink): 1710-1785 Mhz
BTS to Mobile(downlink) 1805-1880 Mhz
Bandwidth : 2* 75 Mhz

## Slide 18: GSM Specification-II
Carrier Separation : 200 Khz
Duplex Distance : 45 Mhz
No. of RF carriers : 124
Access Method : TDMA/FDMA
Modulation Method : GMSK
Modulation data rate : 270.833 Kbps

## Slide 19: GSM Operation
Speech decoding
Channel decoding
De-interleaving
Burst Formatting
De-ciphering
Demodulation
Modulation
Ciphering
Burst Formatting
Interleaving
Channel Coding
Speech coding
Radio Interface
Speech
Speech
13 Kbps
22.8 Kbps
22.8 Kbps
33.6 Kbps
33.6 Kbps
270.83 Kbps

## Slide 20: Physical Channel

## Slide 21: GSM-Frame Structure

## Slide 22: Logical Channels
TCH
(traffic)
CCH
(control)
BCH
CCCH
Dedicated
2.4 kbps
4.8 kbps
9.6 kbps
FCCH(Frequency correction)
SCH(Synchronization)
PCH(Paging)
RACH(Random Access)
AGCH(Access Grant)
SDCCH(Stand Alone)
SACCH(Slow-associated)
FACCH(Fast-associated)
Half rate 11.4kbps
Full rate 22.8kbps
Speech
Data

## Slide 23: Call Routing
Call Originating from MS
Call termination to MS

## Slide 24: Outgoing Call
MS sends dialled number to BSS
BSS sends dialled number to MSC
3,4 MSC checks VLR if MS is allowed the requested service.If so,MSC asks BSS to allocate resources for call.
MSC routes the call to GMSC
GMSC routes the call to local exchange of called user
7, 8,
9,10 Answer back(ring back) tone is routed from called user to MS via GMSC,MSC,BSS

## Slide 25: Incoming Call
Calling a GSM subscribers
Forwarding call to GSMC
Signal Setup to HLR
5. Request MSRN from VLR
Forward responsible MSC to GMSC
Forward Call to current MSC
9. Get current status of MS
11. Paging of MS
13. MS answers
15. Security checks
17. Set up connection

## Slide 26: Handovers
Between 1 and 2 – Inter BTS / Intra BSC
Between 1 and 3 –
Inter BSC/ Intra MSC
Between 1 and 4 –
Inter MSC

## Slide 27: Security in GSM
On air interface, GSM uses encryption and TMSI instead of IMSI.
SIM is provided 4-8 digit PIN to validate the ownership of SIM
3 algorithms are specified :
- A3 algorithm for authentication
- A5 algorithm for encryption
- A8 algorithm for key generation

## Slide 28: Authentication in GSM

## Slide 29: Key generation and Encryption

## Slide 30: Characteristics of GSM Standard
Fully digital system using 900,1800 MHz frequency band.
TDMA over radio carriers(200 KHz carrier spacing.
8 full rate or 16 half rate TDMA channels per carrier.
User/terminal authentication for fraud control.
Encryption of speech and data transmission over the radio path.
Full international roaming capability.
Low speed data services (upto 9.6 Kb/s).
Compatibility with ISDN.
Support of Short Message Service (SMS).

## Slide 31: Advantages of GSM over Analog system
Capacity increases
Reduced RF transmission power and longer battery life.
International roaming capability.
Better security against fraud (through terminal validation and user authentication).
Encryption capability for information security and privacy.
Compatibility with ISDN,leading to wider range of services

## Slide 32: GSM Applications
Mobile telephony
GSM-R
Telemetry System
- Fleet management
- Automatic meter reading
- Toll Collection
- Remote control and fault reporting of DG sets
Value Added Services

## Slide 33: GSM Services
Tele-services
Bearer or Data Services
Supplementary services

## Slide 34: Tele Services
• Telecommunication services that enable voice communication
via mobile phones
• Offered services
- Mobile telephony
- Emergency calling

## Slide 35: Bearer Services
Include various data services for information transfer between GSM and other networks like PSTN, ISDN etc at rates from 300 to 9600 bps
Short Message Service (SMS)
  up to 160 character alphanumeric data transmission to/from the mobile terminal
Unified Messaging Services(UMS)
Group 3 fax
Voice mailbox
Electronic mail

## Slide 36: Supplementary Services
Call related services :
Call Waiting- Notification of an incoming call while on the handset
Call Hold- Put a caller on hold to take another call
Call Barring- All calls, outgoing calls, or incoming calls
Call Forwarding- Calls can be sent to various numbers defined by the user
Multi Party Call Conferencing - Link multiple calls together
CLIP – Caller line identification presentation
CLIR – Caller line identification restriction
CUG – Closed user group

## Slide 37: GSM Evolution
  2nd Generation
    GSM -9.6 Kbps (data rate)
  2.5 Generation ( Future of GSM)
    HSCSD (High Speed ckt Switched data)
      Data rate : 76.8 Kbps (9.6 x 8 kbps)
    GPRS (General Packet Radio service)
      Data rate: 14.4 - 115.2 Kbps
    EDGE (Enhanced data rate for GSM Evolution)
      Data rate: 547.2 Kbps (max)
  3 Generation
    WCDMA(Wide band CDMA)
      Data rate : 0.348 – 2.0 Mbps