## Slide 1
BluetoothTM Wireless Networking
Satish P.
Project Director and Head
Embedded Systems Group
Network Systems and Technologies (P) Ltd.

## Slide 2
Introduction
  What is Bluetooth wireless?
  What can it do for you ?
  How does it compare with other wireless technologies?
  Architectural overview of Bluetooth
  Basic components and network topologies
  Bluetooth protocols
  Security aspects
  Bluetooth profiles
Bluetooth market
  Products and applications
  Bluetooth qualification
Looking forward
Agenda

## Slide 3
What is Bluetooth ?
Bluetooth is a short-range wireless network originally intended to replace the cable(s) connecting portable and/or fixed electronic devices. Such a network is also sometimes called a PAN (Personal Area Network)
Bluetooth is supposed to got it’s name from Harald “Bluetooth” II, King of Denmark 940-981
The concept was first patented by Ericsson. Currently the Bluetooth trade mark is owned by the Bluetooth SIG, a consortium of companies having stake in Bluetooth
Key features are robustness, low power, and low cost.

## Slide 4: What Can Bluetooth Do For You?
Personal Ad Hoc Networks
Cable Replacement
Landline
Data/Voice Access Points

## Slide 5: Comparison with other wireless technologies
802.11
Has higher bitrate compared to Bluetooth . But has higher power consumption. Basic a LAN technology so not a direct competitor for Bluetooth
IrDA
Low cost but require Line of sight. Only point to point
HomeRF
Competing technology. But current Bluetooth is better positioned in market

## Slide 6: Bluetooth Architecture
Operates on the 2.4 GHZ ISM Band
Uses Gaussian Frequency Shift Keying Modulation scheme
Data is transmitted in packets during time slots which are of fixed duration
Uses Quick Frequency Hoping Packet Switched Protocol to achieve noise immunity
Connections can be made up to 10 meters or extended up to 100 meters
Maximum speed supported in Version 1 is 1 Mbps
Each Transceiver has a unique 48 Bit Address
Full Duplex communication is supported through Time Division Duplex (TDD)

## Slide 7: Network Topology
Radio Designation
  Connected radios can be master or slave
  Radios are symmetric (same radio can be master or slave)
Piconet
  Master can connect to seven simultaneous or 200+ active slaves per piconet
  Each piconet has maximum capacity (1 MSPS)
    Unique hopping pattern/ID
Scatternet
  High capacity system
    Minimal impact with up to 10 piconets within range
  Radios can share piconets!

## Slide 8: Packets and Frames
Spread spectrum frequency hopping radio
  79/23 one MHz channels
  Hops every packet
    Packets are 1, 3 or 5 slots long
  Frame consists of two packets
    Transmit followed by receive
  Nominally hops at 1600 times a second (one slot packets)

## Slide 9: Basic Blocks

## Slide 10: Bluetooth Protocol Stack
Key aspects
Interoperability
Different Applications can run over Different Protocol Stacks
Open Interface
Protocol Divided Into 4 layers

## Slide 11: Bluetooth Protocol Stack

## Slide 12: Bluetooth Profiles
Profiles are basically usage models defined by the SIG to ensure that Bluetooth devices and applications developed by different vendors are interoperable
Some examples of profiles are
File transfer Profile
Dial Up Networking Profile
Head Set profile
Hands free Phone Operation profile
Human Interface Device ( HID) Profile etc

## Slide 13: Bluetooth Qualification
BQA
Adopter (Manufacturer)
BQTF
BQB
Qualified
Products
List
Declarations and
documentation
reviewed
Product
tested
Documents
pulled from
Web site
Test report
checked by
BQB
Qualification
Program
Documents

## Slide 14
Inquiry
Page
Connected
AMA
Transmit
data
AMA
T
typical=0.6s
T
typical=2s
HOLD
AMA
PARK
PMA
T
typical=2 ms
T
typical=2 ms
Releases
AMA
Address
Low Power
States
Active
States
Standby
Connecting
States
Unconnected
Standby
Detach
Connection Sequence
Standby
  Waiting to join a piconet
Inquire
  Ask about radios to connect to
Page
  Connect to a specific radio
Connected
  Actively on a piconet (master or slave)
Park/Hold
  Low Power connected states

## Slide 15
Supports Unidirectional or Mutual Encryption based on a Secret Link key Shared Between Two Devices
Security Defined In 3 modes:
  Mode1- No Security
  Mode 2 - Service Level Security: Not Established Before Channel is Established at L2CAP
  Mode 3 - Link Level Security: Device Initiates Security Before LMP Link is Setup
Bluetooth Security

## Slide 16
Blueooth Target Markets
The first wave
1. PC, Notebooks
2. Organizers & Palm Computers
3. Headsets
4. Cellular/ PCS
5. Cordless phones
6. Automotive cellular
7. Digital cameras
The second wave
1. Printers
2. Photo printers
3. Fax machines
4. Industrial, musical and vertical industries products

## Slide 17
Blueooth Target Markets

## Slide 18
Key Players
Ericsson
IBM
Intel
Nokia
Toshiba

## Slide 19
Looking Forward
Version 1.2 Ready for release
  Adaptive Frequency hopping for better noise immunity
  Better security and audio processing features
Version 2.0
  Still on the anvil
  Proposed to support medium ( 2-3 Mbps) and high bit rates (12 Mbps)

## Slide 20: References
www.bluetooth.com
www.bluetooth.org
www.wireless-communication.org/bluetooth/
Bluetooth - Connect without Cables
Jennifer Bray and Charles F Sturman
(Prentice Hall)