## Slide 1: UMTS

## Slide 2: 3G UMTS
Contents
  Why 3G
  UMTS
  Use of UMTS at the moment

## Slide 3: 3G UMTS
The Dream (intention)
  2G and 2.5G systems are incompatible around the world.
    Worldwide devices need to have multiple technologies inside of them, i.e. tri-band phones, dual-mode phones
  To develop a single standard that would be accepted around the world
    One device should be able to work anywhere !
“Access to Information from Anyplace, Anytime”

## Slide 4: 3G UMTS
The Dream (continued)
  Worldwide positioning available
    Able to pinpoint a device and direct services to it.
    Mostly to be used for “Push” services
  Increased data rate
    Maximum 2048Kbps
  Operational
    in Europe by 2002
    Japan 2001 (this was achieved)
    Worldwide usage by 2005 (not going to happen)

## Slide 5: 3G UMTS
The reality
  Different standards with some operators in America and the rest of the world
  In the future market forces may move towards a single standard
    i.e. VHS and Betamax video tapes
  Difficulties
    World wide identical available spectrum
    Agreement on the encoding/decoding technique used
    Local influence groups
      Manufacturers who have invested in one technology

## Slide 6: 3G UMTS
Standard
  The 3G stand was written by the International Telecommunication Union (ITU)
    The standard was referred to as IMT-2000
      The key to the standards was the available data over the air interface
        2Mbps in fixed or in-building environments
        384 kbps in pedestrian or urban environments
        144 kbps in wide area mobile environments
        Variable data rates in large geographic area systems (satellite)

## Slide 7: 3G UMTS
Other parts of the standard
  Frequency Spectrum
  Technical Specification
  Radio and Network components
  Tariffs and Billing
  Technical Assistance
3 Main technical implementations were agreed
  UMTS - Europe
  CDMA2000 - America
  TD-SCDMA –China

## Slide 8: 3G UMTS
Universal Mobile Telecommunication system (UMTS)
  UMTS
    Builds upon the successful European GSM network
      Incorporates the developments made for the GPRS and EDGE networks
    Five areas of standardisation
      Radio
      Core Network
      Terminals
      Services

## Slide 9: 3G UMTS
The core network
  Asynchronous Transfer Method (ATM)
    Has been defined as the core networking technology
      ATM allows circuit switched transfer of data using packets.
      High speed data transfer – currently maximum 10 Gbps
      Guarantee of quality of service for the duration of packet transfer
      Small packets used called cells for the transfer of data to minimise the impact on the routers, network and switches.
  IPv6
    Arguments are being pushed for the core network to allow IPv6
    RFC3314, September 2002
      This would allow packets to be transferred directly from the internet to the device with no translation
      IPv6 does contain QOS headers, which can be used with the correctly configured hardware
      All 3G devices could have a single IP address that would not need to change

## Slide 10: 3G UMTS
UMTS
  Full packet driven architecture
    For voice and for data transmissions.
    Packet based networks allow for an increased amount of traffic on a medium.
    The only time part of that medium is blocked is when a device is transmitting or receiving.
      Consider how often in your phone calls you actually say nothing
        Natural pause between words
        Taking a breath
        Waiting for a response
        Thinking of something to say

## Slide 11: 3G UMTS
UMTS
  Offers voice and data services the same as EDGE
    Services offered will be classed into one of the following
    From these classes certain defined Quality of Service (QOS) specifications are guaranteed like packet delay time
Conversational | Streaming | Interactive | Background
Real-Time |  | Best-effort, guarantee of quality delivery | 
Voice | Streaming Video | Web Pages | MMS, SMS, emails

## Slide 12: 3G UMTS
Intended Data Rates
  Actual data rates will be effected by
    Interference (other devices, background, buildings)
    Over use of the frequency
    Amount of other traffic
    Base station / cell actually attached to
    Speed you are moving at !

## Slide 13: 3G UMTS
Types of Cells and Base station to use them
  Macro Cell
    These cover a large area and will give slow access
    144 Kbps – max speed of 500 Km/h
  Micro Cell
    These should cover a medium area
    384 Kbps max speed 120 Km/h
  Pico Cell
    Less than 100 metres
    2 Mbps – max speed of 10 Km/h
Difficult to predict
  Actual distances and bandwidth depend on local conditions

## Slide 14: 3G UMTS
Types of Cells and Base station to use them
  Cells will operate in a hierarchy overlaying each other
Satellite
Macro-Cell
Micro-Cell
Urban
In-Building
Pico-Cell
Global
Suburban

## Slide 15: 3G UMTS
Consider
  These data rates are in Mega Bits per Second and Kilo Bits
    In terms of data rate the measure of a kilo bit is 1000 bits
      Not the 1024 which is used for data storage
  So
    2 Mega Bits per Second = 244 Kilo Bytes per second (roughly)

## Slide 16: 3G UMTS
Types of Cells and Base station to use them
  Cells will operate in a hierarchy overlaying each other
    Pico Cells will operate in a Time division Duplex (TDD) mode
      TDD mode will use the same frequency to send and receive with a time frame being allocated.
    All other cells will operate in Frequency Division Duplex (FDD) Mode
      FDD will operate in the same manner as GSM, with a different frequencies for the Uplink and Downlink

## Slide 17: 3G UMTS
What transmitters/base stations look like
  Pictures taken from (www.undetectables.co.uk, 2004)

## Slide 18: 3G UMTS
Radio Interface
  Allocated Frequencies

## Slide 19: 3G UMTS
UK 3G Winners ??

## Slide 20: 3G UMTS
Radio Interface
  UMTS uses Wideband-Code Division Multiple Access (W-CDMA)
    Also known as “IMT-2000 Direct Spread”
    Extremely complex algorithms
    Uses 10x the current 2G processing power!
    Modulation is done with Quadrature phase shift keying (QPSK)
      This encodes 2 bits with each change
    Supports two modes of operation
      Frequency Division Duplex (FDD)
      Time Division Duplex (TDD)

## Slide 21: 3G UMTS
W-CDMA
  Operates in the same manner as the CDMA used in the US
    CDMA allows multiple users to communicate at the same time over the same frequency
      Each of the devices is given a “Chipping code” this is known by the device and the base station.
      This chipping code is then used to identify the signal and allows the BS to receive the signal
      The chipping code is used to adjust the frequency of data transferred during the transfer
      The essential point of CDMA is the use of power control

## Slide 22: 3G UMTS
W-CDMA
  Wideband CDMA operates the same but this takes place over a wider area of frequency
    UMTS uses 5MHz for the signal
    CDMA (narrowband) uses 200 KHz
    These communications are secure by the nature that unless the chipping code is known, the sequence of the data can not be known
    Communications can take place as soon as the device is ready and frequency reuse factor is now one

## Slide 23: 3G UMTS
W-CDMA
  Frequency Reuse Factor
    This is the distance which needs to be left between cells
    As the same frequency is reused and the chipping code which is used is change and unique to a BS
    The frequency can be reused in adjoining cells
    Temporary Base stations can be added to the infrastructure if required, as long as the chipping code was unique

## Slide 24: 3G UMTS
Power Control
  If you consider a group of people speaking, Chinese, English and Italian
    If these all speak at the same volume you can then listen for the parts which you understand.
      If the English person starts talking louder than the rest, the all you will hear is Italian
      The other languages will be drowned out
    CDMA Works on the same basis
      One point of CDMA is the power control, so that the power sent out is just enough to allow data transfer to take place.
        As a side effect of this technology this controlling of the power that the radio interface uses, also saves the battery on the device

## Slide 25: 3G UMTS
W-CDMA
  Infrastructure

## Slide 26: 3G UMTS
W-CDMA – UTRAN
  The core network for 3G will remain the same as GSM
    This is a purely cost issue, in the future the infrastructure will be upgraded
GSM | UMTS
Mobile device/station (MS) | User Equipment (UE)
Base Station (BS) | Node-B
Base Station Controller (BSC) | Radio Network Controller (RNC)

## Slide 27: 3G UMTS
W-CDMA
  UMTS Terrestrial Radio Access Network (UTRAN)
    A device which wishes to communicate need’s to request access to the network
      This is to prevent too many devices communicating at once
      Although CDMA will theoretically allow a very large number of user to communicate at once
        What actually happens is the quality of the calls is reduced considerably
        This is a issue for voice but is a disaster for data calls

## Slide 28: 3G UMTS
W-CDMA
  Handover
    UMTS will use a soft handover technique
      GSM used a hard handover technique
      In a handover the device is always attached to at least one BS
Node-B
Node-B
Node-B
Node-B
Node-B
Node-B

## Slide 29: – 3G UMTS
Virtual Home
  As a part of the ITU standard the Virtual Home Environment (VHE) will be supported.
  In 2G a VLR was used to allow the transfer of personal information
  A VHE will take this one stage further
    This will provide a common look and feel interface
    This is independent of the location, connecting network and device
    It is envisaged that this will be used on both circuit switched and packet switched networks
    How this will be achieved is undecided at the moment

## Slide 30: – 3G UMTS
3G UMTS is working in one part of the UK
  Isle of man has the equipment to use 3G
    This equipment is run and operated by O2
    The license spectrum used on this island was given free by the government
    The actual devices used were given to some of the islanders
      The idea was to trial the equipment in a limited manner
      Also they wanted to see if there was a pattern of usage for the technology i.e. the killer app
      As it is known now they have not found the single killer app, like SMS was for GSM
  Japan
    When we consider Japan for the killer app it was email!
      3G bandwidth is not needed for email!

## Slide 31: UMTS
Links
  Details of the 3G license auction (UK)
    www.umts-forum.org/servlet/dycon/ztumts/umts/Live/en/umts/Resources_Licensing_UK
  UMTS standards documents
    www.3gpp2.org/Public_html/specs/index.cfm