## Slide 1: GPRS: A new Dimension to Wireless Communication

## Slide 2: GPRS…..
GPRS is a new set of GSM-bearer services that provide packet mode transmission within the GSM network & interconnects with external packet data networks.

## Slide 3: Contents
Need for GPRS & other proposals
A commercial perspective
Architecture
Protocols
Inter-Connect Scenarios
QoS
Some results

## Slide 4: What is GPRS – A Commercial Perspective
2.5 G
GPRS is an overlay network over the GSM
Very Little change to GSM infrastructure
Provides Data Packet delivery service
Standardized by ETSI
Direct support for Data Network
Better Billing Mechanisms
No need to reorganize spectrum

## Slide 5: Applications….
Web browsing
Email
Banking Transactions
Stock Market Updates
News
Weather & Traffic reports

## Slide 6: Salient Features – A technical Perspective
High Data Rates of about 100 kpbs – an order of magnitude higher than GSM
The setup time is negligible – less than a second
Resource utilization as per requirements – air interface is assigned temporarily on per-packet basis
Hosts can remain “always on”

## Slide 7: GSM Architecture

## Slide 8: GPRS Additions

## Slide 9: The newcomers….
SGSN – Serving GPRS support Node.
  Performs packet routing & transfer
  Mobility management – attach/detach & location management
  Logical Link Management
  AAA
  Stores user Profiles of all MS within its purview

## Slide 10: The Newcomers continued…
GGSN – Gateway GPRS support Node
  Interface between GPRS backbone & External packet data networks
  Converts GPRS packets into appropriate Packet Data Protocol & vice-versa
  It may also perform AAA
Many-2-Many relationship may exist between SGSN & GGSN

## Slide 11: Interfaces…
Gb – Connects BSC with SGSN
Gn – SGSN – SGSN/GGSN (in the same network)
Gp – SGSN – SGSN/GGSN (in different networks)
Gf – For equipment querying at registering time
Gi – Connects PLMN with external Packet Data Networks (PDNs)
Gr – To exchange User profile between HLR & SGSN
Gs – To exchange Database between SGSN & MSC
Gd – Interface between SMS & GPRS

## Slide 12: About the Backbones…
GSNs connected through IP based backbone
Data Packets are encapsulated & tunneled using GPRS Tunneling Protocol (GTP)
GTP may used TCP or IP based on application requirement
Entire GPRS network phase consist of one IP hop
Two Backbones:
  Intra PLMN connect within the same network & are private IP networks
  Inter PLMN connects across different networks. Roaming agreement is necessary
PLMN – Inter PLMN interconnect are called Border Gateways

## Slide 13: GPRS Logical Architecture – put together
BSC
GMSC MSC/VLR
SGSN
PTM-SC
EIR
HLR
AUC
GGSN
IP-Backbone
Network
External
IP Network
External
X.25 Network
Gs
Gf
Gr
Traffic & Signaling
Signaling
BTS - Base Transceiver Station
BSC - Base Station Controller
MSC - Mobile Switching Centre
HLR - Home Location Register
SGSN - Serving GPRS Support Node
GGSN - Gateway GPRS Support Node
PTM-SC - Point-to-Multipoint Service Centre
Notebook & GPRS mobile
BTS
Gb
External
IP Network
Um
ISDN/ PSTN
Gn
Gi

## Slide 14: GPRS Channels
PRACH – Packet Random Access Channel, uplink, used to initiate uplink transfer
PPCH – Packet Paging Channel, downlink, BSC uses this to page the MS before downlink transmission
PAGCH – Packet Access Grant Channel, downlink, resource assignments are sent on this channel
PDTCH – Packet Data Traffic Channel, up & downlink, used to send data packets
PACCH – Packet Associated Control Channel, up & downlink, used to convey signalling along with PDTCH

## Slide 15: Typical Scenario
BTS
BSC
MSC
SGSN
GGSN
GPRS Register
Router
User
LAN
PSPDN

## Slide 16: GPRS Terminals
Class A
  Simultaneous (attach & traffic) support for GPRS & GSM.
Class B
  Simultaneous (attach but not traffic) support for GPRS & GSM.
Class C
  No Simultaneous abilities.

## Slide 17: Some results….
GPRS is well suited for TCP/IP as bearer service
Highly acceptable web browsing experience
Allows a large no. of parallel connections
Operator can easily scale up a GPRS system by increasing PDCHs
More practical than WAP
May be an ideal bearer for WAP

## Slide 18: Limitations…..
New Terminals required
Actual Speeds may vary – may come down to about 38.4 kbps
Could have an impact on cell capacity
20-30% (48+ bytes) protocol overhead in the headers – unacceptable for application sending small packets

## Slide 19: Conclusions
GPRS is a part in the transition from 2G to 3G
Because of its salient features & implementations over different cellular bearers, over 100 million subscribers of 2G TDMA based technologies will benefit
With little cost & major benefits, GPRS provides easy solution to ISPs
Will pave the way for UMTS & EDGE

## Slide 20
Questions??