## Slide 1: 3rd Generation WCDMA / UMTS Wireless Network
Notes: What do WCDMA / UMTS means?
Wideband CDMA, Universal Mobile Telecommunications System, Standards

## Slide 2: Outline
Evolution from 2G to 3G
WCDMA / UMTS Architecture
  Air Interface (WCDMA)
  Radio Access Network (UTRAN)
  Core Network
Radio Resources Management
  Admission Control, Load Control, Packet Scheduler
  Handover Control and Power Control
Additional Briefs
  Radio Network Planning Issues
  High Speed Data Packet Access
  WCDMA vs Ccdma2000
Notes: A very compact review of the very detailed standards

## Slide 3: Outline
What will not be covered
  Antenna, RF Propagation and Fading
  Added Services, e.g. Location Services
  Certain Technical Aspects, e.g. WCDMA TDD Mode, Base Station Synchronization
  Detailed Protocol Structures
  Detailed Design Issues, Optimizations
  Performance Evaluation
  cdma2000

## Slide 4: Evolution : From 2G to 3G
Source : Northstream, Operator Options for 3G Evolution, Feb 2003.
Notes: Roadmap of the Evolution of Wireless Network
2G Technologies -> 2.5G -> 3G
Provides Intermediate Steps of Transitions
Upper: GSM (EDGE: Enhanced Data for GSM Evolution)
Lower: CDMA
Focus on the Upper Stream -> Introduce WHY WCDMA would be today’s focus

## Slide 5: Evolution : From 2G to 3G
Fully specified and world-widely valid, Major interfaces should be standardized and open.
Supports multimedia and all of its components.
Wideband radio access.
Services must be independent from radio access technology and is not limited by the network infrastructure.
Primary Requirements of a 3G Network
Notes: How can we position / define a 3G Network?

## Slide 6: Standardization of WCDMA / UMTS
The 3rd Generation Partnership Project (3GPP)
Role: Create 3G Specifications and Reports
3G is standardized based on the evolved GSM core networks and the supporting Radio Access Technology
Source : Overview of UMTS, Guoyou He, Telecommunication Software and Multimedia Laboratory, Helsinki University of Technology
GSM
Notes: Let’s take a closer look of how 3G Network is evolved and standardized.
Illustrate by connection path.
MS -> Access Network -> Core Network -> External Network
Only CS Domain
NMS: Network Management System
BSS: Base Station System
NSS: Network Support System

## Slide 7: Standardization of WCDMA / UMTS
Introduction of GPRS / E-GPRS
3GPP Release ‘99
Source : Overview of UMTS, Guoyou He, Telecommunication Software and Multimedia Laboratory, Helsinki University of Technology
Notes: Later, in so call 2.5G, E-GPRS is introduced, BSS -> Enhanced RAN
-> First PS Domain
-> Support new external networks connections
In 3GPP Release 99,
New name: UMTS
E-RAN evolved into UTRAN (UMTS Terrestrial Radio Access Network)
Upgrade of BTS, BSC to BS and RNC

## Slide 8: Standardization of WCDMA / UMTS
3GPP Release 4
3GPP Release 5-6 All IP Vision
Source : Overview of UMTS, Guoyou He, Telecommunication Software and Multimedia Laboratory, Helsinki University of Technology
Notes: After R99, there’s R4 and R5/6 (most updated)
Goes all the way to an ALL-IP Network
R4: Minor changes to the CS Domain
-> Separate control and data switching
-> More Scalable
(MSC: Mobile Switching Center, MGW: Media Gateway)
R5/6: Only PS Domain
-> Circuit Routing: Virtual Circuit Switching

## Slide 9: Standardization of WCDMA / UMTS
Multiple Access Method | DS-CDMA
Duplexing Method | FDD/TDD
Base Station Synchronization | Asychronous Operation
Channel Separation | 5MHz
Chip Rate | 3.84 Mcps
Frame Length | 10 ms
Service Multiplexing | Multiple Services with different QoS Requirements Multiplexed on one Connection
Multirate Concept | Variable Spreading Factor and Multicode
Detection | Coherent, using Pilot Symbols or Common Pilot
Multiuser Detection, Smart Antennas | Supported by Standard, Optional in Implementation
WCDMA Air Interface, Main Parameters
Notes: 3G Requires a new Radio/Air Interface
3GPP’s UMTS adopted WCDMA
-> Illustrates briefly

## Slide 10: Outline
Evolution from 2G to 3G
WCDMA / UMTS Architecture
  Air Interface (WCDMA)
  Radio Access Network (UTRAN)
  Core Network
Radio Resources Management
  Admission Control, Load Control, Packet Scheduler
  Handover Control and Power Control
Additional Briefs
  Radio Network Planning Issues
  High Speed Data Packet Access
  WCDMA vs Ccdma2000

## Slide 11: UMTS System Architecture
USIM
ME
Node B
Node B
RNC
Node B
Node B
RNC
MSC/ VLR
GMSC
SGSN
GGSN
HLR
UTRAN
CN
UE
External Networks
Cu
Uu
Iu
Iub
Iur
Notes: -> Brief network by network, and their Functions
-> Introduce the Concepts of Interfaces
-> CN : CS / PS Domain
-> Illustrates sample data paths (CS and PS)
USIM: Universal Subscriber Identity Module
VLR: Visitor Location Register
HLR: Home Location Register

## Slide 12: UMTS Bearer Services
TE
MT
UTRAN
CN Iu EDGE NODE
CN Gateway
TE
End-to-End Service
External Bearer Service
Radio Access Bearer Service
Backbone Network Service
UTRA FDD/TDD Service
TE/MT Local Bearer Sevice
UMTS Bearer Service
CN Bearer Service
Radio Bearer Service
Iu Bearer Service
Physical Bearer Service
UMTS
Notes: Services Point of View
Connections is supported by different layers of bearer services.
-> All defined by the standard
Elaborates some of the services

## Slide 13: UMTS QoS Classes
Traffic class | Conversational class | Streaming class | Interactive class | Background
Fundamental characteristics | Preserve time relation between information entities of the stream Conversational pattern (stringent and low delay) | Preserve time relation between information entities of the stream | Request response pattern Preserve data integrity | Destination is not expecting the data within a certain time Preserve data integrity
Example of the application | Voice, videotelephony, video games | Streaming multimedia | Web browsing, network games | Background download of emails
Notes: Elaborates briefly

## Slide 14: UMTS In Detail
USIM
ME
Node B
Node B
RNC
Node B
Node B
RNC
MSC/ VLR
GMSC
SGSN
GGSN
HLR
UTRAN
CN
UE
External Networks
Cu
Uu
Iu
Iub
Iur
Notes: Short conclusion : Architecture, Services, QoS
Now, Drill into the detail of the UMTS
3 Item: Air Interface, UTRAN, CN

## Slide 15: WCDMA Air Interface
Wideband CDMA, Overview
DS-CDMA, 5 MHz Carrier Spacing,
CDMA Gives Frequency Reuse Factor = 1
5 MHz Bandwidth allows Multipath Diversity using Rake Receiver
Variable Spreading Factor (VSF) to offer Bandwidth on Demand (BoD) up to 2MHz
Fast (1.5kHz) Power Control for Optimal Interference Reduction
Services multiplexing with different QoS
  Real-time / Best-effort
  10% Frame Error Rate to 10-6 Bit Error Rate
UE
UTRAN
CN
Notes: What is an Air Interface?
What’s the Function?
Following Slides
-> Principle and Advantage of the wideband technology
-> Different physical channels and how they operates

## Slide 16: WCDMA Air Interface
UE
UTRAN
CN
Direct Sequence Spread Spectrum
User 1
User N
Spreading
Spreading
Received
Despreading
Narrowband
Code Gain
Frequency Reuse Factor = 1
Wideband
Wideband
5 MHz Wideband Signal allows Multipath Diversity with Rake Receiver
Wideband
Narrowband
f
f
f
f
f
f
t
t
Multipath Delay Profile
Variable Spreading Factor (VSF)
User 1
Spreading : 256
Wideband
f
f
User 2
Spreading : 16
Wideband
f
f
VSF Allows Bandwidth on Demand. Lower Spreading Factor requires Higher SNR, causing Higher Interference in exchange.
Notes: Introduce Spread Spectrum -> In order to illustrates Multipath and VSF

## Slide 17: WCDMA Air Interface
UE
UTRAN
CN
Mapping of Transport Channels and Physical Channels
Broadcast Channel (BCH)
Forward Access Channel (FACH)
Paging Channel (PCH)
Random Access Channel (RACH)
Dedicated Channel (DCH)
Downlink Shared Channel (DSCH)
Common Packet Channel (CPCH)
Primary Common Control Physical Channel (PCCPCH)
Secondary Common Control Physical Channel (SCCPCH)
Physical Random Access Channel (PRACH)
Dedicated Physical Data Channel (DPDCH)
Dedicated Physical Control Channel (DPCCH)
Physical Downlink Shared Channel (PDSCH)
Physical Common Packet Channel (PCPCH)
Synchronization Channel (SCH)
Common Pilot Channel (CPICH)
Acquisition Indication Channel (AICH)
Paging Indication Channel (PICH)
CPCH Status Indication Channel (CSICH)
Collision Detection/Channel Assignment Indicator Channel (CD/CA-ICH)
Highly Differentiated Types of Channels enable best combination of Interference Reduction, QoS and Energy Efficiency,
Notes: Standard…
Following slides:
FACH, RACH, DCH, CPCH, DSCH
Aim -> Illustrates “Random Access, Schedule Access, Dedicated Access”

## Slide 18: WCDMA Air Interface
UE
UTRAN
CN
Common Channels - RACH (uplink) and FACH (downlink)
Random Access, No Scheduling
Low Setup Time
No Feedback Channel, No Fast Power Control, Use Fixed Transmission Power
Poor Link-level Performance and Higher Interference
Suitable for Short, Discontinuous Packet Data
Common Channel - CPCH (uplink)
Extension for RACH
Reservation across Multiple Frames
Can Utilize Fast Power Control, Higher Bit Rate
Suitable for Short to Medium Sized Packet Data
RACH
FACH
1
2
1
3
3
P 3
1
P 1
CPCH
1
P 1
2
P 2

## Slide 19: WCDMA Air Interface
UE
UTRAN
CN
Dedicated Channel - DCH (uplink & downlink)
Dedicated, Requires Long Channel Setup Procedure
Utilizes Fast Power Control
Better Link Performance and Smaller Interference
Suitable for Large and Continuous Blocks of Data, up to 2Mbps
Variable Bitrate in a Frame-by-Frame Basis
Shared Channel - DSCH (downlink)
Time Division Multiplexed, Fast Allocation
Utilizes Fast Power Control
Better Link Performance and Smaller Interference
Suitable for Large and Bursty Data, up to 2Mbps
Variable Bitrate in a Frame-by-Frame Basis
DCH (User 1)
DCH (User 2)
DSCH
1
2
3
1
2
3
1
2
3
1
2

## Slide 20: WCDMA Air Interface
UE
UTRAN
CN
Summary
5 MHz Bandwidth -> High Capacity, Multipath Diversity
Variable Spreading Factor -> Bandwidth on Demand
RACH
CPCH
DCH (User 1)
DCH (User 2)
DSCH
FACH
1
2
1
3
3
P 3
1
P 1
1
P 1
2
P 2
1
2
3
1
2
3
1
2
3
1
2

## Slide 21: UTRAN
UE
UTRAN
CN
USIM
ME
Node B
Node B
RNC
Node B
Node B
RNC
MSC/ VLR
GMSC
SGSN
GGSN
HLR
UTRAN
CN
UE
External Networks
Cu
Uu
Iu
Iub
Iur

## Slide 22: UTRAN
UE
UTRAN
CN
Node B
Node B
RNC
Node B
Node B
RNC
Iub
Iur
UTRAN
RNS
RNS
Two Distinct Elements : Base Stations (Node B) Radio Network Controllers (RNC)
1 RNC and 1+ Node Bs are group together to form a Radio Network Sub-system (RNS)
Handles all Radio-Related Functionality
  Soft Handover
  Radio Resources Management Algorithms
Maximization of the commonalities of the PS and CS data handling
UMTS Terrestrial Radio Access Network, Overview

## Slide 23: UTRAN
UE
UTRAN
CN
Protocol Model for UTRAN Terrestrial Interfaces
Application
Protocol
Data
Stream(s)
ALCAP(s)
Transport
Network
Layer
Physical Layer
Signalling
Bearer(s)
Transport
User
Network
Plane
Control Plane
User Plane
Transport
User
Network
Plane
Transport Network
Control Plane
Radio
Network
Layer
Signalling
Bearer(s)
Data
Bearer(s)
Derivatives :
Iur1, Iur2, Iur3, Iur4
Iub
Iu CS
Iu PS
Iu BC
Functions of Node B (Base Station)
Air Interface L1 Processing (Channel Coding, Interleaving, Rate Adaptation, Spreading, etc.)
Basic RRM, e.g. Inner Loop Power Control
Notes: Protocol Model
Independent Horizontal Layer and Vertical Panes
Node B
Brief

## Slide 24: UTRAN
UE
UTRAN
CN
Node B
Node B
RNC
Logical Roles of the RNC
Controlling RNC (CRNC)
Responsible for the load and congestion control of its own cells
CRNC
Node B
Node B
SRNC
Serving RNC (SRNC)
Terminates : Iu link of user data, Radio Resource Control Signalling
Performs : L2 processing of data to/from the radio interface, RRM operations (Handover, Outer Loop Power Control)
Drift RNC (DRNC)
Performs : Macrodiversity Combining and splitting
Node B
Node B
DRNC
Node B
Node B
SRNC
Node B
Node B
DRNC
UE
UE
Iu
Iu
Iu
Iu
Iur
Iur

## Slide 25: Core Network
UE
UTRAN
CN
USIM
ME
Node B
Node B
RNC
Node B
Node B
RNC
MSC/ VLR
GMSC
SGSN
GGSN
HLR
UTRAN
CN
UE
External Networks
Cu
Uu
Iu
Iub
Iur
Notes: Last Part, Core Network

## Slide 26: Core Network
UE
UTRAN
CN
MSC/ VLR
GMSC
SGSN
GGSN
HLR
CN
External Networks
Iu
Core Network, Overview
Changes From Release ’99 to Release 5
A Seamless Transition from GSM to All-IP 3G Core Network
Responsible for Switching and Routing Calls and Data Connections within, and to the External Networks (e.g. PSTN, ISDN and Internet)
Divided into CS Network and PS Network
Notes: Following slides:
Take 2 example for illustration, R99 and R5

## Slide 27: Core Network
UE
UTRAN
CN
MSC/ VLR
GMSC
SGSN
GGSN
HLR
External Networks
Iu-cs
Core Network, Release ‘99
CS Domain :
  Mobile Switching Centre (MSC)
    Switching CS transactions
  Visitor Location Register (VLR)
    Holds a copy of the visiting user’s service profile, and the precise info of the UE’s location
  Gateway MSC (GMSC)
    The switch that connects to external networks
PS Domain :
  Serving GPRS Support Node (SGSN)
    Similar function as MSC/VLR
  Gateway GPRS Support Node (GGSN)
    Similar function as GMSC
Register :
  Home Location Register (HLR)
    Stores master copies of users service profiles
    Stores UE location on the level of MSC/VLR/SGSN
Iu-ps

## Slide 28: Core Network
UE
UTRAN
CN
MGW
MGW
SGSN
GGSN
External Networks
Iu-cs
Core Network, R5
1st Phase of the IP Multimedia Subsystem (IMS)
  Enable standardized approach for IP based service provision
  Media Resource Function (MRF)
  Call Session Control Function (CSCF)
  Media Gateway Control Function (MGCF)
CS Domain :
  MSC and GMSC
    Control Function, can control multiple MGW, hence scalable
  MSG
    Replaces MSC for the actual switching and routing
PS Domain :
  Very similar to R’99 with some enhancements
Iu-ps
MSC
GMSC
Iu-cs
MRF
CSCF
HSS
MGCF
Services & Applications
Services & Applications
IMS Function
Notes: Point out changes first
HSS: Home Subscriber Server
(Many Database Functions, e.g. HLR, DNS, Security, Network Access, etc)

## Slide 29: Summary
System Architecture, Bearer Services, QoS Classes
WCDMA Air Interface : Spread Spectrum, Transport Channels
UTRAN : Roles of RNCs and Node Bs
Core Network : Roles of Different Components of R’99 and R5
USIM
ME
Node B
Node B
RNC
Node B
Node B
RNC
MSC/ VLR
GMSC
SGSN
GGSN
HLR
UTRAN
CN
UE
External Networks
Cu
Uu
Iu
Iub
Iur

## Slide 30: Radio Resources Management
Evolution from 2G to 3G
WCDMA / UMTS Architecture
  Air Interface (WCDMA)
  Radio Access Network (UTRAN)
  Core Network
Radio Resources Management
  Admission Control, Load Control, Packet Scheduler
  Handover Control and Power Control
Additional Briefs
  Radio Network Planning Issues
  High Speed Data Packet Access
  WCDMA vs cdma2000

## Slide 31: Radio Resources Management
Network Based Functions
  Admission Control (AC)
    Handles all new incoming traffic. Check whether new connection can be admitted to the system and generates parameters for it.
  Load Control (LC)
    Manages situation when system load exceeds the threshold and some counter measures have to be taken to get system back to a feasible load.
  Packet Scheduler (PS)
    Handles all non real time traffic, (packet data users). It decides when a packet transmission is initiated and the bit rate to be used.
Connection Based Functions
  Handover Control (HC)
    Handles and makes the handover decisions.
    Controls the active set of Base Stations of MS.
  Power Control (PC)
    Maintains radio link quality.
    Minimize and control the power used in radio interface, thus maximizing the call capacity.
Source : Lecture Notes of S-72.238 Wideband CDMA systems, Communications Laboratory, Helsinki University of Technology
Notes: Brief, Brief, Brief…

## Slide 32: Network Based Functions
RT / NRT : Real-time / Non-Real-time RAB : Radio Access Bearer
Source : Lecture Notes of S-72.238 Wideband CDMA systems, Communications Laboratory, Helsinki University of Technology
Notes: Introduces different States
Introduces how AC, LC, PS reacts
Admission Control (AC)
Handles all new incoming traffic. Check whether new connection can be admitted to the system and generates parameters for it.
Load Control (LC)
Manages situation when system load exceeds the threshold and some counter measures have to be taken to get system back to a feasible load.
Packet Scheduler (PS)
Handles all non real time traffic, (packet data users). It decides when a packet transmission is initiated and the bit rate to be used.

## Slide 33: Connection Based Function
Power Control
Prevent Excessive Interference and Near-far Effect
Open-Loop Power Control
  Rough estimation of path loss from receiving signal
  Initial power setting, or when no feedback channel is exist
Fast Close-Loop Power Control
  Feedback loop with 1.5kHz cycle to adjust uplink / downlink power to its minimum
  Even faster than the speed of Rayleigh fading for moderate mobile speeds
Outer Loop Power Control
  Adjust the target SIR setpoint in base station according to the target BER
  Commanded by RNC
Fast Power Control
If SIR < SIRTARGET, send “power up” command to MS
Outer Loop Power Control
If quality < target, increases SIRTARGET
Notes: Connection based function…

## Slide 34: Connection Based Function
Handover
Softer Handover
  A MS is in the overlapping coverage of 2 sectors of a base station
  Concurrent communication via 2 air interface channels
  2 channels are maximally combined with rake receiver
Soft Handover
  A MS is in the overlapping coverage of 2 different base stations
  Concurrent communication via 2 air interface channels
  Downlink: Maximal combining with rake receiver
  Uplink: Routed to RNC for selection combining, according to a frame reliability indicator by the base station
A Kind of Macrodiversity

## Slide 35: Additional Briefs
Evolution from 2G to 3G
WCDMA / UMTS Architecture
  Air Interface (WCDMA)
  Radio Access Network (UTRAN)
  Core Network
Radio Resources Management
  Admission Control, Load Control, Packet Scheduler
  Handover Control and Power Control
Additional Briefs
  Radio Network Planning Issues
  High Speed Data Packet Access
  WCDMA vs cdma2000
Notes: Additional Briefs:
Make the presentation more complete
Drive of some further study areas

## Slide 36: Radio Network Planning Issues
Radio Link Power Budgets
  Interference margin (loading) + Fast fading margin (power control headroom) + Soft handover gain (macrodiversity)
  Cell Coverage is obtained
Load Factor
  Estimation of Supported Traffic per Base Station
  Required SNR, Intracell Interference, Intercell Interference
  Orthogonality of Channels
  One of the example:
Soft Capacity
  CDMA has no definite capacity limit
  Can always “borrow” capacity from other cell or decrease QoS
Other Issues
  Network Sharing
  Co-planning
  Inter-operator Interference

## Slide 37: HSDPA
High Speed Downlink Packet Access
Standardized in 3GPP Release 5
Improves System Capacity and User Data Rates in the Downlink Direction to 10Mbps in a 5MHz Channel
Adaptive Modulation and Coding (AMC)
  Replaces Fast Power Control : User farer from Base Station utilizes a coding and modulation that requires lower Bit Energy to Interference Ratio, leading to a lower throughput
  Replaces Variable Spreading Factor : Use of more robust coding and fast Hybrid Automatic Repeat Request (HARQ, retransmit occurs only between MS and BS)
HARQ provides Fast Retransmission with Soft Combining and Incremental Redundancy
  Soft Combining : Identical Retransmissions
  Incremental Redundancy : Retransmits Parity Bits only
Fast Scheduling Function
  which is Controlled in the Base Station rather than by the RNC

## Slide 38: WCDMA vs cdma2000
Some of the Major Differences | WCDMA | cmda2000 | Remarks
Spread Sprectrum Technique | 5Mhz Wideband DS-SS | Multicarrier, 3x1.25MHz Narrowband DS-SS, 250kHz Guard Band | Multicarrier does not requires a contiguous spectral band. Both scheme can achieve similar performance
Chip Rates | 3.84Mcps | 3.6864Mcps (1.2288 per carrier) | Chip Rate alone does not determine system capacity
Frame Lengths | 10ms | 20ms for data, 5ms for control | Response and efficiency tradeoff
Power Control Rate | 1.5kHz | 800Hz | Higher gives better link performance
Base Station Synchronization | Asynchronous | Synchronized | Asynchronous requires not timing reference which is usually hard to acquire. Synchronized operation usually gives better performance
Adopted by Telecommunications Industry Association, backward compatible with IS-95, lately moved to 3GPP2 (in contrast to 3GPP for WCDMA) as the CDMA MultiCarrier member of the IMT-2000 family of standard

## Slide 39: Wrap Up and Key References
What we have been talked about
  2G to 3G Evolution
  WCDMA Air Interface
  UTRAN
  Core Network
  Radio Resources Management
  Network Planning Issues
  High Speed Data Packet Access
  WCDMA vs cdma2000
Key References
  WCDMA for UMTS, Radio Access for Third Generation Mobile Communications, 2nd Ed., Edited by Harri Holma and Antti Toskala
  Overview of UMTS, Guoyou He, Telecommunication Software and Multimedia Laboratory, Helsinki University of Technology
  Course materials from Course S-72.238 : Wideband CDMA systems, Communications Laboratory, Helsinki University of Technology