## Slide 1: What is Wi-Max?

## Slide 2: What is Wi-Max?
WiMAX is a wireless digital communications system, (a.k.a.IEEE 802.16) intended for wireless metropolitan area networks.
WiMAX connects IEEE 802.11(Wi-Fi) hotspots to the Internet and provides a wireless extension to cable and DSL.
WiMAX can provide broadband wireless access (BWA) up to 30 miles (50 km) for fixed stations, and 3 - 10 miles (5 - 15 km) for mobile stations.
It allows users connectivity without a direct line of sight to a base station. This does not necessarily mean that users 50 km away without line of sight will have connectivity.

## Slide 3: What is Wi-Max?
The technology also provides shared data rates up to 70 Mbit/s, which, according to WiMAX proponents, is enough bandwidth to simultaneously support more than 60 businesses with T1-type connectivity and well over a thousand homes at 1Mbit/s DSL-level connectivity.
WiMAX does not conflict with Wi-Fi but complements it. Because IEEE 802.16 networks use the same Logical Link Controller (standardized by IEEE 802.2) as other LANs and WANs, it can be both bridged and routed to them.

## Slide 4: What is Wi-Max?
First wireless client can scan or be manually configured to match the channel of the wireless access point.
Access Point checks to see if client is authorized to access network.
The access point transmits information about the frequency it till hop to next and the length of time before the changes again.

## Slide 5: How Wireless Networks Work
If DHCP is enabled network settings are transmitted to the client.
Packets are randomly transmitted between client and access point.
At random time the frequency is changed to random frequency. This helps to prevent someone intercepting your packets.

## Slide 6
Photo courtesy of howstuffworks.com

## Slide 7: WiMax Standards
Frequency Range:
802.16: 10 – 66 GHz
802.16a: 2 – 11 GHz
The addition of the 802.16a was created for use of unlicensed frequencies.
The 5-6 GHz range is used for non line of sight (NLOS) transmissions.
802.16e has amendments made to incorporate the addition of mobile devices.
Photo courtesy Intel

## Slide 8: WiMax Unleashed

## Slide 9: WiMax Unleashed

## Slide 10: Future Possibilities
With 802.16e’s addition of mobile devices future cell phones and PDA’s will be able to have access to high speed internet.
Due to the mesh architecture capabilities of the wimax hardware the transmitters could be used to create a backup (or primary) communications network that cant be destroyed with a single attack.

## Slide 11: Technological Advantages over WiFi
Covers a broader spectrum of frequencies
(WiFi = 2.4 GHz – WiMax = 10-66 GHz plus added coverage in the 2-11 GHz range)
Coverage area is greater than that of WiFi
(Can cover a radius of up to 50 km)
Enhanced MAC (Media Access Control) over WiFi
(WiFi = competition over Access Point – WiMax = continuous access to Access Point)

## Slide 12: Technological Advantages over WiFi (cont’d)
WiMax incorporates more “duplexing” options
    WiFi only supports TDD (Time Division Duplexing) – send and receive functions occur on the same channel
    WiMax supports TDD as well as FDD (Frequency Division Duplexing) – send and receive functions occur on different frequencies, simultaneously)

## Slide 13: Implementation and Uses of WiMax
Connection Capability
Alternative internet connection
VoIP implementation

## Slide 14: Uses of WiMax continued…
Implementation with Legacy Cellular Networks
Used for faster Internet Connection
Multiplayer Gaming