## Slide 1
Evolution of Emissions Measurement Techniques Past Developments and Future Trends
By HORIBA Instruments, Inc. 29 Apr 1998

## Slide 2: Overview
Evolution of Test Procedures
  New rules required new tests and equipment
Development of Improved Test Equipment
  Better samplers
  Modern analyzers
  Electric dynamometers
Future Problems and Methods
  Fast Response, FTIR , Mass Spectrometer
  Exhaust Flow Measurement
  Mini-Diluter

## Slide 3: Original FTP
NDIR HC
NDIR CO
NDIR NO
Notes: The first emissions tests were done in the 1960’s
The state of California
Drive trace “California 7 mode 7 cycle”
Concentration based
Used NDIR analyzers for all 3 compnents, Horiba AIA-1

## Slide 4: ECE Big Bag
NDIR HC
NDIR CO
NDIR NO
Gas Meter
Raw Sample Bags
Notes: The ECE Big Bag Test measured actual mass of emissions
Big bag captured all of vehicles exhuast
Pneumatic integration of result
Volume determined at end of test by emptying bags through gas meter.
NDIR analyzers
Problems arose from water collection in the bags. The technique was not used very long, being replaced by CVS method..

## Slide 5: Route of the LA-4
Notes: The LA-4 was an actual commuter’s route in Los Angeles California.
It is said that the EPA put 5th wheels on 6 vehicles and had them driven over “typical” commuting routes in Los Angeles. They placed them on a wall for visual comparison. To them, the 4th one “looked most typical” so it became the LA-4 and the basis for all US testing to follow.
The EPA was administered by Mr. Ruckelshouse, who was a lawyer, not an engineer.

## Slide 6: US CVS Test
FID HC
NDIR CO
CLA NOx
MEXA 8000
CVS Sampler
Air
Volume
Sample Bags
Notes: The EPA’s CVS Introduced new equipment that made repeatable and accurate mass emissions possible. The mass calculation meant that the impact on the environment could be meaningfully assessed.
Variable dilution - constant volume sampler to manage water vapor and solve the water vapor problem.
Proprotional sampling into small sample bags
Total Hydrocarbon measurement by FID
NO and NO2 measurement with Chemiluminescent analyzer
Calibrated PDP pump for Volume Measurement
Empirical Driver Trace from actual commute
Horiba exteded its analyzer line to include FID and CLA. The OPE advanced the analyzer technology and the MEXA-8000 incorporated them together in a single analysis bench.
VETS computer system for test automation on HP 1000 and DEC PDP Mini-computers.
The Clean air act called for a 90% reduction from previous levels. To establish these levels, cars that had certified on the California Cycle were measured. They averaged 4.1 grams HC per mile. From this we got the .41 g/mi requirement and from the amendments to the Clean Air Act, the 0.4 ULEV requirment (anohter 90% reduction)

## Slide 7: US 1975 3-Phase Test
(.57 x
Cold Portion
)
Hot Portion
+
(.43 x
=
Weighted Result
)
Not Run
P1
P2
P3
Notes: The 1975 3-Phase test was created in respone to criticism that existing tests did not take into account that significant numbers of vehicle trips started with warmed up vehicles, not the overhight “cold soak” required by the test procedures. Cold vehicles polluted much more than warm ones and manufacturers were pessimistic about meeting standards.
EPA responded by defining “hot” part for the test, to be run 10 minures after the cold portion to simulate a shopping trip.
The warmed up parts of both cycles were deemed to be eqivalent, so the stabilized part of the hot portion is not measured. The values from the cold stabilized are used.
This explains the unusual calculation for weighted grams in the US EPA calculation procedures.
The complications of this 3 phase test procedure prompted the developmeint of mini-computer based automation systems like VETS.

## Slide 8: Highway Fuel Economy Test
Rotary Engine Controversy
Ohio Turnpike Drive Trace
Stats:
  10.5 Miles
  765 Seconds
  Max
    Speed 63 mph
    Accel ?
Notes: In the early 70’s, just after EPA added the CO2 measurement. Fuel economy could be calculated from the fuel/exhuast carbon balance, since all of the carbon in the exhaust was now measured.
Fuel economies calculated this way were quite different than those reported by the manufacturers , and different from what consumers were calculating themselves. The LA-4 calculated fuel economies were lower than expected.
This was a significant issue during the time of oil embargos and rising fuel costs.
Mazda had just introduced a rotary engine that did especially poorly on FTP fuel economy.
To address these concerns, the EPA took several vehicles, including a Mazda RX-7, out to the Ohil Turnpike and recorded their speeds on a typical highway drive pattern. A composite of these became the HWFET. Although the emissions from this cycle did not become a part of the regulation, the fuel economy calculated, a higher one, did.

## Slide 9: Diesel Testing
New Requirements
  Particulate Measurement- Tunnel
  Heavier HC’s - Heated FID
NDIR CO2
NDIR CO
CLA NOx
MEXA 9000
Heated FIDHC
Dilution Tunnel
Particulate Sampling
PDP Pump
Sample Bags
Notes: Also in the era of concern about fuel cost and availability, the diesel engine became interesting and was even introduced on a few short lived models of passenger vehicles.
Diesels present measurement challenges because the hydrocarbons emitted are heavier and condense out of the gas at ambient temperatures. Also troublesome are the significant particulate soot emissions.
The heated FID (Horiba FIA-21 and FIA 210) was applied wth a continuous integration instead of a bag.
A mixing chamber - dilution tunnel - was needed to insure that the particulate sample was accurate.

## Slide 10
Full Flow Dilution Tunnel
Notes: A full blown apparatus of this type is complicated.
- bag sampler
- heat exchanger
- calibrated PDP pump
- continuous HC integration
- particulate filter collectors
- gas meters volume accumulator
- dilutent sampler
- heated sample lines
Horiba supplied the DLT - and DPS systems

## Slide 11: Alternative Fuels
Notes: President Bush promoted interest in Alternative fuels Methanol and Ethanol
New measurement issues:
- capturing the water soluable methanol emission
- capturing the aldehydes that a FID could not measure
New equipment and methods:
- bublers and wet chemistry
- impingers and DNPH
- heated TP connectors and/or RMT’s

## Slide 12: Inspection and Maintenance IM240 Test
NDIR CO/CO2
FID HC CLA NOx
Real time Integrator (Computer)
CFV Flow Meter
Blower
Notes: With the clean-up of new cars more attention could be given to in use vehicles.
A poorly operating “gross emitter” could easily produce as much pollution as 20 new cars.
A method to reasonably find and fix these vehicles was sought.
IM240 pgm
- 4 minute composite drive cycle
- CVS like dilution method - single large flow rate
- single range - dual detector instruments
- no bag, computer integration in real time
- simple dynamometer
Horiba’s IM240 sampler and IM series instruments
IMVETS PC Windows based computer systems

## Slide 13: SFTP Aggressive Drive Cycle US06
Supplement to FTP
  Capture the greater emissions from agressive driving
High speeds
  80 mph
Strong accelerations
  Challenge for Dynomometers
  Difficult for small cars
Notes: Automotive engineers proved very skillful at designing emission control strategies and systems that minimized pollution with the type of driving represented by the LA-4 driving cycle.
However, when the driver demanded maximum power from the vehicle, these strategies sometimes took second priority to performance.
To remedy this and recognize that the LA-4 did not represent the aggressive driving that is possible in modern vehicles, in 1994, the EPA promulgated the SFTP, Supplemental Federal Test Procedure, which included, among other things, the US06 aggressive driving cycle.

## Slide 14: Equipment Development
Analyzer Benches
  Computer Controllers
  Modular Design (Mexa 7000)
Dynamometers
  From dual 8.65” rollers to single 48” roll
CVS
  CFV Type
  SAO Type
Computer Automation
  VETS 9000
  VETS 7000
  VETS 7000NT
Diesel Sampling
  Mini/Micro Dilution Tunnels
Notes: In addition to the evolution of federal test procedures, there has also been an evolutonary improvement in the equipment supplied to perfrom these tests.
Analyzer benches have become sophisticated and now include micro computer and PC based system controllers. Today, the modular design of the MEXA 7000 represents state of the art.
Dynamometers used to have small twin rollers, flywheels for inertia simulation and hydrokinetic brakes. Now they have a large roll, simulation of inertia, and sophisticated AC motors.
The CVS systems use stable CFVs instead of PDP pumps and heat exchangers.
Of course, a stead change has taken place in computer technology from the proprietary CPU’s and operating systems of past mini computers to the WINTEL NT systems that have become a commodity today.
For large engne particulate there are the convenient mini and micro tunnels.

## Slide 15
Overview of the MEXA 7000
PC based controller using UNIX Windows like software
Low sample flow requirement (approx. 10- 15 liters/min)
Small size/foot print (1150/1970mm and 1-bay)
Lower operating costs - 30 %
Modularity
Separate heated analyzers that allow short htd. lines
True digital analyzers wit h 24 bit A/D converters, using LAN to connect to MCU
Wide dynamic ranges (single range available)
Notes: The state of the art in analyzers and analyzer benches is the MEXA-7000.

## Slide 16: MEXA 7000 Control Concept
Notes: Here are the flow and electrical interconnection concepts of the MEXA
The modular functional units make possible a multitude of flow configurations.
On the electrical side the IFC acts as a data concentration device. It supports LAN, Parallel, Multidrop RS485 serial and RS232 so that each module gets the appropriate kind of automation and data collection support.
A real-time UNIX (LYNX) X-window touch screen interface for the PC based Main Control Unit that puts the intelligence for the bench in one maintainable software platform.

## Slide 17: Dynamometers
Improvements
  Large Roller
    More realistic road simulation
  Electric Inertia Simulation
    More precision
Notes: The industry has also changed from the small twin roller hydrokinetic dynamomter to the 48” single roll AC electic dynamometer.
The old twin rollers were from standard well casing, hence the unusual 8.65” diameter.
There were concerns and studies about the ability of the twin roll and the un-road -like tire deformation it caused to properly simulate the tire-road interface. In addition, the precision of the water brake power absorber was inadequate, especially compared with the increasing precision of the gas anaalyzers and sampler flow measurements.
A drive cycle like the new US06 would not be feasible on the old dynos.

## Slide 18: Horiba Large Roll Dyno

## Slide 19: Dynamometer
Notes: Horiba’s new low cost 48” singe roll dyno is shown here mounted in its smaller sized pit.
Atop the dyno is shown the calibration arm. This allows calibration of the load cell from above, without the need to get into the pit.