## Slide 1: Modelamiento No Lineal

## Slide 2: Respuestas del Macizo Rocoso
Elastico vs No lineal
Rigidéz del Sistema (LSS)
Velocidad de lineración de energía (ERR)
Aplicado al diseño de soporte
Aplicado al diseño de pilares
Aplicado a la estabilidad de la falla
Notes: To do this we will need to delve into some more complex issues regarding non-linear modelling and loading system stiffness considerations.

## Slide 3
Equivalence of overstressing and damage
1
3 -
1
1
Aumenta el sobre esfuerzo
Aumenta el daño
Notes: Since in elastic modelling we require the rockmass to respond elastically, we interpret the results by assuming that there is a correspondence between the amount of overstressing and damage. This is fundamental to this interpretation procedure. Without such a correspondence we have no basis to make predictions regarding expected levels of damage.
We now need to reconsider this assumption.

## Slide 4
Equivalence of overstressing and damage
1
3 - Confinement
1
1
Increased Overstressing
Increased Damage
Soft loading system
Stiff loading system
Notes: It is entirely possible that given the same amount of overstressing that we could get completely different amounts of damage. This will depend on the loading system stiffness. A stiff loading system will tend to provide smaller amounts of damage than a soft loading system.

## Slide 5
Elástico vs No lineal
Si existe un sobre esfuerzo actuando sobre un elemento este se deformará de manera no lineal. Esta deformación disipa el sobre esfuerzo. El exceso de esfuerzo se transfiere a las zonas aledañas. Y estas transfieren devuelta una vez deformadas
Notes: If the loading system overstresses the rock, and the rock can not sustain the load, it yields to the load and deforms non-linearly. It is the yielding of the rock that dissipates the stress. The stresses get transferred to adjacent pillars and abutments.
The end result can be viewed as partially excavating the pillar, i.e. somewhere between the elastic result and the case where rock is completely excavated.

## Slide 6: Interpretación de Modelos No Lineales
Notes: Let’s have a look at a non-linear modelling example. In this case a pillar has been overstressed and has yielded.

## Slide 7: Modelos No Lineales
En este caso no se muestran sobre esfuerzos
Notes: First let’s examine 1. Note that unlike an elastic analysis, the results show a complete lack of stress concentration in the pillar. In fact the stresses are lower in the pillar than just about everywhere else.

## Slide 8: Non-linear model interpretation
El sobre esfuerzo de corte es caso 0 en todas partes, En este caso no puede utilizarse como un indicador de daño
Notes: If we now consider the excess stress we see that is zero or less everywhere, and just about exactly zero throughout the pillar. Unlike elastic model interpretation, consideration of excess stress is not very useful.
Note that excess stress (or strength factor) can still be used to determine where the stresses are below but approaching the rock strength. This might indicate where we expect the failure to migrate to, but does not indicate where we expect increased damage with future mining.

## Slide 9: Non-linear model interpretation
Deformaciones plásticas están de acuerdo con el potencial daño a observar
Notes: Finally looking at the non-linear strain we see that the pillar has yielded. The magnitude of the strain indicates the level of damage we expect.

## Slide 10
Elástico vs Plástico
1
3 -
1
1
Increased Overstressing
Deformaciones No lineales

## Slide 11: Deformaciones Elásticas
De las ecuaciones de equilibrio
σxx = σxxf + [ (1-ν) εxxelastic + ν ( εyyelastic + εzzelastic ) ] E / [ (1+ν) (1-2ν) ]
  σyy = σyyf + [ (1-ν) εyyelastic + ν ( εzzelastic + εxxelastic ) ] E / [ (1+ν) (1-2ν) ]
  σzz = σzzf + [ (1-ν) εzzelastic + ν ( εxxelastic + εyyelastic ) ] E / [ (1+ν) (1-2ν) ]
  τxy = τxyf + εxyelastic E / (1+ν)
  τyz = τyzf + εyzelastic E / (1+ν)
  τxz = τxzf + εxzelastic E / (1+ν)
E y v son modulos de young y poisson respectivamente

## Slide 12: Deformaciones Plásticas

## Slide 13: Modelo de Deformación Plástica
linear (Bingham) creep model
En cada paso se evalúa si el elemento posee esfuerzos superiores a la resistencia si ocurre se calcula una deformación plástica linealmente dependiendo del módulo de viscosidad G
Para análisis no lineal se requiere la discretisación del tiempo o paso y el módulo de viscosidad.
σ = Strength + C Δεplastic /Δt
C = G Δt

## Slide 14: Modelo Constitutivo Sobre Esfuerzo Deformación Plástica
Una vez deformado un Δε de acuerdo al modelo de creep se recalcula el sobre esfuerzo de acuerdo a un modelo constitutivo y se transfiere éste a los elementos aledaños
σ1 - σ1° - C Δε1plastic /Δt = UCS + q ( σ3 - σ3° - C Δε3plastic /Δt )
Modelo Constitutivo Hoek and Brown
σ3 - σ3° - C Δε3plastic /Δt = To
En caso de tener un sobre esfuerzo de tracción
Se produce deformación hasta alcanzar los valores de resistencia residual, luego las deformaciones se estabilizan. Valores de resistencia residual

## Slide 15: Equilibrio
La suma de las deformaciones parciales Δε producto de la sucesión de deformaciones plásticas define la deformación total ε
σ1° = [ (1-ν) ε1plastic + ν ( ε2plastic + ε3plastic ) ] E / [ (1+ν) (1-2ν) ]
σ2° = [ (1-ν) ε2plastic + ν ( ε3plastic + ε1plastic ) ] E / [ (1+ν) (1-2ν) ]
σ3° = [ (1-ν) ε3plastic + ν ( ε1plastic + ε2plastic ) ] E / [ (1+ν) (1-2ν) ]

## Slide 16: Parámetros Modelos No Lineales
Módulos de Viscosidad Gs es para FF blocks y Gn para DD elements (MPa)
Discretización de cada periodo de minería para generar STOL menor al índicado
Seleccionar el modo elasto plastic

## Slide 17: Creep
Con este parámetro los elementos se deforman y se realiza la transferencia de exceso de esfuerzo de corte a las zonas aledañas para cada paso
NLD regulará el número de pasos a discretizar cada mining step

## Slide 18: Ángulo de Fricción Crítico
s = (1 - 2) sin() cos()
n = 1 sin²() + 2 cos² ()
|s| = Cohesion + n tan()
|(1 - 2) sin() cos()|
= Cohesion + [1 sin²() + 2 cos²()] tan()

1
2
s
n
Notes: One of the problems in setting up any non-linear model is selection of realistic strength parameters. While this may seem obvious, it is often not as easy as one might think. By definition, active faults are either very close to or exactly at equilibrium with the far field stresses prior to mining.
As an example, consider a condition where 1 is twice 2. If  is 20º or above, then all orientations are stable. For  of 15º,  must be less than 18º or more than 57º. For  of 10º,  must be less than 11º or more than 69º.
Consider a condition where 1 is three times 2. If  is 30º or above, then all orientations are stable. For  of 20º,  must be less than 12º or more than 58º. For  of 15º,  must be less than 9º or more than 67º. For  of 10º,  must be less than 5º or more than 75º.
La razón entre esfuerzos define el ángulo de buzamiento critico para producir falla.
For a planar structure it is relatively straight forward to determine the friction angle necessary to resist slip for various orientations and stress ratios. For a non-planar fault in 3D this can be much more difficult.

## Slide 19: Sobre Esfuerzo de Corte para un Ángulo de 36 grados
Notes: Here I have plotted the excess in-plane shear stress for a 36º friction angle.
To do this select Plot > Failure Modes > ip in-plane excess stress. Don’t forget to set the friction angle using Plot > Failure Modes > ipmod in-plane parameters.
We can now clearly see where we expect slip to occur and the magnitude of damage we expect.

## Slide 20: ESS
Las diferencias en los sobre esfuerzos de corte implican deformaciones plásticas que consumen sobre esfuerzo

## Slide 21: Hung2-36
Simulación con Ángulo de fricción de 36 grados peak y residual. Se define el material 2.

## Slide 22
Modelamiento Lineal y No lineal
ESS
Deformación
La geometría de las zonas de deformación son diferentes con respecto a las mostradas en el modelamiento no lineal. Se debe considerar que el sistema rocoso se acondiciona al ESS
Notes: La geometría de las zonas de deformación son diferentes con respecto a las mostradas en el modelamiento no lineal. Se debe considerar que el sistema rocoso se acondiciona al ESS

## Slide 23: Tarea 2
Monitorear las deformaciones en la falla y en la roca de caja de modo de establecer criterios de estabilidad
Parámetros de resistencia de la estructura y roca de caja
Analizar los estados de tensiones en la estructura y en las zonas aledañas a la excavación.
Analizar diferentes modelos constitutivos y establecer rangos de deformaciones en función de los modelos constitutivos y los parámetros de resistencia.

## Slide 24: Parámetros