## Slide 1: Bridges
Notes: This module will cover bridges and how they are input into HEC-RAS.

## Slide 2: 2 Types of Flow @ Bridges
Low Flow - Flow where the water surface does not reach the low beam
High Flow - Flow where the water surface reaches the deck or higher
There are sub-types for both low and high flow
Often both types of flow occur in single simulation with different profiles
Notes: These are not that important to know - except you must specify analysis methods for each.

## Slide 3: Low Flow

## Slide 4: Low Flow Bridge Modeling 3 Types of Flow
Class A Low Flow - Subcritical
Class B Low Flow - Passes through critical depth
Class C Low Flow - Supercritical
Notes: Again, not that important. You will see in the output from time to time.

## Slide 5: Low Flow Bridge Hydraulics 4 methods of modeling
Energy - physically based, accounts for friction losses and geometry changes through bridge, as well as losses due to flow transition & turbulence.
Momentum - physically based, accounts for friction losses and geometry changes through bridge.
FHWA WSPRO - energy based as well as some empirical attributes. Developed for bridges that constrict wide floodplains with heavily vegetated overbank areas. Subcritical flow only.
Yarnell - empirical formula developed to model effects of bridge piers. Subcritical flow only.
Notes: Again, not that important. You will see in the output from time to time.

## Slide 6: Low Flow Bridge Hydraulics Appropriate Methods
Bridge piers are small obstruction to flow, friction losses predominate - Energy, Momentum, or WSPRO
Pier and friction losses predominate - Momentum
Flow passes through critical depth in vicinity of bridge - Energy or Momentum
Pier losses are dominant - Yarnell
Supercritical flow without piers - Energy or Momentum
Supercritical flow with piers - Momentum
Notes: Again, not that important. You will see in the output from time to time.

## Slide 7: Low Flow Bridge Modeling Class A Low Flow - Energy Method
Friction losses are computed as length times average friction slope.
Energy losses are empirical coefficient times change in velocity head (expansion and contraction losses).
Does not account for pier drag forces.
Notes: If piers are large part of obstruction to flow, this method is probably not appropriate. Also appropriate for supercritical flow.

## Slide 8: Low Flow Bridge Modeling Class A Low Flow - Momentum Method
Friction losses are external skin friction = wetted perimeter times length times shear stress.
Requires entering coefficient of drag for piers, CD
Check “Options” menu under “Bridge & Culvert Data” window for momentum equation options. Usually accept program defaults
Notes: Momentum is best for when piers and friction losses are predominant.

## Slide 9: Low Flow Bridge Modeling CD Coefficients for Piers
Circular Pier 1.20
Elongated piers with semi circular ends 1.33
Elliptical piers with 2:1 length to width 0.60
Elliptical piers with 4:1 length to width 0.32
Elliptical piers with 8:1 length to width 0.29
Square nose piers 2.00
Triangular nose with 30 degree angle 1.00
Triangular nose with 60 degree angle 1.39
Triangular nose with 90 degree angle 1.60
Triangular nose with 120 degree angle 1.72
Notes: Taken from Table 5.2 of Hydraulic Reference Manual - page 5-13

## Slide 10: Low Flow Bridge Modeling Class A Low Flow - Yarnell Equation
Based on 2,600 lab experiments on different pier shapes
Requires entering pier shape coefficient, K
Should only be used where majority of losses are due to piers.
Notes: Appropriate for Class A low flow only. Should be used only when piers are the predominant obstruction ( such as a RR trestle)

## Slide 11: Low Flow Bridge Modeling Yarnell’s Pier Coefficient, K
Semi-circular nose and tail 0.90
Twin-cylinder piers with
connecting diaphragm 0.95
Twin-cylinder piers without diaphragm 1.05
90 degree triangular nose and tail 1.05
Square nose and tail 1.25
Ten pile trestle bent 2.50
Notes: Taken from Table 5.3 of Hydraulic Reference Manual (page 5-14)

## Slide 12: Low Flow Bridge Modeling Class A Low Flow - WSPRO
Federal Highway Administrations method of analyzing bridges
Uses energy equation in an iterative procedure
Notes: This is applicable for sub-critical flow only. Should not probably be used where piers are large obstruction to flow.

## Slide 13: Low Flow Bridge Modeling Class A Low Flow - Summary
Energy & Momentum equations are appropriate for most bridges
Yarnell should only be used when piers are the major obstacles to flow
Yarnell cannot be used when there are no piers
Conservative approach is to select all methods and use highest energy loss
Notes: Also note that WSPRO and Yarnell are only applicable for sub-critical flows. If piers are involved, Momentum and Yarnell approaches are best. If both piers and friction are about equal, then momentum is best.

## Slide 14: High Flow - Pressure

## Slide 15: High Flow - Pressure

## Slide 16: High Flow - Pressure & Weir

## Slide 17: High Flow Bridge Modeling
When bridge deck is a small obstruction to the flow and not acting like a pressurized orifice, use energy method.
When overtopped and tailwater is not submerging flow, use pressure/weir method.
When overtopped and highly submerged, use energy method.

## Slide 18: High Flow - Weir Flow
Q = Total flow over the weir
C = Coefficient of discharge for weir flow (~2.5 to 3.1 for free flow)
L = Effective length of the weir
H = Difference between energy elev. upstream and road crest
Default Max Submergence = 0.95 (95%) (see next slide)
After max submergence reached, program reverts to energy equation for solution.

## Slide 19: High Flow - Submergence
Default Max Submergence = 0.95 (95%) (see next slide)
After max submergence reached, program reverts to the energy equation for the solution.

## Slide 20: High Flow - Submergence

## Slide 21: Adding the Bridge
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 22: Adding the Bridge
Select the Brdg/Culv button from the geometry data window:
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 23: Adding the Bridge
This brings up the Bridge Culvert Data window:
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 24: Adding the Bridge
From the options menu, select “Add a Bridge and/or Culvert”:
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 25: Adding the Bridge
This brings up a window asking for the river station of the bridge. It will locate the bridge numerically between cross-sections:
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 26: Adding the Bridge
This brings up a window with the adjacent upstream and downstream cross-sections plotted:
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 27: Adding the Bridge
Next, select the Deck/Roadway button from the Bridge data window:
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 28: Adding the Bridge
Notice the weir coefficient and max submergence window are showing the default values:
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 29: Adding the Bridge
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 30: Adding the Bridge
Enter the data for the required values. Note that the U.S. and D.S. sideslopes are for cosmetic purposes only unless using the WSPRO method for low flow:
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 31: Adding the Bridge
Use the “Copy Up to Down” button to repeat the station-high chord-low chord data from the upstream to the downstream side, if applicable:
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 32: Adding the Bridge
After selecting OK from the bridge deck window, it replots the U.S. and D.S. x-sections showing the bridge deck:
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 33: Adding the Bridge
Piers can be added by selecting the Pier button from the bridge data window:
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 34: Adding the Bridge
This brings up the Pier Data Editor where you can add the data for the pier(s) :
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 35: Adding the Bridge
The pier is then shown graphically on the plot:
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 36: Adding the Bridge
The modeling options, including low flow and high flow modeling methods, are available by selecting the Bridge Modeling Approach button:
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 37: Adding the Bridge
This brings up Bridge Modeling Approach Editor window. Notice the option to compute each type of low flow method and the option to select which one you use:
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 38: Adding the Bridge
See following graph
Orifice Coef. - between 0.7 and 0.9

## Slide 39: High Flow - Orifice Discharge

## Slide 40: Adding the Bridge
There are several other options in the options menu from the bridge data window …
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 41: Adding the Bridge
… as well as the view menu:
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 42: Adding the Bridge
The geometric data schematic is also updated automatically:
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 43: Locating Cross-Sections Near Bridges
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 44: Cross-Sections Near Bridges
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 45: Cross-Sections Near Bridges
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 46: Cross-Sections Near Bridges
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 47: Cross-Sections Near Bridges
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 48: Cross-Sections Near Bridges
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 49: Cross-Sections Near Bridges
Rule of Thumb:
ER = 2:1
CR = 1:1
Notes: Best to enter after main cross sections are in (4, 3, 2, and 1). Automatically brings up bounding cross sections based on station of bridge

## Slide 50: Bridge Cross Sections

## Slide 51: Bridge Cross Sections

## Slide 52: Bridge Cross Sections Example Computation of Le and Lc
This assumes ER=2 and CR=1

## Slide 53: Expansion & Contraction Coefficients

## Slide 54: Bridge Modeling Expansion and Contraction Coefficients at the 4 cross-sections for a bridge (example)
Expansion Contraction
Cross-Section 4 (furthest US) 0.5 0.3
Cross-Section 3 0.5 0.3
Cross-Section 2 0.5 0.3
Cross-Section 1(furthest DS) 0.3 0.1
Notes: Refer to same handout for locations of x-sections 2, 3, and 4

## Slide 55: Ineffective Flows
At XS’s 2 & 3

## Slide 56: The End