## Slide 1
CI62B DISEÑO DE OBRAS PORTUARIAS
Débora Riquelme Valencia

## Slide 2: Características Generales
1. Dimensiones
Eslora
Manga
Calado Full
Calado en Lastre
Puntal
Francobordo
1.1 Eslora:
Longitud total de una embarcación medida desde la proa hasta la popa
1.2 Manga:
Anchura máxima de la sección transversal del casco del buque
1.3 Calado:
Profundidad que alcanza en el agua la parte sumergida de un barco. Se mide desde el canto inferior de la quilla hasta la línea de flotación con máxima carga (full) o descarga (en lastre)
1.4 Francobordo:
Altura máxima de la sección transversal emergida de la nave, medida en las bandas del mismo. Depende del estado de carga de la nave.
1.5 Puntal:
Altura máxima de la sección transversal

## Slide 3: Movimientos de una Nave
Deriva - Swaying:
Movimiento del buque, libre o amarrado, consistente en un desplazamiento global del mismo en la dirección el eje horizontal principal perpendicular al plano longitudinal del buque.
Vaivén - Surging:
Movimiento del buque libre o amarrado consistente en un desplazamiento global del mismo en la dirección del eje horizontal paralelo al plano longitudinal del buque
Alteo - Heaving:
Movimiento del buque libre o amarrado consistente en un desplazamiento global del mismo en la dirección de su eje vertical principal
Cabeceo - Pitching:
Movimiento del buque libre o amarrado consistente en un giro alrededor del eje horizontal principal perpendicular al plano longitudinal del buque. Produce la máxima oscilación vertical en la proa y en la popa.
Guiñada - Yawing:
Movimiento del buque libre o amarrado consistente en un giro alrededor del eje vertical principal del buque.
Balanceo - Rolling:
Movimiento del buque libre o amarrado consistente en un giro alrededor del eje horizontal principal paralelo al plano longitudinal del buque.

## Slide 4: Nave Según su Carga
1. Carga de Pasajeros
En la actualidad el diseño estándar de estos cruseros es el Panamax de sobre los 90.000 GT. Sin embargo, exiten Post Panamax con un tamaño máximo de 150.000 GT el cual es un tamaño intermedio para los grandes cruceros del futuro.

## Slide 6: Nave Según su Carga
2. Carga de Contenedores
En la actualidad, mucha de la carga general se transporta en contenedores.
Los portacontenedores, también se conocen como "box" ships. Los contenedores que transportan estas naves, tienen 20 y 40 pies de largos.
2. Carga de Contenedores
La capacidad de un portacontenedor se mide en TEU.
Feeder container ship
Portacontenedor con equipo de descarga propio

## Slide 7
Portacontenedor de tamaño mediano
Portacontenedor de tamaño grande
Típica feeder container ship de tamaño mediano de 900 TEU

## Slide 8: Nave Según su Carga
2. Carga de Contenedores
Todas las bodegas de los portacontenedores tienen guías para que los contenedores puedan deslizar y descender.

## Slide 9: Nave Según su Carga
2. Carga de Contenedores - Multipropósito
Estas naves son capaces de transportar carga general, carga a granel y en la cubierta pueden transportar contenedores.
Normalmente, estas naves operan con equipos propios, tales como grúas.

## Slide 10: Cinco Generaciones de Portacontenedores

## Slide 11: Cinco Generaciones de Portacontenedores
You can see these numbers painted along the deck.
The securing and lashing of containers on ship's decks is a difficult operation in terms of the work environment. There are great problems during loading and discharge of containers. The stevedores who carry out this work, known as riggers, have to work on container stacks which often are 13 metres high or more above the ship's deck. Safety arrangements are in some ports poor and the work frequently has to be performed in the dark, under windy and rainy or sometimes icy conditions. The difficulties are to a large extent due to the lashing equipment. The immense diversity of the devices used gives rise to great problems. Securing of containers is the responsibility of the ship's master, which can mean that there are large differences in the manner in which the operation is effected between individual vessels and shipping companies.
In the early years of containerisation, existing general cargo vessels were converted with the removal of tween decks and the addition of cell guides into the cargo holds. On deck, the hatch covers were strengthened and fittings added for lashings. However, the containers on deck were seldom stowed above one high and so were secured to the vessel by 'traditional' cargo ship methods. Often seen still trading today, are a few of the 'first generation' vessels built during the late sixties and early seventies. These ships were the first to be designed and built as pure container carriers. The holds and hatch covers were as wide as possible, and container posts were fitted on deck to facilitate loading of deck-stowed containers out to the ship's side. For this generation of vessel, two systems of securing the cargo were common. One relied on the use of twistlocks in conjunction with lashing bars or chains, and the second relied on the use of stacking cones and bridge pieces in conjunction with lashing bars or chains. Gradually, due to the increased utilisation of differing height containers, the second method became redundant and it became common practice to use twistlocks throughout the stow. This method normally allowed containers to be stacked three high and, in some cases, four high if the fourth tier was light in weight or empty. For first generation vessels, computer technology was not available onboard to speedily calculate dynamic loads acting on container lashings and frames. The shipboard computer (if any) was only used to calculate stresses and stability for the ship itself. Therefore, the shipboard staff would ensure the vessel was lashed according to a lashing plan taken from the lashing equipment manufacturer's manual, which appeared to assume an ideal stow with respect to the distribution of weight in each stack (the homogenous stack).
On post-panamax vessels - where among other features the vessel's large beam results in an unavoidable, relatively large GM (metacentric height), and 6-high stowage on deck is common - the modern practice is for the vessel to be fitted with a lashing bridge; a substantial steel structure running athwartships between each forty foot container bay. This allows the second and third tiers of containers to be secured to the bridge using lashing rods and turnbuckles, whilst the whole stow is secured throughout with twistlocks. The lashing bridge allows the anchoring points for each stack to be moved higher up the stack, which allows the lashings to be more effective in reducing the tipping moments acting on a stack when a vessel is rolling heavily. However, the practice of fitting the bridges between forty foot bays means that the twenty foot containers can only take advantage of the lashing bridges at one end. So, in effect, the twenty foot stacks have to revert to the limits of a conventional lashing system.. This is the case, because the practice of estimating the forces acting on a stack divides the container weight equally between each end of the container. So the weight in each twenty foot container is limited by the capacity of the lashing system at the container end, which does not have the advantage of being secured by a lashing bridge. On smaller vessels, the whole stow is also secured throughout with twistlocks, and the lowest three tiers are secured to the hatch cover or support post using the lashing bar/turnbuckle combination. However, since the mid 1980s, naval architects have produced computer programs to calculate the dynamic loads acting on container stacks. Such programs have been designed for use by ships' officers and container planners. On modern vessels, 5-high and 6-high stowage on deck is common; the use of onboard computers to check the dynamics of the stow in all weather conditions is vitally important for the safe carriage of the cargo.
Container Lashing
Dependiendo de la cantidad de TEU y de las dimensiones del casco, las naves portacontenedores pueden clasificarse en los siguientes grupos o clases:
Small Feeder < 1000 TEU
Feeder 1000 – 2500 TEU
Panamax 2500 -4500/5000 TEU
Post Panamax 4500/5000 – 10000 TEU
Suezmax 10000-12000 TEU
Post- Suezmax > 12000 TEU
Small Feeder < 1000 TEU
Normalmente son utilizados para viajes cortos.
La manga de estas naves son menores a 23 m
Feeder 1000 - 2500 TEU
Transportan más de 1000 TEU y son utilizados para suministrar mayor cantidad de contenedores, además su servicio comercial es ser utilizado donde la demanda por naves portacontenedores es baja.
La manga de un feeders es de 23 – 30 m
Panamax
Hacia 1988, las dimensiones del casco de la nave portacontenedores más grande, eran las del Panamax, cuya eslora y manga fue limitada por el largo y ancho de las cámaras del Canal de Panamá, i.e. una máxima breadth (manga) de 32.3 m, una max. length (eslora) de 294.1 m (965 ft), y el max. draught (calado) de 12.0 m (39.5 ft).
Estas condiciones para pasar a través del Canal. Estas dimensiones corresponden a una capacidad entre 4,500 and 5,000 teu.
Post - Panamax
En 1988, se construyó el primer portacontenedor con una manga mayor a 32.3 m. Esta fue la primera nave Post- Panamax.
La nave post – Panamax más grande tiene una capacidad aproximada de 9,600 teu y excede la manga del Panamax en aprox. 13 m..
Suezmax
Denominados también como Ultra Large Container Ships (ULCS).
Tienen una capacidad de transportar 12,000 TEU.
Estas naves tiene una breadth de 50 m / 57 m y max. draught de 16.4 m /14.4 m para pasar a través del Canal de Suez.
Post - Suezmax

## Slide 12: Nave Según su Carga
3. Carga a Granel
La principal ventaja que presenta el transporte de la carga a granel es que el costo de embalaje puede ser muy reducido y la operación de descarga y carga puede ser muy rápida.

## Slide 13
Estas naves generalmente transportan mineral de hierro o carbón.
Bulk carrier con grúas torre.
Muchos bulk carrier son diseñados para transporte de carga a granel y contenedores.
Bulk carrier de tamaño mediano con cubierta plegable y grúa gantry sobre rieles

## Slide 14
Nave para el transporte de madera en chips, en el cual se muestra el sistema de descarga.
Bulk carrier de cemento con grúas sobre rieles para descarga y carga del material.

## Slide 16: Ro-Ro Vessel

## Slide 17: Ro-Ro Vessel