## Slide 1: GEOTECHNICAL ENGINEERING IN RESIUDAL SOILS University of Chile, Santiago PART 2: Factors controlling the properties or soils (three main groups ?)

## Slide 2: SOIL GROUPING – ON WHAT BASIS?
Undisturbed and remoulded?
Normally consolidated and over-consolidated?
Fully saturated and partially saturated?
Sedimentary (transported) and residual?
Perhaps the best basic grouping is as follows:
(a) Sedimentary soils
(b) Residual soils
(c) Remoulded (or destructured) soils

## Slide 3: Factors influencing soil formation - two factors make sedimentary soils more predictable: (a) sorting processes (b) stress history

## Slide 4: Soil properties are closely linked to their composition and the processes which formed them
We need to be aware of the formation processes applicable to any particular soil

## Slide 5: SEDIMENTARY SOILS:
The sorting process during erosion, transportation and redeposition tends to produce homogeneous soils
The loading and unloading ie “stress history” is a major influence on behavioural characteristics - provides the basis for division into N.C. and O.C.
( Importance of stress history probably somewhat over-stated)
Leaching, aging and hardening are equally important influences

## Slide 6: Influence of aging or “hardening” on soft normally consolidated clay” (OCR = 2)

## Slide 7: RESIDUAL SOILS – IMPORTANT CHARACTERISTICS :
Variability and heterogenuity
Structure – (a) from features of parent rock
(b) new, from weathering process.
The soil may not be “particulate” ie not a collection of individual particles.
Absence of stress history influence
Presence of unusual clay minerals
The zone of interest to geotechnical engineers may be mainly above the water table.

## Slide 8: Factors governing behaviour of three groups

## Slide 9: REMOULDED SOILS
The term “de-structured” soils is sometimes preferred for these soils
Includes soils prepared by sedimentation from an artificial soil slurry.
While generally free of structure, some compaction processes my create minor structural characteristics.