## Slide 1: GEOTECHNICAL ENGINEERING IN RESIDUAL SOILS University of Chile, Santiago PART 3: GROUPING & CLASSIFICATION SCHEMES FOR RESIDUAL SOILS

## Slide 2: Present Classification Systems:
Methods based on the weathering profile
(b) Methods based on pedalogical classification systems
(c) Methods intended for local use on specific soil types only

## Slide 3: Methods based on weathering profile:
Profile from Little (1969), based on experience with weathered granite

## Slide 4: Note the six weathering categories:
VI Soil
V Completely weathered
lV Highly weathered
lll Moderately weathered (rock 80 to 90%)
ll Slightly weathered
l Fresh rock

## Slide 5: Limitations of this method
describes the weathering profile of igneous rocks in the tropics (Little’s intention)
does not provide any comparative information between soils from one rock type and another
the profile shown in the Little figure is relevant only to certain types of rocks
other types of rock produce different profiles.

## Slide 6: Variations in weathering profile

## Slide 7: Notes on weathering profiles:
Weathering of (igneous) acidic rocks produces a thick gradual transition zone, while basic rocks produce a very thin sharp transition zone.
With volcanic ash or lahar layers, weathering may be greater deeper down – depending on relative age of layers.
With limestones, there is no transition zone. The weathering process is simply one of solution of the whole rock.
Soil profile from highly stratified sandstone reflects the layers of the parent rock as much as the weathering influence.

## Slide 8: Use of Pedalogical Group Names
Various group names have been borrowed from pedalogical systems used by soil science.
They have crept in randomly - for convenience
The first and best known is probably laterite
The three most commonly used at present are probably lateritic soil, latosol, and black cotton soil

## Slide 9: Three pedalogial groups

## Slide 10: British Geological Society System
A very complex system based on pedologial methods
Almost no clear connection between classification groups and engineering properties
Probably best ignored for engineering purposes

## Slide 11: Methods for specific local use
Toncer and Lohnes describe a method for use with lateritic soils in Hawaii and Puerto Rico.
Pender describes an adaptation of Little’s method for use with NZ weathered greywacke
With and Zeiglet describe a system specifically developed for one project - the Baltimore subway project
These approaches are very practical and very useful

## Slide 12: A USEFUL GROUPING SYSTEM
The two components of residual soil that give them distinctive characteristics are:
Mineralogical composition
Structure
These can be used as the basis for a grouping system for residual soils

## Slide 13: Three main groups on basis of mineralogical composition:
Group A: Soils without strong mineralogical influence
Group B: Soils with strong mineralogical influence from conventional (usual) clay minerals commonly found in sedimentary soils.
Group C: Soils with strong mineralogical influence from special clay minerals not found in sedimentar soils.

## Slide 14: Each group can be sub-divided on basis of soil structure.
Types of soil structure:
Macro structure – joints, fault lines, bedding planes, - features visible to the naked eye.
Micro structure – bonding or cementing between particles – not visible to the naked eye.

## Slide 15: Macro- structure in weathered sandstone

## Slide 16: Minor macro-structure but important micro-structure (sensitive volcanic ash)

## Slide 17: Soil with no structural influence - tropical red clay

## Slide 18: Group A Soils – little influence from mineralogy.
Generally of a rather coarse nature ie a relatively low clay fraction
Clay fraction usually of low activity mineral ie kaolinite.
A common example of this group is weathered granite.

## Slide 19
A group A soil: Weathered granite

## Slide 20: Group B – Soils with strong infuence from “common” clay minerals
One dominant group – “black cotton soils”
Strongly influenced by presene of active clay minerals of the smectite group
The clay mineral montmorillinite is the most common member of this group.

## Slide 21
Group B soil: Montmorillinite clay
- shallow failure on gentle slope

## Slide 22: Group C soils: strong influence from unusual clay minerals
Three important minerals:
Allophane/imogolite
Halloysite
Sesquioxides.

## Slide 23: Weathering sequence for the three unusual clay minerals
Volcanic ash - “glass” composition
Allophane
Halloysite
Laterite - Sesquioxides - Hydrated oxides of iron (geothite) and aluminium (gibbsite)

## Slide 24: Notes on this weathering process:
Formation of allophane is conditional on non crystalline parent material (glass)
The weathering process involves both chemical change and leaching (solution) out of silica
Removal of silica leads to concentration of iron and aluminium compounds – the sesquioxides.
The sesquioxides tend to act as cementing agents, leading to formation of laterite, a hard gravelly material

## Slide 25: Outline of Grouping System
Major Division - mineralogy | Sub-group - structure | Other information - especially parent rock
Group A – no strong mineralogical influence | Macro-structure Micro-structure No structure | 
Group B – strong influence from “normal” clay minerals | Macro-structure Micro-structure No structure | 
Group C – strong influence from unusual clay minerals | Macro-structure Micro-structure No structure | 

## Slide 26: Grouping system

## Slide 27: Group examples and properties

## Slide 28: The place of conventional classification systems:
This grouping system is not intended to be a rigorous classification system to replace existing systems
It is intended to identify soil groups that can be expected to have similar engineering properties
It should be used alongside other well established systems, in particular the Unified Soil Classification System.

## Slide 29: A point about the Plasticity Chart
The position a soil occupies on the chart is a very useful indicator of likely behaviour.

## Slide 30: FIN Gracias por su atencion