## Slide 1: GEOTECHNICAL ENGINEERING IN RESIDUAL SOILS University of Chile, Santiago PART 7: GEOTECHNICAL ENGINEERING IN RESIDUAL SOILS

## Slide 2: A General Observation on Geotechnical Engineering in Residual Soils :
Two important factors should be recognised:
The soil itself may behave rather differently from “normal” sedimentary soils.
A lot of the “action” or activity of interest to geotechnical engineers often occurs above the water table, so the pore pressure state here needs to be taken into account.

## Slide 3: Foundation Design and Settlement Estimates
Shallow Foundations – Bearing Capacity
Relatively high strength of most residual soils means that surface foundations are widely used
Normal bearing capacity theories apply, but following points should be noted

## Slide 4: Points to Note
High permeability means that foundation loading may be drained.
Design still usually done on basis of undrained strength (E/Q loading is still undrained)
Heterogeneous material makes measurement of shear strength difficult. Plate loading tests a good alternative.
Influence of discontinuities needs consideration – effect not as great as on slope behaviour.
Construction in hilly areas means bearing capacity may be influenced by proximity of slopes.

## Slide 5: Settlement Predictions
Magnitude
Rate
Oedometer test probably still the most used basis for settlement predictions
Alternatives are in situ tests, especially plate loading tests

## Slide 6: Magnitude
It appears that estimates based on oedometer test results are generally conservative –ie they are overestimates. Two possible reasons for this are:
Sample disturbance – mentioned earlier – can be minimised by block sampling
Influence of pore pressure state in the ground not taken into account – assumption usually made that pore pressure equilibrium state is unchanged by construction of foundation.

## Slide 7: Possible pore pressure states

## Slide 8: We cannot know the pore pressure state at time of construction
If foundation and structure are built during wet weather, the final pore pressure is likely to be less – meaning an increase in effective stress, and an underestimate of settlement
If foundation and structure are built during dry weather, the final pore pressure is likely to be more – meaning a decrease in effective stress, and an overestimate of settlement
(swelling could even occur)

## Slide 9: (b) Time Rate

## Slide 10: Solutions for the 2D case of a strip footing, and the 3D case of a circular footing have been obtained by Davis & Poulos (1972)
Numerical methods were used to obtain the solutions
Because there is no longer a fixed max drainage path length, the time factor T is defined in terms either of the depth to the hard layer, or a dimension of the foundation.
The solutions are given for a range of ratios of depth to foundation dimension.

## Slide 11: David & Poulos solution for a strip footing

## Slide 12: Davis & Poulos solution for a circular footing

## Slide 13: Consider the following example:
Circular footing of radius = 1m
A deep soil layer overlying an impermeable base
A soil with a cv value of 0.1 m2/day
Assuming h/a to be about 50, the value of T90 is about 20, so that t90 is about 200 days or 6 months.
Many residual soils have cv values greater than this, so that if the construction period is 6 months or longer, most settlement will occur during construction

## Slide 14: If settlement occurs as the load is applied then we can not divide settlement into immediate (elastic) settlement and consolidation (primary) settlement It is also not possible to divide settlement into primary and secondary settlement

## Slide 15: Deep Foundations
Large bored piles are widely used in residual soils, especially for high rise building in cities.
Some bored piles are constructed dry and some wet (ie drilled below water level)
Dry piles are a big advantage – material can be inspected directly, and hole can be properly cleaned out
Larger safety factors are necessary when bored piles are formed wet, because base of hole may not be properly cleaned out.

## Slide 16: Slope Stability & Slope Engineering
Slope in residual soils often stable at steep angles
Slips are commonly triggered by heavy rainfall
Extent to which stability can be evaluated by analytical methods often very limited because of:
uncertainty in strength parameters,
influence of discontinuites,
uncertain seepage conditions.

## Slide 17: Types of slides (failure modes) in residual soils

## Slide 18: Limitations of Analytical Methods
With respect to strength parameters, - three slope categories:
Slopes of homogeneous soils
Slopes containing distinct continuous planes of weakness
Slopes of heterogeneous material, but without distinct planes of weakness

## Slide 19: Slope of homogeneous soil

## Slide 20: Slopes consisting of homogeneous materials
Value of  can be measured with reasonable accuracy
Value of c is very significant but not so easy to measure (tests at low stress levels needed)

## Slide 21: Slope containing distinct planes of weakness

## Slide 22: Slopes containing specific planes of weakness
Presence of discontinuities may completely rule out analytical methods of assessing stability
Sometimes, discontinuities all have a common orientation.
If the orientation can be determined, and the strength on it measured, then analytical methods may still be possible

## Slide 23: Slope of heterogenous material, without distinct planes of weakness

## Slide 24: Slopes of heterogeneous materials without distinct planes of weakness
Not the same situation as previous case
Determination of strength parameters still very difficult, because of difficulty of sampling
It may be possible to determine strength parameters by back analysis – we will look at these methods later.

## Slide 25: Seepage Conditions & Pore Pressures
Slips in residual soils usually occur during periods of heavy rainfall – the result of incresed pore pressures
This is an important difference between residual and sedimentary soils.
For example, in “London clay” pore pressures do not change significantly with seasons – they only change as a result of human activity

## Slide 26: Further notes re pore pressures
Stability analysis must normally be carried out in terms of effective stresses
The pore pressure must be the “worst case” value, or at least a value related to a storm intensity, ie a 10 year or a 100 year storm
By doing this, a “supposed” known risk is accepted, similar to the risk accepted in designing for floods

## Slide 27: Influence of negative pore pressures
Many slopes in residual soils are stable at steep angles because of negative pore pressure (suction or pore water tension)
Influence of rainfall may simply be to reduce the negative pore pressure
Rainfall can still induce failures even though the water table does not rise above base of slope

## Slide 28: Prediction of Pore Pressures in Residual Soils
There are no reliable ways of predicting the “worst cast” pore pressures, or the values corresponding to particular storm events
Various methods are being proposed, from theoretical to empirical
It is unlikely that there will ever be reliable theoretical methods – because of heterogenuity and difficulty of defining relevant parameters

## Slide 29: A theoretical method available in the Seep/W and Slope/W programmes

## Slide 30: What the method does
SEEP/W is used to carry out a transient analysis of the changes in water table and pore pressures below and above the water table.
Inputs include rainfall intensity, and soil parameters such as permeability, compressibility, and air entry value.
The transient pore pressure conditions are then transferred to SLOPE/W to determine corresponding safety factors.

## Slide 31: Influence of rainfall on safety factor after 4 days of intense rainfall - note that the water table has not risen above the toe of the slope

## Slide 32: Change in suction graphs Toe of slope is at Elev. 13m

## Slide 33: Strength change with suction change
Note: “Suction strength” is actually a component of frictional strength but is calculated separately in the strength parameters used.

## Slide 34: Safety factor related to rainfall intensity
Note that no change in SF occurs until rainfall intensity exceeds a certain value

## Slide 35: How reliable is this theoretical method?
The “model” used for seepage in partially saturated soils and for predicting pore pressure changes in response to rainfall is a reasonable approximation, but involves simplistic assumptions
The model for the soil shear strength also involves simplifying assumptions to take account of partial saturation
The method is very useful for helping to understand the concepts involved in seepage mechanics above the water table, and especially the influence of partial saturation

## Slide 36: The Hong Kong situation
Hong Kong has been doing field measurements of pore pressure response to weather effects for about 3 decades.
In conjunction with this attempts have been made to develop predictive methods
These methods are essentially empirical
Pore pressure response can be divided into two types – seasonal response and storm response.

## Slide 37: Piezometer response in Hong Kong slopes - note the great variety of responses

## Slide 38: Comments on the computer method and the Hong Kong records
The great variety of responses obtained from the Hong Kong measurements shows the difficulty of trying to predict pore pressure behaviour theoretically
The computer prediction does agree with one of the Hong Kong forms – it predicts no response until the rainfall intensity reaches a certain value. It thus predicts no seasonal response, only intense storm response.
This sort of behaviour seems quite hard to explain

## Slide 39: Note Kenny & Lau paper (1984)
Their study, both from observation and theoretical considerations, suggests that pore pressures in a slope will only change significantly with seasonal change if cv is greater than about 0.1m2/day.

## Slide 40: Mechanics of Analytical Methods
In general effective stress analysis is essential
The only exception is an embankment built on a residual soil – the undrained strength of the foundation soil could be used
Any well recognised method of stability analysis is OK – Bishop, Sarma, Morgenstern & Price, Spencer etc.

## Slide 41: Particular Rock/Soil Types
We will look at particular residual soil types later in Part 6 of this course, in particular:
Ingneous Rocks
Sandstones
Volcanic materials

## Slide 42: Safety Factors – the Hong Kong “Guide”

## Slide 43: Back Analysis Methods to Determine Soil Parameters
Analysis of a single slip
Analysis of a number of slips in same material
Analysis of intact slopes
Analysis for retaining forces for cuts in slopes

## Slide 44: Can we determine the values of c and  from this one slip?

## Slide 45: Which is the correct combination of c and  ? - there are several ways to find out.

## Slide 46: Slip circle analysis using each set of c and  values

## Slide 47: Ignore the actual slip - determine new combinations of c and  to give SF = 1

## Slide 48: Mohr-Coulomb failure lines for the c and  combinations

## Slide 49: Back Analysis of a Number of Slips in the Same Material
For each slip it is possible to calculate the average value of shear stress and effective normal stress along the slip surface (Pore pressure must be known)
This gives one point to plot on a graph of shear stress against normal stress
With a number of such points a Mohr-Coulomb failure line can be determined.

## Slide 50: London Clay Example

## Slide 51: Analysis of Data from a Large Number of Intact Slopes (in the same material)
Field surveys and measurements can gather data on slope height and slope angle from as many slopes as possible consisting of the same material.
The higher and steeper the slopes the better
This information an be plotted and then a “curve fitting” procedure used to determine values of c and 

## Slide 52: Curve fitting to slope height & slope angle data - can be quite a tedious procedure

## Slide 53: Determination of Retaining Forces for Cuts in Steep Slopes
Determination of the force P to retain a cut as shown can be quite difficult – back analysis can provide a solution – this will be a tutorial exercise.

## Slide 54: Assessment of the stability of natural slopes involves the following:
Visual inspection of the slope
Geological appraisal of slope and surrounding area
Inspection of aerial photos
Inspection of any existing cuts in similar material
Analytical studies
It is probably the case that 80 to 90% of the “input” into any assessment of slope stability comes from non analytical methods – only 10 to 20 % from analytical methods

## Slide 55: Visual inspection – shape of slope surface

## Slide 56: Remedial measure to stabilise slopes
Engineers often are called in after a slip has occurred to advise on how to stabilise the slope.
Site investigation and soil testing should be focused on gaining information useful for designing remedial work.
Too often a lot of time and money are spent on investigation and measurement of properties which are not helpful to the design of remedial measures.

## Slide 57: First possibility is to reduce the disturbing forces:
Flatten the slope
Reduce the height
Add a toe weight (berm)

## Slide 58: Second possibility is to increase the shear resistance of the soil
Lower the pore water pressure (drainage) - frequently used
Use mechanical keying such as piling or retaining walls – sometimes used
Grout the soil – rarely used

## Slide 59: The measure(s) to be used in a particular situation depend on the nature of the slope and the slip.
Two kinds of slope/slip:
Slope of limited height – rotational slips
Slope of great height – translational slips

## Slide 60: Slopes of limited height/ rotational slips – reshaping

## Slide 61: Drainage measures

## Slide 62: Slopes of “unlimited” height – translational slides. Reducing pore pressure is often the only practical possibility

## Slide 63: Other notes:
In many situations, it is only possible to raise the safety factor by a small amount - from 1.0 to 1.1 or 1.2
Mechanical methods can sometimes be used – especially in urban situations
Grouting is rarely possible – slides generally occur in clay, and grouting is often not possible in clay.

## Slide 64: Earthworks and Compaction

## Slide 65: Issues in compacting residual soils
Soil is much wetter than optimum
Soil is highly variable
Soil is an allophane clay, without a clear optimum water content
Soil is highly structured & sensitive, and softens during compaction (over-compaction)

## Slide 66: Soils much wetter than optimum
No simple solution – essentials are:
Adequate spells of dry (and windy) weather
Plenty of wide, open space, so the soil can be spread out, and exposed to max. sunshine and max. wind
Good site management. Maximising use of dry weather, and not exposing loose fill to rainfall. All stockpiles should be sealed by surface shaping and rolling to prevent water infiltration.

## Slide 67: Highly variable soils on small sites - control using optimum water content and dry density almost impossible.

## Slide 68: An alternative method uses undrained shear strength and air voids as control parameters
This method completely overcomes the problem of variable soil type – the same limits of undrained shear strength and air voids apply regardless of variations in the soil.

## Slide 69: Concept of the method

## Slide 70: Important aspects of the method
The lower limit on undrained shear strength prevents the soil being too wet
The upper limit on air voids prevents the soil being too dry
Most clayey soils compacted at optimum w/c content have a shear strength of between about 150 kPa and 200 kPa.
The resulting fill has properties essentially the same as those produced by the conventional control method.

## Slide 71: Suitable control limits for compaction specification are:
Undrained shear strength:
Minimum average value: 150 kPa (10 tests)
Minimum single value: 120 kPa
Air voids:
For “normal” soils: not greater than 8%
For volcanic ash (allophane) clay: not greater than 10% or 12%

## Slide 72: Measurement of undrained shear strength and air voids
Undrained shear strength is easily measured in the field using a hand vane apparatus. Some authorities prefer to take samples and do U.C. Tests.
Air voids has to be measured in the normal way – by measuring density, water content and specific gravity.

## Slide 73: Hand shear vane of the “Pilcon” type, for in situ measurement of undrained shear strength

## Slide 74: Standard compaction test together with undrained shear strength measurements
Soil tested was a clay from weathered sandstone

## Slide 75: Additional advantages of the shear strength & air voids method of compaction control
Criteria can easily be changed to meet a particular objective
If a highly plastic (ductile) fill is needed (eg for an earth dam core) the shear strength can be lowered – 70 to 100 kPa would be appropriate
For the subgrade of a highway pavement a higher strength might be desirable – say at least 200kpa

## Slide 76: Soils Without a Clear Peak Dry Density & no Opt. Water Content – especially allophane clays
The shear strength and air voids method
is ideal for such soils

## Slide 77: Compaction of soils subject to loss of strength when remoulded or compacted (an effect called “over-compaction”)

## Slide 78: It is Important to Recognise that Compaction has Two Effects:
It “densifies” the soil, ie it pushes the particles closer together
It destroys the structure of the soil and causes it to soften. Particles and bonds may be crushed and trapped water released.
With some soils this softening effect may be small, but with other soils it may be very significant.

## Slide 79: Overcoming this problem??
Make sure you understand the properties of the soil – ie carry out adequate laboratory tests.
Find out if the soil softens with repeated compaction, and how easily it softens.
Carry out field trials of excavation and compaction to determine the best procedure. (Use a strength measurement for evaluation)
Sometimes “light” compaction with a tracked bulldozer is better than heavy sheeps-foot rollers

## Slide 80: Compaction of Ganular & Non-plastic Materials
Proctor compaction tests or relative density tests are not always useful
Tests on gravel/sand show very flat curves and water contents may not be reliable
Despite this, the test gives a useful guide to the density which can be expected in the field.
It is often the case that higher densities can be achieved by field compaction than in the Proctor test

## Slide 81: Field Trials of Compaction Are Very Useful
Objective should be to determine:
An appropriate density to aim for
The type of equipment and number of passes to achieve this density
Appropriate control methods
- measurement of density or strength

## Slide 82: For compaction control of granular materials, the use of hand penetrometers is becoming common
Small “falling weight” dynamic penetrometers are easy to use.
The parameter measured is blows/distance penetrated.
This is a measure of both density and strength – for granular materials they are closely related

## Slide 83: Types of hand penetrometers

## Slide 84: Penetrometers commonly used in some parts of the world
Dynamic: Scala penetrometer
Tip: 20mm dia. 30o point angle
Hammer weight: 9 kg
Height of fall: 51.0cm
Parameter measured: S = no of blows/100mm
Correlation with SPT:
SPT N value = 1.5 S from Scala test
Common specification
Scala S value from 50mm to 150mm in compacted fill not less than 10-12

## Slide 85: Penetrometers commonly used in some parts of the world (contd)
US Army Corps of Engineers:
Tip 12.8mm diameter 30o cone angle
Parameter measured (originally) Force in units of 0.5 pounds (1.102 kg)
The cone can be calibrated with either CBR or with undrained shear strength.
The cone is intended mainly for cohesive soils of soft to moderate strength.