## Slide 1: GEOTECHNICAL ENGINEERING IN RESIDUAL SOILS University of Chile, Santiago PART 8: OTHER SPECIAL SOIL GROUPS - PARTIALLY SATURATED SOILS, EXPANSIVE SOILS, COLLAPSING SOILS

## Slide 2: Partially saturated soils: Factors that control their existence
Climate
Particle size of the soil
Depth of water table
Topography

## Slide 3: Climate is clearly the most dominant influence
Australia, South Africa, parts of the Middle East, are known to have large areas of partially saturated soils
Wet tropical countries like Indonesia and Malaysia, and temperate countries like New Zealand and most of Northern Europe and North America contain only minor areas of partially saturated soils

## Slide 4: Climate has two significant effects:
Warm, wet climates promote intense weathering, and the formation of fine grained soils ie clays.
Warm, wet climates inhibit evaporation from the soil
These factors mean that the soils are likely to be fully saturated.
In dry climates, the opposite is likely to be true.

## Slide 5: Particle size has a very important influence
As already discussed, water cannot drain out of a very fine grained soil under gravity
The finest particle size permitting easy drainage under gravity is about 0.06mm – the division between sand and silt
Soils finer than this can still become unsaturated - by evaporation, at ground surface or along fissures or cracks in the soil

## Slide 6: The Hong Kong weathered granites – an example of partially saturated soils
Hong Kong appears to be reasonably warm and wet – but has partially saturated soils
Weathered granites in Hong Kong are not very fine grained – and the place is very hilly (ie deep water table) - this accounts for partial saturation

## Slide 7: Measurements of degree of saturation – Hong Kong study Sr = 40% with deep water table Sr = 90% with shallow water table

## Slide 8: Mechanics of Partially Saturated Soils
Soil behaviour is controlled by the effective stresses acting on it
The presence of air complicates the estimation of effective stress – pore air pressure and pore water pressure have different values, pore air pressure being greater.
Various attempts have been made to find a “form” of the effective stress equation applicable to partially saturated soils

## Slide 9: Bishop’s equation was the first and is still probably the best known
 = ( - ua) +  (ua – uw)
where  = effective stress
 = total stress
ua = pore air pressure
uw = pore water pressure
 = parameter depending on degree of saturation, having a value from 0 to1.
ua – uw is generally called the matric suction

## Slide 10: To help understand this equation consider a natural soil close to the ground surface
The air pressure is atmospheric (ie zero) so the equation becomes
 =  -  uw
Normally the equation would be
 =  – uw
so the effect of air in the soil is to reduce the influence of the pore pressure on the effective stress in the soil (Since  is less than one)

## Slide 11: Effective stress – pore pressure relationship and degree of saturation

## Slide 12: Attempts to apply this equation to analyse practical problems have not met with much success
Simpler semi-empirical approaches have been proposed
Fredlund & Rahardjo have proposed treating the components of strength coming from ( - ua) and (ua – uw) separately
This avoids trying to determine the actual or true effective stress.

## Slide 13: Main interest in analytical treatment of partially saturated soils appears be slope stability
Two behaviour “models” are needed:
One to relate the pore pressure in the ground to weather conditions (transient behaviour)
One to relate the soil strength to the pore pressure state (actually to the effective stress state)

## Slide 14: Lam, Fredlund, and Barbour (1987) method:
A form of the conventional continuity equation
Where Q is flow into element from external source
mw is the slope of the volumetric water content versus u
The volumetric water content () is the volume of water per unit volume of soil, so that:

## Slide 15: The volumetric water content, , is the volume of water per unit volume of soil, 
Changes in  arise from two sources:
Water that moves in or out as a result of compression of the soil (as in normal consolidation)
Water that flows in and out and is inter-changed with air - ie the degree of saturation varies.

## Slide 16: Volumetric water content curves

## Slide 17: Apart from  (or mw), a second parameter governs seepage, namely k – and must be defined

## Slide 18: The application of this method, along with any other complex seepage analysis, requires a numerical solution and therefore can really only be used if a suitable computer programme is available The programme SEEP/W is based around this method of Lam et al

## Slide 19: Fredlund and Rahardjo’s equation for shear strength
= c + (ua – uw)tanb + ( - ua)tan
where b = angle of cohesion intercept increase with increasing stress.
In this expression, the frictional component of shear strength is divided into two components – one essentially from the total stress, and one from the soil “suction” ie the negative pore pressure

## Slide 20: Extended Mohr-Coulomb failure envelope for partially saturated soils (Fredlund’s equation)

## Slide 21: The computer programme Slope/W uses this equation when dealing with partially saturated soils
The parameter b is usually found to have a value between 15o and 20o, (according to the writer’s of the computer programme SLOPE/W), though it could theoretically exceed 45o (????)

## Slide 22: The Fredlund expression for shear strength is not really satisfactory theoretically as it implies the contribution to shear strength from soil suction is a cohesion component, whereas it is actually a frictional component . However, the expression provides a means of modelling unsaturated soils for practical purposes.

## Slide 23: Note the difference between the Fredlund approach and Bishop’s approach.

## Slide 24: Expanisive or Swelling Clays
These problem soils occur in relatively dry countries, especially South Africa (and other parts of Africa) and Australia
The ground surface swells causing distortion and damage to buildings on shallow foundations.

## Slide 25: Conditions for occurrence of expansive clays
existence of clayey soils containing active clay minerals – smectite (montmorillonite)
a fairly dry climate, with long dry seasons and some periods of rainfall.
Both factors must be present – a case where both soil properties and groundwater conditions are equally important.

## Slide 26: Expansive clays represent a soil condition rather than a particular type of material.
Soils of the CH type found in relatively low lying flat areas having a relatively dry climate are most likely to cause swelling problems

## Slide 27: Basic mechanism
In their natural state, the soils exist in a state of high “suction” ie large negative pore water pressure
This natural state is upset and water becomes available to the soil. It soaks up water and swells
In the worst cases the soil is partly saturated, but the problem can still occur with fully saturated soils.

## Slide 28: Sources of increased water supply to the soil:
Most commonly, a change in land use
This could be urban development, or conversion of land to farming.
Irrigation or leaking pipes supply water to the ground
An external water source is not essential – simply covering the ground can be enough

## Slide 29: This swelling soil problem is simply an extension of the foundation settlement situation covered earlier – Assignment No 2
The negative pore pressure is much greater
The net change in effective stress becomes negative and the soil swells rather than compresses

## Slide 30: Situation where no external water source is needed to cause soil swelling - covering the surface cuts off evaporation, and water is taken up by the soil

## Slide 31: Estimation of Swelling Pressure and Swell Magnitude
The main concern with swelling clays is the magnitude rather than the pressure
Methods in use for estimating pressure and magnitude range from purely empirical to theoretical.
We will only consider methods which make use, or relate to the principle of effective stress in this course.

## Slide 32: Methods using the principle of effective stress involve the following:
Estimation of initial and final stresses and changes in effective stress throughout layer
Measurement of swell characteristics of the soil.
Calculation of swell of sub-layers, similar to normal settlement estimates

## Slide 33: Basic soil swelling model – 2 identical samples – water added – one allowed to swell, the other restrained

## Slide 34: Measurement of swell pressure, and swell magnitude – identical samples, differing stresses applied, water added

## Slide 35: This graph can be used directly to estimate potential swell. Note the important limitations:
The test data may be dependent on the time of year the test is done
The swell estimate assumes that “wetting” of the soil causes the suction to entirely disappear. This may not be the case in practice.

## Slide 36: Collapsing Soils
Soils which undergo a sudden decrease in volume when water becomes available to them
Usually refers to foundation performance
They behave in the opposite manner to swelling soils
Unlike swelling soils, their behaviour cannot be explained on the basis of effective stress concepts

## Slide 37: Occurrence of collapsing soils (all are partially saturated)
Loess soils – wind blown deposits having a very loose open structure
2. Highly weathered residual soils, such as some weathered granites, - and a variety of rock types in Brazil result in a “porous clay” with collapsing behaviour
Saline soils – found in various countries, including northern Chile

## Slide 38: Influence of wetting:
Softens the soil particles themselves
Softens bonds between particles
Dissolves bonding material
Eliminates surface tension forces between particles that were providing stability

## Slide 39: Illustration of collapsing behaviour

## Slide 40: Some partially saturated soils can show both expansive and collapse behaviour