## Slide 1: 8-BIT LOAD GROUP
EL54B, Sistemas para el Procesamiento de la Información
Mnemonic | Symbolic Operation | Flags |  |  |  |  |  |  |  | Op-Code |  |  |  | No. of Bytes | No. of M Cycles | No. of T States
 |  | S | Z |  | H |  | P/V | N | C | 76 | 543 | 210 | Hex |  |  | 
LD r, s | r ← s | ● | ● | X | ● | X | ● | ● | ● | 01 | r | s |  | 1 | 1 | 4
LD r, n | r ← n | ● | ● | X | ● | X | ● | ● | ● | 00 | r | 110 |  | 2 | 2 | 7
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  | 
LD r, (HL) | r ← (HL) | ● | ● | X | ● | X | ● | ● | ● | 01 | r | 110 |  | 1 | 2 | 7
LD r, (IX+d) | r ← (IX+d) | ● | ● | X | ● | X | ● | ● | ● | 11 | 011 | 101 | DD | 3 | 5 | 19
 |  |  |  |  |  |  |  |  |  | 01 | r | 110 |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | d | → |  |  |  | 
LD r, (IY+d) | r ← (IY+d) | ● | ● | X | ● | X | ● | ● | ● | 11 | 111 | 101 | FD | 3 | 5 | 19
 |  |  |  |  |  |  |  |  |  | 01 | r | 110 |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | d | → |  |  |  | 
LD (HL), r | (HL) ← r | ● | ● | X | ● | X | ● | ● | ● | 01 | 110 | r |  | 1 | 2 | 7
LD (IX+d), r | (IX+d) ← r | ● | ● | X | ● | X | ● | ● | ● | 11 | 011 | 101 | DD | 3 | 5 | 19
 |  |  |  |  |  |  |  |  |  | 01 | 110 | r |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | d | → |  |  |  | 
r , s : Registros | B | C | D | E | H | L | A | ● = Flag not affected, 0 = Flag reset 1 = Flag set, X = Flag is unknown ↕ = Flag affected according operation result IFF = Interrupt enable Flip-Flop content copied in P/V
 | 000 | 001 | 010 | 011 | 100 | 101 | 111 | 

## Slide 2: 8-BIT LOAD GROUP
Mnemonic | Symbolic Operation | Flags |  |  |  |  |  |  |  | Op-Code |  |  |  | No. of Bytes | No. of M Cycles | No. of T States
 |  | S | Z |  | H |  | P/V | N | C | 76 | 543 | 210 | Hex |  |  | 
LD (IY+d), r | (IY+d) ← r | ● | ● | X | ● | X | ● | ● | ● | 11 | 111 | 101 | FD | 3 | 5 | 19
 |  |  |  |  |  |  |  |  |  | 01 | 110 | r |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | d | → |  |  |  | 
LD (HL), n | (HL) ← n | ● | ● | X | ● | X | ● | ● | ● | 00 | 110 | 110 | 36 | 2 | 3 | 10
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  | 
LD (IX+d), n | (IX+d) ← n | ● | ● | X | ● | X | ● | ● | ● | 11 | 011 | 101 | DD | 4 | 5 | 19
 |  |  |  |  |  |  |  |  |  | 00 | 110 | 110 | 36 |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | d | → |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  | 
LD (IY+d), n | (IY+d) ← n | ● | ● | X | ● | X | ● | ● | ● | 11 | 111 | 101 | FD | 4 | 5 | 19
 |  |  |  |  |  |  |  |  |  | 00 | 110 | 110 | 36 |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | d | → |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  | 
LD A, (BC) | A ← (BC) | ● | ● | X | ● | X | ● | ● | ● | 00 | 001 | 000 | 0A | 1 | 2 | 7
LD A, (DE) | A ← (DE) | ● | ● | X | ● | X | ● | ● | ● | 00 | 011 | 010 | 1A | 1 | 2 | 7
EL54B, Sistemas para el Procesamiento de la Información
r , s : Registros | B | C | D | E | H | L | A | ● = Flag not affected, 0 = Flag reset 1 = Flag set, X = Flag is unknown ↕ = Flag affected according operation result IFF = Interrupt enable Flip-Flop content copied in P/V
 | 000 | 001 | 010 | 011 | 100 | 101 | 111 | 

## Slide 3: 8-BIT LOAD GROUP
Mnemonic | Symbolic Operation | Flags |  |  |  |  |  |  |  | Op-Code |  |  |  | No. of Bytes | No. of M Cycles | No. of T States
 |  | S | Z |  | H |  | P/V | N | C | 76 | 543 | 210 | Hex |  |  | 
LD A, (nn) | A ← (nn) | ● | ● | X | ● | X | ● | ● | ● | 00 | 111 | 010 | 3A | 3 | 4 | 13
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  | 
LD (BC), A | (BC) ← A | ● | ● | X | ● | X | ● | ● | ● | 00 | 000 | 010 | 02 | 1 | 2 | 7
LD (DE), A | (DE) ← A | ● | ● | X | ● | X | ● | ● | ● | 00 | 010 | 010 | 12 | 1 | 2 | 7
LD (nn), A | (nn) ← A | ● | ● | X | ● | X | ● | ● | ● | 00 | 110 | 010 | 32 | 3 | 4 | 13
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  | 
LD A, I | A ← I | ↕ | ↕ | X | 0 | X | IFF | 0 | ● | 11 | 101 | 101 | ED | 2 | 2 | 9
 |  |  |  |  |  |  |  |  |  | 01 | 010 | 111 | 57 |  |  | 
LD A, R | A ← R | ↕ | ↕ | X | 0 | X | IFF | 0 | ● | 11 | 101 | 101 | ED | 2 | 2 | 9
 |  |  |  |  |  |  |  |  |  | 01 | 011 | 111 | 5F |  |  | 
LD I, A | I ← A | ● | ● | X | ● | X | ● | ● | ● | 11 | 101 | 101 | ED | 2 | 2 | 9
 |  |  |  |  |  |  |  |  |  | 01 | 000 | 111 | 47 |  |  | 
LD R, A | R ← A | ● | ● | X | ● | X | ● | ● | ● | 11 | 101 | 101 | ED | 2 | 2 | 9
 |  |  |  |  |  |  |  |  |  | 01 | 001 | 111 | 4F |  |  | 
EL54B, Sistemas para el Procesamiento de la Información
r , s : Registros | B | C | D | E | H | L | A | ● = Flag not affected, 0 = Flag reset 1 = Flag set, X = Flag is unknown ↕ = Flag affected according operation result IFF = Interrupt enable Flip-Flop content copied in P/V
 | 000 | 001 | 010 | 011 | 100 | 101 | 111 | 

## Slide 4
Mnemonic | Symbolic Operation | Flags |  |  |  |  |  |  |  | OP-Code |  |  |  | No. of Bytes | No. of M Cycles | No. of T Cycles | Comments | 
 |  | S | Z |  | H |  | P/V | N | C | 76 | 543 | 210 | Hex |  |  |  |  | 
LD dd,nn | dd ← nn | • | • | X | • | X | • | • | • | 00 | dd0 | 001 |  | 3 | 3 | 10 | dd | Pair
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  | 00 | BC
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  | 00 | DE
LD IX,nn | IX ← nn | • | • | X | • | X | • | • | • | 11 | 011 | 101 | DD | 4 | 4 | 14 | 01 | HL
 |  |  |  |  |  |  |  |  |  | 00 | 100 | 001 | 21 |  |  |  | 01 | SP
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  |  | 
LD IY,nn | IY ← nn | • | • | X | • | X | • | • | • | 11 | 111 | 101 | FD | 4 | 4 | 14 |  | 
 |  |  |  |  |  |  |  |  |  | 00 | 100 | 001 | 21 |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  |  | 
LD HL,(nn) | H ← (nn+1) | • | • | X | • | X | • | • | • | 00 | 101 | 010 | 2A | 3 | 5 | 16 |  | 
 | L ← (nn) |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  |  | 
LD dd,(nn) | ddH ← (nn+1) | • | • | X | • | X | • | • | • | 11 | 101 | 101 | ED | 4 | 6 | 20 |  | 
 | ddL ← (nn) |  |  |  |  |  |  |  |  | 01 | dd1 | 011 |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  |  | 
LD IX,(nn) | IXH ← (nn+1) | • | • | X | • | X | • | • | • | 11 | 011 | 101 | DD | 4 | 6 | 20 |  | 
 | IXL ← (nn) |  |  |  |  |  |  |  |  | 00 | 101 | 010 | 2A |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  |  | 
EL54B, Sistemas para el Procesamiento de la Información
Notes: | dd is any of the register pairs BC, DE, HL, SP qq is any of the register pairs AF, BC, DE, HL (PAIR)H, (PAIR)L refer to high order and low order eight bits of the register pair respectively.
Notes: | Where a 16-bit 'nn' value or address is specified: ← n → ← n → the first byte of the pair is the least significant byte.
16-BIT LOAD GROUP

## Slide 5
Mnemonic | Symbolic Operation | Flags |  |  |  |  |  |  |  | OP-Code |  |  |  | No. of Bytes | No. of M Cycles | No. of T Cycles | Comments | 
 |  | S | Z |  | H |  | P/V | N | C | 76 | 543 | 210 | Hex |  |  |  |  | 
LD IY,(nn) | IYH ← (nn+1) | • | • | X | • | X | • | • | • | 11 | 111 | 101 | FD | 4 | 6 | 20 |  | 
 | IYL ← (nn) |  |  |  |  |  |  |  |  | 00 | 101 | 010 | 2A |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  |  | 
LD (nn),HL | (nn+1) ← H | • | • | X | • | X | • | • | • | 00 | 100 | 010 | 22 | 3 | 5 | 16 |  | 
 | (nn) ← L |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  |  | 
LD (nn),dd | (nn+1) ← ddH | • | • | X | • | X | • | • | • | 11 | 101 | 101 | ED | 4 | 6 | 20 |  | 
 | (nn) ← ddL |  |  |  |  |  |  |  |  | 01 | dd0 | 011 |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  |  | 
LD (nn),IX | (nn+1) ← IXH | • | • | X | • | X | • | • | • | 11 | 011 | 101 | DD | 4 | 6 | 20 |  | 
 | (nn) ← IXL |  |  |  |  |  |  |  |  | 00 | 100 | 010 | 22 |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  |  | 
LD (nn),IY | (nn+1) ← IYH | • | • | X | • | X | • | • | • | 11 | 111 | 101 | FD | 4 | 6 | 20 |  | 
 | (nn) ← IYL |  |  |  |  |  |  |  |  | 00 | 100 | 010 | 22 |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  |  | 
LD SP,HL | SP ← HL | • | • | X | • | X | • | • | • | 11 | 111 | 001 | F9 | 1 | 1 | 6 |  | 
EL54B, Sistemas para el Procesamiento de la Información
Notes: | dd is any of the register pairs BC, DE, HL, SP qq is any of the register pairs AF, BC, DE, HL (PAIR)H, (PAIR)L refer to high order and low order eight bits of the register pair respectively.
Notes: | Where a 16-bit 'nn' value or address is specified: ← n → ← n → the first byte of the pair is the least significant byte.
16-BIT LOAD GROUP

## Slide 6
Mnemonic | Symbolic Operation | Flags |  |  |  |  |  |  |  | OP-Code |  |  |  | No. of Bytes | No. of M Cycles | No. of T Cycles | Comments | 
 |  | S | Z |  | H |  | P/V | N | C | 76 | 543 | 210 | Hex |  |  |  |  | 
LD SP,IX | SP ← IX | • | • | X | • | X | • | • | • | 11 | 011 | 101 | DD | 2 | 2 | 10 |  | 
 |  |  |  |  |  |  |  |  |  | 11 | 111 | 001 | F9 |  |  |  |  | 
LD SP,IY | SP ← IY | • | • | X | • | X | • | • | • | 11 | 111 | 101 | FD | 2 | 2 | 10 |  | 
 |  |  |  |  |  |  |  |  |  | 11 | 111 | 001 | F9 |  |  |  |  | 
PUSH qq | (SP-2) ← qqL | • | • | X | • | X | • | • | • | 11 | qq0 | 101 |  | 1 | 3 | 11 | qq | Pair
 | (SP-1) ← qqH |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | BC
 | SP ← SP-2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | DE
PUSH IX | (SP-2) ← IXL | • | • | X | • | X | • | • | • | 11 | 011 | 101 | DD | 2 | 4 | 15 | 1 | HL
 | (SP-1) ← IXH |  |  |  |  |  |  |  |  | 11 | 100 | 101 | E5 |  |  |  | 1 | AF
 | SP ← SP-2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PUSH IY | (SP-2) ← IYL | • | • | X | • | X | • | • | • | 11 | 111 | 101 | FD | 2 | 4 | 15 |  | 
 | (SP-1) ← IYH |  |  |  |  |  |  |  |  | 11 | 100 | 101 | E5 |  |  |  |  | 
 | SP ← SP-2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
POP qq | qqH ← (SP+1) | • | • | X | • | X | • | • | • | 11 | qq0 | 001 |  | 1 | 3 | 10 |  | 
 | qqL ← (SP) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | SP ← SP+2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
POP IX | IXH ← (SP+1) | • | • | X | • | X | • | • | • | 11 | 011 | 101 | DD | 2 | 4 | 14 |  | 
 | IXL ← (SP) |  |  |  |  |  |  |  |  | 11 | 100 | 001 | E1 |  |  |  |  | 
 | SP ← SP+2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
POP IY | IYH ← (SP+1) | • | • | X | • | X | • | • | • | 11 | 111 | 101 | FD | 2 | 4 | 14 |  | 
 | IYL ← (SP) |  |  |  |  |  |  |  |  | 11 | 100 | 001 | E1 |  |  |  |  | 
 | SP ← SP+2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
EL54B, Sistemas para el Procesamiento de la Información
Notes: | dd is any of the register pairs BC, DE, HL, SP qq is any of the register pairs AF, BC, DE, HL (PAIR)H, (PAIR)L refer to high order and low order eight bits of the register pair respectively.
Notes: | Where a 16-bit 'nn' value or address is specified: ← n → ← n → the first byte of the pair is the least significant byte.
16-BIT LOAD GROUP

## Slide 7
Mnemonic | Symbolic Operation | Flags |  |  |  |  |  |  |  | OP-Code |  |  |  | No. of Bytes | No. of M Cycles | No. of T Cycles | Comments | 
 |  | S | Z |  | H |  | P/V | N | C | 76 | 543 | 210 | Hex |  |  |  |  | 
ADD A,r | A ← A + r | ↕ | ↕ | X | ↕ | X | V | 0 | ↕ | 10 | 000 | r |  | 1 | 1 | 4 | r | Reg
ADD A,n | A ← A + n | ↕ | ↕ | X | ↕ | X | V | 0 | ↕ | 11 | 000 | 110 |  | 2 | 2 | 7 | 000 | B
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  | 001 | C
ADD A,(HL) | A ← A + (HL) | ↕ | ↕ | X | ↕ | X | V | 0 | ↕ | 10 | 000 | 110 |  | 1 | 2 | 7 | 010 | D
ADD A,(IX+d) | A ← A + (IX+d) | ↕ | ↕ | X | ↕ | X | V | 0 | ↕ | 11 | 011 | 101 | DD | 3 | 5 | 19 | 011 | E
 |  |  |  |  |  |  |  |  |  | 10 | 000 | 110 |  |  |  |  | 100 | H
 |  |  |  |  |  |  |  |  |  | ← | d | → |  |  |  |  | 101 | L
ADD A,(IY+d) | A ← A + (IY+d) | ↕ | ↕ | X | ↕ | X | V | 0 | ↕ | 11 | 111 | 101 | FD | 3 | 5 | 19 | 111 | A
 |  |  |  |  |  |  |  |  |  | 10 | 000 | 110 |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | d | → |  |  |  |  |  | 
ADC A,s | A ← A + s + CY | ↕ | ↕ | X | ↕ | X | V | 0 | ↕ |  | 001 |  |  |  |  |  | s is any of r, n, (HL), (IX+d), (IY+d) as shown for ADD instruction. The indicated bits replace the 000 in the ADD set above. | 
SUB A,s | A ← A - s | ↕ | ↕ | X | ↕ | X | V | 1 | ↕ |  | 010 |  |  |  |  |  |  | 
SBC A,s | A ← A - s - CY | ↕ | ↕ | X | ↕ | X | V | 1 | ↕ |  | 011 |  |  |  |  |  |  | 
AND s | A ← A ⋀ s | ↕ | ↕ | X | 1 | X | P | 0 | 0 |  | 100 |  |  |  |  |  |  | 
OR s | A ← A ⋁ s | ↕ | ↕ | X | 0 | X | P | 0 | 0 |  | 110 |  |  |  |  |  |  | 
XOR s | A ← A ⊕ s | ↕ | ↕ | X | 0 | X | P | 0 | 0 |  | 101 |  |  |  |  |  |  | 
CP s | A - s | ↕ | ↕ | X | ↕ | X | V | 1 | ↕ |  | 111 |  |  |  |  |  |  | 
EL54B, Sistemas para el Procesamiento de la Información
Notes: | The V symbol in the P/V flag column indicates that the P/V flag contains the overflow of the result of the operation. Similarly the P symbol indicates parity. V = 1 means overflow. V = 0 means not overflow. P = 1 means parity of the result is even. P = 0 means parity of the result is odd.
8-BIT ARITHMETIC AND LOGICAL GROUP

## Slide 8
Mnemonic | Symbolic Operation | Flags |  |  |  |  |  |  |  | OP-Code |  |  |  | No. of Bytes | No. of M Cycles | No. of T Cycles | Comments | 
 |  | S | Z |  | H |  | P/V | N | C | 76 | 543 | 210 | Hex |  |  |  |  | 
INC r | r ← r + 1 | ↕ | ↕ | X | ↕ | X | V | 0 | • | 00 | r | 100 |  | 1 | 1 | 4 | r | Reg
INC (HL) | (HL) ← (HL) + 1 | ↕ | ↕ | X | ↕ | X | V | 0 | • | 00 | 110 | 100 |  | 1 | 3 | 11 | 000 | B
INC (IX+d) | (IX+d) ← (IX+d) + 1 | ↕ | ↕ | X | ↕ | X | V | 0 | • | 11 | 011 | 101 | DD | 3 | 6 | 23 | 001 | C
 |  |  |  |  |  |  |  |  |  | 00 | 110 | 100 |  |  |  |  | 010 | D
 |  |  |  |  |  |  |  |  |  | ← | d | → |  |  |  |  | 011 | E
INC (IY+d) | (IY+d) ← (IY+d) + 1 | ↕ | ↕ | X | ↕ | X | V | 0 | • | 11 | 111 | 101 | FD | 3 | 6 | 23 | 100 | H
 |  |  |  |  |  |  |  |  |  | 00 | 110 | 100 |  |  |  |  | 101 | L
 |  |  |  |  |  |  |  |  |  | ← | d | → |  |  |  |  | 111 | A
DEC s | s ← s - 1 | ↕ | ↕ | X | ↕ | X | V | 1 | • |  |  | 101 |  |  |  |  | s is any of r, (HL), (IX+d), (IY+d) as shown for INC. Same format and states as INC. Replace 100 with 101 in OP code. | 
EL54B, Sistemas para el Procesamiento de la Información
Notes: | The V symbol in the P/V flag column indicates that the P/V flag contains the overflow of the result of the operation. Similarly the P symbol indicates parity. V = 1 means overflow. V = 0 means not overflow. P = 1 means parity of the result is even. P = 0 means parity of the result is odd.
8-BIT ARITHMETIC AND LOGICAL GROUP

## Slide 9
Mnemonic | Symbolic Operation | Flags |  |  |  |  |  |  |  | OP-Code |  |  |  | No. of Bytes | No. of M Cycles | No. of T Cycles | Comments | 
 |  | S | Z |  | H |  | P/V | N | C | 76 | 543 | 210 | Hex |  |  |  |  | 
ADD HL,ss | HL ← HL + ss | • | • | X | X | X | • | 0 | ↕ | 00 | ss1 | 001 |  | 1 | 3 | 11 | ss | Reg.
ADC HL,ss | HL ← HL + ss + CY | ↕ | ↕ | X | X | X | V | 0 | ↕ | 11 | 101 | 101 | ED | 2 | 4 | 15 | 00 | BC
 |  |  |  |  |  |  |  |  |  | 01 | ss1 | 010 |  |  |  |  | 01 | DE
SBC HL,ss | HL ← HL - ss - CY | ↕ | ↕ | X | X | X | V | 0 | ↕ | 11 | 101 | 101 | ED | 2 | 4 | 15 | 10 | HL
 |  |  |  |  |  |  |  |  |  | 01 | ss0 | 010 |  |  |  |  | 11 | SP
ADD IX,pp | IX ← IX + pp | • | • | X | X | X | • | 0 | ↕ | 11 | 011 | 101 | DD | 2 | 4 | 15 | pp | Reg.
 |  |  |  |  |  |  |  |  |  | 00 | pp1 | 001 |  |  |  |  | 00 | BC
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 01 | DE
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 10 | IX
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 11 | SP
ADD IY,rr | IY ← IY + pp | • | • | X | X | X | • | 0 | ↕ | 11 | 111 | 101 | FD | 2 | 4 | 15 | rr | Reg.
 |  |  |  |  |  |  |  |  |  | 00 | pp1 | 001 |  |  |  |  | 00 | BC
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 01 | DE
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 10 | IY
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 11 | SP
INC ss | ss ← ss + 1 | • | • | X | • | X | • | • | • | 00 | ss0 | 011 |  | 1 | 1 | 6 | ss as above | 
INC IX | IX ← IX + 1 | • | • | X | • | X | • | • | • | 11 | 011 | 101 | DD | 2 | 2 | 10 |  | 
 |  |  |  |  |  |  |  |  |  | 00 | 100 | 011 | 23 |  |  |  |  | 
INC IY | IY ← IY + 1 | • | • | X | • | X | • | • | • | 11 | 111 | 101 | FD | 2 | 2 | 10 |  | 
 |  |  |  |  |  |  |  |  |  | 00 | 100 | 011 | 23 |  |  |  |  | 
DEC ss | ss ← ss - 1 | • | • | X | • | X | • | • | • | 00 | ss1 | 011 |  | 1 | 1 | 6 | ss as above | 
DEC IX | IX ← IX + 1 | • | • | X | • | X | • | • | • | 11 | 011 | 101 | DD | 2 | 2 | 10 |  | 
 |  |  |  |  |  |  |  |  |  | 00 | 101 | 011 | 2B |  |  |  |  | 
DEC IY | IY ← IY + 1 | • | • | X | • | X | • | • | • | 11 | 111 | 101 | FD | 2 | 2 | 10 |  | 
 |  |  |  |  |  |  |  |  |  | 00 | 101 | 011 | 2B |  |  |  |  | 
EL54B, Sistemas para el Procesamiento de la Información
Notes: | ss is any of the register pairs BC, DE, HL, SP. pp is any of the register pairs BC, DE, IX, SP. rr is any of the register pairs BC, DE, IY, SP.
16-BIT ARITHMETIC GROUP

## Slide 10
Mnemonic | Symbolic Operation | Flags |  |  |  |  |  |  |  | OP-Code |  |  |  | No. of Bytes | No. of M Cycles | No. of T Cycles | Comments | 
 |  | S | Z |  | H |  | P/V | N | C | 76 | 543 | 210 | Hex |  |  |  |  | 
JP nn | PC ← nn | • | • | X | • | X | • | • | • | 11 | 000 | 011 | C3 | 3 | 3 | 10 |  | 
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  | cc | Condition
JP cc,nn | If condition cc | • | • | X | • | X | • | • | • | 11 | cc | 010 |  | 3 | 3 | 10 | 000 | NZ non zero
 | is true PC ← nn, |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  | 001 | Z zero
 | otherwise |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  | 010 | NC non carry
 | contiue |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 011 | C carry
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 100 | PO parity odd
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 101 | PE parity even
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 110 | P sign positive
JR e | PC ← PC + e | • | • | X | • | X | • | • | • | 00 | 011 | 000 | 18 | 2 | 3 | 12 | 111 | M sign negative
 |  |  |  |  |  |  |  |  |  | ← | e-2 | → |  |  |  |  |  | 
JR C,e | If C = 0, | • | • | X | • | X | • | • | • | 00 | 111 | 000 | 38 | 2 | 2 | 7 | If condition not met | 
 | continue |  |  |  |  |  |  |  |  | ← | e-2 | → |  |  |  |  |  | 
 | If C = 1, |  |  |  |  |  |  |  |  |  |  |  |  | 2 | 3 | 12 | If condition is met | 
 | PC ← PC + e |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
EL54B, Sistemas para el Procesamiento de la Información
Notes: | e represents the extension in the relative addressing mode. e is a signed two's complement number in the range <-126,129>. e-2 in the op-code provides an effective address of PC+e as PC is incremented by 2 prior to the addition of e.
JUMP GROUP

## Slide 11
Mnemonic | Symbolic Operation | Flags |  |  |  |  |  |  |  | OP-Code |  |  |  | No. of Bytes | No. of M Cycles | No. of T Cycles | Comments | 
 |  | S | Z |  | H |  | P/V | N | C | 76 | 543 | 210 | Hex |  |  |  |  | 
JR NC,e | If C = 1, | • | • | X | • | X | • | • | • | 00 | 110 | 000 | 30 | 2 | 2 | 7 | If condition not met | 
 | continue |  |  |  |  |  |  |  |  | ← | e-2 | → |  |  |  |  |  | 
 | If C = 0, |  |  |  |  |  |  |  |  |  |  |  |  | 2 | 3 | 12 | If condition is met | 
 | PC ← PC + e |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
JR Z,e | If Z = 0, | • | • | X | • | X | • | • | • | 00 | 101 | 000 | 28 | 2 | 2 | 7 | If condition not met | 
 | continue |  |  |  |  |  |  |  |  | ← | e-2 | → |  |  |  |  |  | 
 | If Z = 1, |  |  |  |  |  |  |  |  |  |  |  |  | 2 | 3 | 12 | If condition is met | 
 | PC ← PC + e |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
JR NZ,e | If Z = 1, | • | • | X | • | X | • | • | • | 00 | 100 | 000 | 20 | 2 | 2 | 7 | If condition not met | 
 | continue |  |  |  |  |  |  |  |  | ← | e-2 | → |  |  |  |  |  | 
 | If Z = 0, |  |  |  |  |  |  |  |  |  |  |  |  | 2 | 3 | 12 | If condition is met | 
 | PC ← PC + e |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
JP (HL) | PC ← HL | • | • | X | • | X | • | • | • | 11 | 101 | 001 | E9 | 1 | 1 | 4 |  | 
JP (IX) | PC ← IX | • | • | X | • | X | • | • | • | 11 | 011 | 101 | DD | 2 | 2 | 8 |  | 
 |  |  |  |  |  |  |  |  |  | 11 | 101 | 001 | E9 |  |  |  |  | 
JP (IY) | PC ← IY | • | • | X | • | X | • | • | • | 11 | 111 | 101 | FD | 2 | 2 | 8 |  | 
 |  |  |  |  |  |  |  |  |  | 11 | 101 | 001 | E9 |  |  |  |  | 
DJNZ e | B ← B - 1 | • | • | X | • | X | • | • | • | 00 | 010 | 000 | 10 | 2 | 2 | 8 | If B = 0 | 
 | If B = 0, |  |  |  |  |  |  |  |  | ← | e-2 | → |  |  |  |  |  | 
 | continue |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | If B ≠ 0, |  |  |  |  |  |  |  |  |  |  |  |  | 2 | 3 | 13 | If B ≠ 0 | 
 | PC ← PC + e |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
EL54B, Sistemas para el Procesamiento de la Información
Notes: | e represents the extension in the relative addressing mode. e is a signed two's complement number in the range <-126,129>. e-2 in the op-code provides an effective address of PC+e as PC is incremented by 2 prior to the addition of e.
JUMP GROUP