## Slide 1
EL54B, Sistemas para el Procesamiento de la Información
GENERAL PURPOSE ARITHMETIC AND CPU CONTROL GROUPS
Mnemonic | Symbolic Operation | Flags |  |  |  |  |  |  |  | OP-Code |  |  |  | No. of Bytes | No. of M Cycles | No. of T Cycles | Comments
 |  | S | Z |  | H |  | P/V | N | C | 76 | 543 | 210 | Hex |  |  |  | 
DAA | Converts acc. | ↕ | ↕ | X | ↕ | X | P | • | ↕ | 00 | 100 | 111 | 27 | 1 | 1 | 4 | Decimal adjust
 | content into |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | accumulator
 | packed BCD |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | following add |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | or subtract |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | with packed |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | BCD operands |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CPL | A ← Ā | • | • | X | 1 | X | • | 1 | • | 00 | 101 | 111 | 2F | 1 | 1 | 4 | Complement
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | accumulator
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | (one's complement)
NEG | A ← Ā + 1 | ↕ | ↕ | X | ↕ | X | V | 1 | ↕ | 11 | 101 | 101 | ED | 2 | 2 | 8 | Negate acc. ( two's
 |  |  |  |  |  |  |  |  |  | 01 | 000 | 100 | 44 |  |  |  | complement )
CCF | CY ← | • | • | X | X | X | • | 0 | ↕ | 00 | 111 | 111 | 3F | 1 | 1 | 4 | Complement
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | carry flag
SCF | CY ← 1 | • | • | X | 0 | X | • | 0 | 1 | 00 | 110 | 111 | 37 | 1 | 1 | 4 | Set carry flag
NOP | No operation | • | • | X | • | X | • | • | • | 00 | 000 | 000 | 00 | 1 | 1 | 4 | 
HALT | CPU halted | • | • | X | • | X | • | • | • | 01 | 110 | 110 | 76 | 1 | 1 | 4 | 
DI | IFF ← 0 | • | • | X | • | X | • | • | • | 11 | 110 | 011 | F3 | 1 | 1 | 4 | 
EI | IFF ← 1 | • | • | X | • | X | • | • | • | 11 | 111 | 011 | FB | 1 | 1 | 4 | 
IM0 | Set interrupt | • | • | X | • | X | • | • | • | 11 | 101 | 101 | ED | 2 | 2 | 8 | 
 | mode 0 |  |  |  |  |  |  |  |  | 01 | 000 | 110 | 46 |  |  |  | 
IM1 | Set interrupt | • | • | X | • | X | • | • | • | 11 | 101 | 101 | ED | 2 | 2 | 8 | 
 | mode 1 |  |  |  |  |  |  |  |  | 01 | 010 | 110 | 56 |  |  |  | 
IM2 | Set interrupt | • | • | X | • | X | • | • | • | 11 | 101 | 101 | ED | 2 | 2 | 8 | 
 | mode 2 |  |  |  |  |  |  |  |  | 01 | 011 | 110 | 5E |  |  |  | 
Notes: | IFF indicates the interrupt enable flip-flop.
 | CY indicates the carry flip-flop.
 | Interrupts are not sampled at the end of EI or DI
● = Flag not affected, 0 = Flag reset 1 = Flag set, X = Flag is unknown ↕ = Flag affected according operation result IFF = Interrupt enable Flip-Flop content copied in P/V

## Slide 2
Mnemonic | Symbolic Operation | Flags |  |  |  |  |  |  |  | OP-Code |  |  |  | No. of Bytes | No. of M Cycles | No. of T Cycles | Comments
 |  | S | Z |  | H |  | P/V | N | C | 76 | 543 | 210 | Hex |  |  |  | 
EX DE,HL | DE ↔ HL | • | • | X | • | X | • | • | • | 11 | 101 | 011 | EB | 1 | 1 | 4 | 
EX AF,AF' | AF ↔ AF' | • | • | X | • | X | • | • | • | 00 | 001 | 000 | 8 | 1 | 1 | 4 | 
EXX | BC ↔ BC' | • | • | X | • | X | • | • | • | 11 | 011 | 001 | D9 | 1 | 1 | 4 | Register bank and
 | DE ↔ DE' |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | auxiliary register
 | HL ↔ HL' |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | bank exchange
EX (SP),HL | H ↔ (SP+1) | • | • | X | • | X | • | • | • | 11 | 100 | 011 | E3 | 1 | 5 | 19 | 
 | L ↔ (SP) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
EX (SP),IX | IXH ↔ (SP+1) | • | • | X | • | X | • | • | • | 11 | 011 | 101 | DD | 2 | 6 | 23 | 
 | IXL ↔ (SP) |  |  |  |  |  |  |  |  | 11 | 100 | 011 | E3 |  |  |  | 
EX (SP),IY | IYH ↔ (SP+1) | • | • | X | • | X | • | • | • | 11 | 111 | 101 | FD | 2 | 6 | 23 | 
 | IYL ↔ (SP) |  |  |  |  |  |  |  |  | 11 | 100 | 011 | E3 |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
LDI | (DE) ← (HL) | • | • | X | 0 | X | ↕ | 0 | • | 11 | 101 | 101 | ED | 2 | 4 | 16 | Load (HL) into (DE),
 | DE ← DE + 1 |  |  |  |  |  |  |  |  | 10 | 100 | 000 | A0 |  |  |  | increment the pointers and
 | HL ← HL + 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | decrement the byte
 | BC ← BC - 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | counter (BC)
LDIR | (DE) ← (HL) | • | • | X | 0 | X | 0 | 0 | • | 11 | 101 | 101 | ED | 2 | 5 | 21 | If BC ≠ 0
 | DE ← DE + 1 |  |  |  |  |  |  |  |  | 10 | 110 | 000 | B0 | 2 | 4 | 16 | If BC = 0
 | HL ← HL + 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | BC ← BC - 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Repeat until |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | BC = 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
LDD | (DE) ← (HL) | • | • | X | 0 | X | ↕ | 0 | • | 11 | 101 | 101 | ED | 2 | 4 | 16 | 
 | DE ← DE - 1 |  |  |  |  |  |  |  |  | 10 | 101 | 000 | A8 |  |  |  | 
 | HL ← HL - 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | BC ← BC - 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
EL54B, Sistemas para el Procesamiento de la Información
Notes: |  P/V flag is 0 if the result of BC-1 = 0, otherwise P/V =1  Z flag is 1 if A = (HL), otherwise Z = 0
EXCHANGE GROUP AND BLOCK TRANSFER AND SEARCH GROUP

## Slide 3
Mnemonic | Symbolic Operation | Flags |  |  |  |  |  |  |  | OP-Code |  |  |  | No. of Bytes | No. of M Cycles | No. of T Cycles | Comments
 |  | S | Z |  | H |  | P/V | N | C | 76 | 543 | 210 | Hex |  |  |  | 
LDDR | (DE) ← (HL) | • | • | X | 0 | X | 0 | 0 | • | 11 | 101 | 101 | ED | 2 | 5 | 21 | If BC ≠ 0
 | DE ← DE - 1 |  |  |  |  |  |  |  |  | 10 | 111 | 000 | B8 | 2 | 4 | 16 | If BC = 0
 | HL ← HL - 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | BC ← BC - 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Repeat until |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | BC = 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CPI | A - (HL) | ↕ | ↕ | X | ↕ | X | ↕ | 1 | • | 11 | 101 | 101 | ED | 2 | 4 | 16 | 
 | HL ← HL + 1 |  |  |  |  |  |  |  |  | 10 | 100 | 001 | A1 |  |  |  | 
 | BC ← BC - 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CPIR | A - (HL) | ↕ | ↕ | X | ↕ | X | ↕ | 1 | • | 11 | 101 | 101 | ED | 2 | 5 | 21 | If BC ≠ 0 and A ≠ (HL)
 | HL ← HL + 1 |  |  |  |  |  |  |  |  | 10 | 110 | 001 | B1 | 2 | 4 | 16 | If BC = 0 or A = (HL)
 | BC ← BC - 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Repeat until |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | A = (HL) or |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | BC = 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CPD | A - (HL) | ↕ | ↕ | X | ↕ | X | ↕ | 1 | • | 11 | 101 | 101 | ED | 2 | 4 | 16 | 
 | HL ← HL - 1 |  |  |  |  |  |  |  |  | 10 | 101 | 001 | A9 |  |  |  | 
 | BC ← BC - 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CPDR | (DE) ← (HL) | ↕ | ↕ | X | ↕ | X | ↕ | 1 | • | 11 | 101 | 101 | ED | 2 | 5 | 21 | If BC ≠ 0 and A ≠ (HL)
 | HL ← HL - 1 |  |  |  |  |  |  |  |  | 10 | 111 | 001 | B9 | 2 | 4 | 16 | If BC = 0 or A = (HL)
 | BC ← BC - 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Repeat until |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | A = (HL) or |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | BC = 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
EL54B, Sistemas para el Procesamiento de la Información
Notes: |  P/V flag is 0 if the result of BC-1 = 0, otherwise P/V =1  Z flag is 1 if A = (HL), otherwise Z = 0
EXCHANGE GROUP AND BLOCK TRANSFER AND SEARCH GROUP

## Slide 4
Mnemonic | Symbolic Operation | Flags |  |  |  |  |  |  |  | OP-Code |  |  |  | No. of Bytes | No. of M Cycles | No. of T Cycles | Comments |  |  |  | 
 |  | S | Z |  | H |  | P/V | N | C | 76 | 543 | 210 | Hex |  |  |  |  |  |  |  | 
CALL nn | (SP-1) ← PCH | ● | ● | X | ● | X | ● | ● | ● | 11 | 001 | 101 | CD | 3 | 5 | 17 |  |  |  |  | 
 | (SP-2) ← PCL |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  |  |  |  |  | 
 | SP ← SP - 2 |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  |  |  |  |  | 
 | PC ← nn |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CALL cc,nn | If condition cc is | ● | ● | X | ● | X | ● | ● | ● | 11 | cc | 100 |  | 3 | 3 | 10 | If cc is false |  |  |  | 
 | false continue, |  |  |  |  |  |  |  |  | ← | n | → |  | 3 | 5 | 17 | If cc is true |  |  |  | 
 | otherwise same |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  |  |  |  |  | 
 | as CALL nn |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | cc | Condition |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 000 | NZ non zero |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 001 | Z zero |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 010 | NC non carry |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 011 | C carry |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 100 | PO parity odd |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 101 | PE parity even |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 110 | P sign positive |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 111 | M sign negative |  |  | 
RET | PCL ← (SP) | ● | ● | X | ● | X | ● | ● | ● | 11 | 001 | 001 | C9 | 1 | 3 | 10 |  |  |  |  | 
 | PCH ← (SP+1) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | SP ← SP + 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
RET cc,nn | If condition cc is | ● | ● | X | ● | X | ● | ● | ● | 11 | cc | 000 |  | 1 | 1 | 5 | If cc is false |  |  |  | 
 | false continue, |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 3 | 11 | If cc is true |  |  |  | 
 | otherwise same |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | as RET |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | cc same as for |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | CALL cc,nn |  |  |  | 
EL54B, Sistemas para el Procesamiento de la Información
CALL AND RETURN GROUP

## Slide 5
Mnemonic | Symbolic Operation | Flags |  |  |  |  |  |  |  | OP-Code |  |  |  | No. of Bytes | No. of M Cycles | No. of T Cycles | Comments |  |  |  |  |  | 
 |  | S | Z |  | H |  | P/V | N | C | 76 | 543 | 210 | Hex |  |  |  |  |  |  |  |  |  | 
RETI | Return from | ● | ● | X | ● | X | ● | ● | ● | 11 | 101 | 101 | ED | 2 | 4 | 14 | Same as RET |  |  |  |  |  | 
 | interrupt. |  |  |  |  |  |  |  |  | 01 | 001 | 101 | 4D |  |  |  | except detected by |  |  |  |  |  | 
 | PCL ← (SP) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | interrupting device |  |  |  |  |  | 
 | PCH ← (SP+1) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | to re-enable interrupts. |  |  |  |  |  | 
 | SP ← SP + 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
RETN | Return from | ● | ● | X | ● | X | ● | ● | ● | 11 | 101 | 101 | ED | 2 | 4 | 14 | Same as RET |  |  |  |  |  | 
 | non maskable |  |  |  |  |  |  |  |  | 01 | 000 | 101 | 45 |  |  |  | except detected by |  |  |  |  |  | 
 | interrupt. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | interrupting device |  |  |  |  |  | 
 | PCL ← (SP) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | to re-enable interrupts. |  |  |  |  |  | 
 | PCH ← (SP+1) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | SP ← SP + 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
RST p | (SP-1) ← PCH | ● | ● | X | ● | X | ● | ● | ● | 11 | t | 111 |  | 1 | 3 | 11 |  | t |  | P |  |  | 
 | (SP-2) ← PCL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 000 |  | 00H |  |  | 
 | PCH ← 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 001 |  | 08H |  |  | 
 | PCL ← P |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 010 |  | 10H |  |  | 
 | SP ← SP - 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 011 |  | 18H |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 100 |  | 20H |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 101 |  | 28H |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 110 |  | 30H |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 111 |  | 38H |  |  | 
EL54B, Sistemas para el Procesamiento de la Información
Notes | RETN loads IFF2 - IFF1
CALL AND RETURN GROUP

## Slide 6
Mnemonic | Symbolic Operation | Flags |  |  |  |  |  |  |  | OP-Code |  |  |  | No. of Bytes | No. of M Cycles | No. of T Cycles | Comments | 
 |  | S | Z |  | H |  | P/V | N | C | 76 | 543 | 210 | Hex |  |  |  |  | 
IN A,(n) | A ← (n) | • | • | X | • | X | • | • | • | 11 | 011 | 011 | DB | 2 | 3 | 11 | n to A0 ~ A7 | 
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  | Acc to A8 ~ A15 | 
IN r,(C) | r ← (C) | ↕ | ↕ | X | ↕ | X | P | 0 | • | 11 | 101 | 101 | ED | 2 | 3 | 12 | C to A0 ~ A7 | 
 |  |  |  |  |  |  |  |  |  | 01 | r | 000 |  |  |  |  | B to A8 ~ A15 | 
 | If r = 110 only |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | the flags will |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | r , s | Reg.
 | be affected. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 000 | B
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 001 | C
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 010 | D
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 011 | E
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 100 | H
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 101 | L
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 111 | A
INI | (HL) ← (C) | X | ↕ | X | X | X | X | 1 | X | 11 | 101 | 101 | ED | 2 | 4 | 16 | C to A0 ~ A7 | 
 | B ← B - 1 |  |  |  |  |  |  |  |  | 10 | 100 | 010 | A2 |  |  |  | B to A8 ~ A15 | 
 | HL ← HL + 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
INIR | (HL) ← (C) | X | 1 | X | X | X | X | 1 | X | 11 | 101 | 101 | ED | 2 | 5 | 21 | C to A0 ~ A7 | 
 | B ← B - 1 |  |  |  |  |  |  |  |  | 10 | 110 | 010 | B2 |  | (If B ≠ 0) |  | B to A8 ~ A15 | 
 | HL ← HL + 1 |  |  |  |  |  |  |  |  |  |  |  |  | 2 | 4 | 16 |  | 
 | Repeat until |  |  |  |  |  |  |  |  |  |  |  |  |  | (If B = 0) |  |  | 
 | B = 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
IND | (HL) ← (C) | X | ↕ | X | X | X | X | 1 | X | 11 | 101 | 101 | ED | 2 | 4 | 16 | C to A0 ~ A7 | 
 | B ← B - 1 |  |  |  |  |  |  |  |  | 10 | 101 | 010 | AA |  |  |  | B to A8 ~ A15 | 
 | HL ← HL - 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
EL54B, Sistemas para el Procesamiento de la Información
Notes: |  If the result of B - 1 is zero the Z flag is set, otherwise it is reset.
INPUT AND OUTPUT GROUP

## Slide 7
Mnemonic | Symbolic Operation | Flags |  |  |  |  |  |  |  | OP-Code |  |  |  | No. of Bytes | No. of M Cycles | No. of T Cycles | Comments | 
 |  | S | Z |  | H |  | P/V | N | C | 76 | 543 | 210 | Hex |  |  |  |  | 
INDR | (HL) ← (C) | X | 1 | X | X | X | X | 1 | X | 11 | 101 | 101 | ED | 2 | 5 | 21 | C to A0 ~ A7 | 
 | B ← B - 1 |  |  |  |  |  |  |  |  | 10 | 111 | 010 | BA |  | (If B ≠ 0) |  | B to A8 ~ A15 | 
 | HL ← HL - 1 |  |  |  |  |  |  |  |  |  |  |  |  | 2 | 4 | 16 |  | 
 | Repeat until |  |  |  |  |  |  |  |  |  |  |  |  |  | (If B = 0) |  |  | 
 | B = 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
OUT (n),A | (n) ← A | • | • | X | • | X | • | • | • | 11 | 010 | 011 | D3 | 2 | 3 | 11 | n to A0 ~ A7 | 
 |  |  |  |  |  |  |  |  |  | ← | n | → |  |  |  |  | Acc to A8 ~ A15 | 
OUT (C),r | (C) ← r | • | • | X | • | X | • | • | • | 11 | 101 | 101 | ED | 2 | 3 | 12 | C to A0 ~ A7 | 
 | r as for |  |  |  |  |  |  |  |  | 01 | r | 001 |  |  |  |  | B to A8 ~ A15 | 
 | IN r,(C) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | except |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | not r = 110 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
OUTI | (C) ← (HL) | X | ↕ | X | X | X | X | 1 | X | 11 | 101 | 101 | ED | 2 | 4 | 16 | C to A0 ~ A7 | 
 | B ← B - 1 |  |  |  |  |  |  |  |  | 10 | 100 | 011 | A3 |  |  |  | B to A8 ~ A15 | 
 | HL ← HL + 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
OTIR | (C) ← (HL) | X | 1 | X | X | X | X | 1 | X | 11 | 101 | 101 | ED | 2 | 5 | 21 | C to A0 ~ A7 | 
 | B ← B - 1 |  |  |  |  |  |  |  |  | 10 | 110 | 011 | B3 |  | (If B ≠ 0) |  | B to A8 ~ A15 | 
 | HL ← HL + 1 |  |  |  |  |  |  |  |  |  |  |  |  | 2 | 4 | 16 |  | 
 | Repeat until |  |  |  |  |  |  |  |  |  |  |  |  |  | (If B = 0) |  |  | 
 | B = 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
OUTD | (C) ← (HL) | X | ↕ | X | X | X | X | 1 | X | 11 | 101 | 101 | ED | 2 | 4 | 16 | C to A0 ~ A7 | 
 | B ← B - 1 |  |  |  |  |  |  |  |  | 10 | 101 | 011 | AB |  |  |  | B to A8 ~ A15 | 
 | HL ← HL - 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
OTDR | (C) ← (HL) | X | 1 | X | X | X | X | 1 | X | 11 | 101 | 101 | ED | 2 | 5 | 21 | C to A0 ~ A7 | 
 | B ← B - 1 |  |  |  |  |  |  |  |  | 10 | 111 | 011 | BB |  | (If B ≠ 0) |  | B to A8 ~ A15 | 
 | HL ← HL - 1 |  |  |  |  |  |  |  |  |  |  |  |  | 2 | 4 | 16 |  | 
 | Repeat until |  |  |  |  |  |  |  |  |  |  |  |  |  | (If B = 0) |  |  | 
 | B = 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
EL54B, Sistemas para el Procesamiento de la Información
INPUT AND OUTPUT GROUP

## Slide 8
Mnemonic | Symbolic Operation | Flags |  |  |  |  |  |  |  | OP-Code |  |  |  | No. of Bytes | No. of M Cycles | No. of T Cycles | Comments | 
 |  | S | Z |  | H |  | P/V | N | C | 76 | 543 | 210 | Hex |  |  |  |  | 
BIT b,r | Z ← | X | ↕ | X | 1 | X | X | 0 | • | 11 | 001 | 011 | CB | 2 | 2 | 8 | r | Reg
 |  |  |  |  |  |  |  |  |  | 01 | b | r |  |  |  |  | 000 | B
BIT b,(HL) | Z ← | X | ↕ | X | 1 | X | X | 0 | • | 11 | 001 | 011 | CB | 2 | 3 | 12 | 001 | C
 |  |  |  |  |  |  |  |  |  | 01 | b | 110 |  |  |  |  | 010 | D
BIT b,(IX+d) | Z ← | X | ↕ | X | 1 | X | X | 0 | • | 11 | 011 | 101 | DD | 4 | 5 | 20 | 011 | E
 |  |  |  |  |  |  |  |  |  | 11 | 001 | 011 | CB |  |  |  | 100 | H
 |  |  |  |  |  |  |  |  |  | ← | d | → |  |  |  |  | 101 | L
 |  |  |  |  |  |  |  |  |  | 01 | b | 110 |  |  |  |  | 111 | A
BIT b,(IY+d) | Z ← | X | ↕ | X | 1 | X | X | 0 | • | 11 | 111 | 101 | FD | 4 | 5 | 20 |  | 
 |  |  |  |  |  |  |  |  |  | 11 | 001 | 011 | CB |  |  |  | b | Bit Tested
 |  |  |  |  |  |  |  |  |  | ← | d | → |  |  |  |  | 000 | 0
 |  |  |  |  |  |  |  |  |  | 01 | b | 110 |  |  |  |  | 001 | 1
SET b,r | rb ← 1 | • | • | X | • | X | • | • | • | 11 | 001 | 011 | CB | 2 | 2 | 8 | 010 | 2
 |  |  |  |  |  |  |  |  |  | 11 | b | r |  |  |  |  | 011 | 3
SET b,(HL) | (HL)b ← 1 | • | • | X | • | X | • | • | • | 11 | 001 | 011 | CB | 2 | 3 | 12 | 100 | 4
 |  |  |  |  |  |  |  |  |  | 11 | b | 110 |  |  |  |  | 101 | 5
SET b,(IX+d) | (IX+d)b ← 1 | • | • | X | • | X | • | • | • | 11 | 011 | 101 | DD | 4 | 5 | 20 | 110 | 6
 |  |  |  |  |  |  |  |  |  | 11 | 001 | 011 | CB |  |  |  | 111 | 7
 |  |  |  |  |  |  |  |  |  | ← | d | → |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | 11 | b | 110 |  |  |  |  |  | 
SET b,(IY+d) | (IY+d)b ← 1 | • | • | X | • | X | • | • | • | 11 | 111 | 101 | FD | 4 | 5 | 20 |  | 
 |  |  |  |  |  |  |  |  |  | 11 | 001 | 011 | CB |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | ← | d | → |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | 11 | b | 110 |  |  |  |  |  | 
RES b,s | sb ← 0 | • | • | X | • | X | • | • | • | 10 |  |  |  |  |  |  | To form new OP- | 
 | s ≡ r, (HL), |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | code replace 11 | 
 | (IX+d), |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | of SET b,s with | 
 | (IY+d) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 10. Flags and | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | time states same | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | as for SET | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | instruction. | 
EL54B, Sistemas para el Procesamiento de la Información
Notes: | The notation sb indicates bit b (0 to 7) of location s.
BIT SET, RESET AND TEST GROUP

## Slide 9
Mnemonic | Symbolic Operation | Flags |  |  |  |  |  |  |  | OP-Code |  |  |  | No. of Bytes | No. of M Cycles | No. of T Cycles | Comments | 
 |  | S | Z |  | H |  | P/V | N | C | 76 | 543 | 210 | Hex |  |  |  |  | 
RLCA |  | • | • | X | 0 | X | • | 0 | ↕ | 00 | 000 | 111 | 07 | 1 | 1 | 4 | Rotate left circular | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | accumulator | 
RLA |  | • | • | X | 0 | X | • | 0 | ↕ | 00 | 010 | 111 | 17 | 1 | 1 | 4 | Rotate left | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | accumulator | 
RRCA |  | • | • | X | 0 | X | • | 0 | ↕ | 00 | 001 | 111 | DF | 1 | 1 | 4 | Rotate right circular | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | accumulator | 
RRA |  | • | • | X | 0 | X | • | 0 | ↕ | 00 | 011 | 111 | 1F | 1 | 1 | 4 | Rotate right | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | accumulator | 
RLC r |  | ↕ | ↕ | X | 0 | X | P | 0 | ↕ | 11 | 001 | 011 | CB | 2 | 2 | 8 | Rotate left circular | 
 |  |  |  |  |  |  |  |  |  | 00 | 000 | r |  |  |  |  | register r | 
RLC (HL) |  | ↕ | ↕ | X | 0 | X | P | 0 | ↕ | 11 | 001 | 011 | CB | 2 | 4 | 15 |  | 
 |  |  |  |  |  |  |  |  |  | 00 | 000 | 110 |  |  |  |  | r | Reg
RLC (IX+d) |  | ↕ | ↕ | X | 0 | X | P | 0 | ↕ | 11 | 011 | 101 | DD | 4 | 6 | 23 | 000 | B
 | r,(HL),(IX+d),(IY+d) |  |  |  |  |  |  |  |  | 11 | 001 | 011 | CB |  |  |  | 001 | C
 |  |  |  |  |  |  |  |  |  | ← | d | → |  |  |  |  | 010 | D
 |  |  |  |  |  |  |  |  |  | 00 | 000 | 110 |  |  |  |  | 011 | E
RLC (IY+d) |  | ↕ | ↕ | X | 0 | X | P | 0 | ↕ | 11 | 111 | 101 | FD | 4 | 6 | 23 | 100 | H
 |  |  |  |  |  |  |  |  |  | 11 | 001 | 011 | CB |  |  |  | 101 | L
 |  |  |  |  |  |  |  |  |  | ← | d | → |  |  |  |  | 111 | A
 |  |  |  |  |  |  |  |  |  | 00 | 000 | 110 |  |  |  |  |  | 
RL s |  | ↕ | ↕ | X | 0 | X | P | 0 | ↕ |  | 010 |  |  |  |  |  | Instruction format | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | and states are as | 
 | s ≡ r,(HL),(IX+d),(IY+d) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | shown for RLC's. | 
EL54B, Sistemas para el Procesamiento de la Información
ROTATE AND SHIFT GROUP

## Slide 10
Mnemonic | Symbolic Operation | Flags |  |  |  |  |  |  |  | OP-Code |  |  |  | No. of Bytes | No. of M Cycles | No. of T Cycles | Comments | 
 |  | S | Z |  | H |  | P/V | N | C | 76 | 543 | 210 | Hex |  |  |  |  | 
RRC s |  | ↕ | ↕ | X | 0 | X | P | 0 | ↕ |  | 001 |  |  |  |  |  | To form new | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | OP-code, replace | 
 | s ≡ r,(HL),(IX+d),(IY+d) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 000 of RLC's with | 
RR s |  | ↕ | ↕ | X | 0 | X | P | 0 | ↕ |  | 011 |  |  |  |  |  | shown code. | 
 | s ≡ r,(HL),(IX+d),(IY+d) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SLA s |  | ↕ | ↕ | X | 0 | X | P | 0 | ↕ |  | 100 |  |  |  |  |  |  | 
 | s ≡ r,(HL),(IX+d),(IY+d) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SRA s |  | ↕ | ↕ | X | 0 | X | P | 0 | ↕ |  | 101 |  |  |  |  |  |  | 
 | s ≡ r,(HL),(IX+d),(IY+d) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SRL s |  | ↕ | ↕ | X | 0 | X | P | 0 | ↕ |  | 111 |  |  |  |  |  |  | 
 | s ≡ r,(HL),(IX+d),(IY+d) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
RLD |  | ↕ | ↕ | X | 0 | X | P | 0 | • | 11 | 101 | 101 | ED | 2 | 5 | 18 | Rotate digit left | 
 |  |  |  |  |  |  |  |  |  | 01 | 101 | 111 | 6F |  |  |  | and right between | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | the accumulator | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | and location (HL). | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | The content of the | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | upper half of the | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | accumulator is | 
RRD |  | ↕ | ↕ | X | 0 | X | P | 0 | • | 11 | 101 | 101 | ED | 2 | 5 | 18 | unaffected. | 
 |  |  |  |  |  |  |  |  |  | 01 | 100 | 111 | 67 |  |  |  |  | 
EL54B, Sistemas para el Procesamiento de la Información
ROTATE AND SHIFT GROUP