## Slide 1: EL 653
Architectural Level Synthesis and Optimization
Extracted from “Synthesis and Optimization of Digital Circuits”, Giovanni de Micheli,
McGraw-Hill, 1994

## Slide 2: Introduction
Architectural synthesis means constructing the macroscopic structure of a digital circuit, starting from behavioral models that can be captured by data-flow or sequencing graphs
The outcome is
  Structural view of the circuit (data path)
  Logic level specification of the control unit
Data path is an interconnection of
  resources to implement arithmetic or logic functions
  steering logic circuits (e.g. multiplexers and buses) to send data to the appropriate destination at the appropriate time
  register or memory to store data

## Slide 3: Evaluation of Implemented Circuits
Area
Cycle time (clock period)
Latency (the number of cycles to perform all operations)
Throughput (computation rate) for pipelined circuits

## Slide 4: Circuit Specification
Behavioral-level circuit models
Resources
Constraints

## Slide 5: Resources
Functional resources process data – implement arithmetic and logic functions
  Primitive resources – designed carefully once and often used (e.g. encoders, decoders). Stored in libraries and fully characterized
  Application-specific resources – solves a particular task
Memory resources store data (e.g. registers, read-only memory, read-write memory)
Interface resources support data transfer (e.g. busses, I/O pads)

## Slide 6: Constraints
Interface constraints
  Additional specifications to ensure that the circuit can be embedded in a given environment
  Relate to the format and timing of the I/O data transfers
Implementation constraints
  Reflect the desire of the designer to achieve a structure with some properties

## Slide 7: The Fundamental Architectural Synthesis Problems
We assume that a circuit is specified by
  A sequencing graph
  A set of functional resources (fully characterized)
  A set of constraints
We assume that storage is implemented by registers and interconnections by wires
Architectural synthesis consists of two stages
  Placing the operations in time and space (time interval for execution and bind to resources)
  Detailed interconnection of the data path and the logic level specification of the control unit

## Slide 8: The Temporal Domain: Scheduling
We denote the execution delays of the operations by the set
Start time of an operation is defined as the time at which the operation starts its execution
Start time of operations, represented by the set are attributes of the vertices of the sequencing graph
Scheduling is the task of determining the start times, subject to the precedence constraints specified by the sequencing graph

## Slide 9: The temporal Domain: Scheduling
Latency of a scheduled sequencing graph is denoted by , it is the difference between the start time of the sink and the start time of the source,
A schedule of a sequencing graph is a function , where denotes the operation start time such that
A scheduled sequencing graph is a vertex-weighted, where each vertex is labeled by its start time

## Slide 10: Sequencing Graph
Operation | Start time
 | 1
 | 2
 | 3
 | 4
Operations assumed to have unit execution delay

## Slide 11: Scheduled Sequencing Graph
Latency

## Slide 12
One resource per type
Operation |  | Start time
Multiply | ALU | 
 |  | 1
 |  | 2
 |  | 3
 |  | 4
 |  | 5
 |  | 6
 |  | 7

## Slide 13: Exercise
Consider the graph in previous slides with the following conditions
  Multiplication propagation delay: 35 nsec
  Other operations propagation delay: 25 nsec
  Cycle time: 50 nsec
Make the corresponding scheduled sequencing graph

## Slide 14: The Spatial Domain: Binding
The type of an operation is the type of computation it performs
  arithmetic (addition, multiplication)
  application-specific operation (Boolean function evaluation)
The notion of type is extended to resources
A resource type can implement more than one operation type
Resource-type set is the set of resources types

## Slide 15: The Spatial Domain: Binding
Assuming resources types, the resource types set is denoted by
The function denotes the resource type that can implement an operation
No-operations do not require any binding to any resource
Resource sharing is applied when there are more than one operation with the same type

## Slide 16: The Spatial Domain: Binding
Resource binding is a mapping where denotes that the operation corresponding to , with type , is implemented by the rth instance of the resource type for each
A simple case of binding is a dedicated resource. Each operation is bound to one resource, and the resource binding is a one-to-one function

## Slide 17: Sequencing Graph
 | (1,1)
 | (1,2)
 | (1,3)
 | (2,1)
 | (2,2)
 | (1,4)
 | (1,5)
There are 11 operations
Assuming that 11 resources are available
Resources type are {multiplier, ALU}
Multiplier is type 1, ALU is type 2
6 instances of multiplier and five instances of the ALU are needed
 | (1,6)
 | (2,3)
 | (2,4)
 | (2,5)

## Slide 18
 | (1,1)
 | (1,2)
 | (1,2)
 | (2,1)
 | (2,1)
 | (1,3)
 | (1,3)
 | (1,4)
 | (2,1)
 | (2,2)
 | (2,2)
Multiplier is type 1, ALU is type 2
4 instances of multiplier and 2 instances of the ALU are needed
(1,1)
(1,2)
(1,3)
(1, 4)
(2,2)
(2,1)

## Slide 19: Area and Performance Estimation
Accurate area and delay estimation is not a simple task
Architectural synthesis and optimization require estimating area and performance variations as a result of architectural-level decisions
Schedule provides latency, binding provides area
It is important to forecast the impact of scheduling and binding decisions on area and performance
Two types of circuits
  Resource-dominated
  General

## Slide 20: Resource-Dominated Circuits
Area and delay of resources are known
Parameters of other components can be neglected or considered a fixed overhead
Estimated area of a structure is the sum of the areas of the bound resource instances
For a given cycle time, the execution delay of the operations can be derived
Latency of a circuit can be determined by its schedule

## Slide 21: Example
Circuit considered as resource dominated
Area of the multiplier is 5 units, and its propagation is 35 nsec
Area of the ALU is 1 unit, and its propagation is 25 nsec
Overhead is 1 unit
Cycle time is 40 nsec, and then all operations require one cycle to execute
Implementation with dedicated resources requires 6*5 + 5*1 +1=36 and latency is 4 cycles
An implementation with one resource of each type requires 5+1+1=7. Latency is 7 cycles

## Slide 22: General Circuits
Estimated area is the sum of the areas of the bound resources instances plus the area of the steering logic, registers (or memories), control unit, and wiring area
Latency depends on the schedule, which must take into account the propagation delay on paths between register boundaries
Data path components
  Registers
  Steering logic
  Wiring
Control unit

## Slide 23: Registers
All data transferred from a resource to another across a cycle boundary must be stored into a register
Register usage can be derived by examining a scheduled sequencing graph. Number of registers can be minimized
Accurate estimation of the number of registers requires scheduling and binding
The set up and propagation delay times of registers must be added to the propagation delay of the combinational logic to evaluate the evaluate their effect on cycle time

## Slide 24: Steering Logic
Affects the area and propagation delay
Area of multiplexers is known, however to know the number of required multiplexers, we need the binding
Multiplexers add propagation delay
Two considerations are necessary for busses area and delay estimation
  Busses can be considered as a fixed overhead
  Bus drivers and receivers can be considered as distributed multiplexers

## Slide 25: Wiring
Wiring contributes to the overall area and delay
Wiring area overhead is estimated from the structure (binding is known) by using models that are appropriate for the physical design style of the implementation
Propagation delay on wires is proportional to wiring length
To estimate wiring length we need the structure (binding) as well as the placement of the physical implementation of the resources
Fast floor planners or statistical placement models are used
Statistical wiring models can also be used. It has been shown that the average interconnection length is proportional to the total number of blocks to the α power, where 0 ≤ α ≤ 1
Wiring delay and area are related to the average interconnection length

## Slide 26: Control Unit
Difficult task
Control circuit contributes to the overall area and delay because some control signals can be part of the critical path
Simple models for estimating the size of the control circuit can be based on latency

## Slide 27: Strategies for Architectural Optimization
Comprises scheduling and binding
The goal of architectural optimization is to determine a scheduled sequencing graph with a complete resource binding that satisfies the given constraints and optimizes some figures of merit
Architectural optimization consists of determining a schedule φ and a binding β that optimizes the objectives (area latency, cycle-time)
Architectural exploration is often done by exploring the area / latency trade-off for different values of the cycle time
Other approaches are the search for cycle-time / latency trade-off for some binding or the area / cycle time trade-off for some schedules