## Slide 1: EL 653
Register Transfer Level Design with Verilog
Extracted from “Verilog Digital System Design”, Zainalabedin Navabi,
McGraw-Hill, 2006

## Slide 2: RTL Design
RTL design is referred to take a high level design of a design, partition it, describe and implement various component of the architecture
In general a circuit is composed by a data part and a control part
Data part consists of data components and the bussing structure of the design
Control part is usually a state machine generating control signals that control the flow of data in the data part

## Slide 3: Control / Data Partitioning

## Slide 4: Data Part / Data Path
The data part consist of the interconnection of data components and busses
Data components
  Registers
  Combinational logic units
  Registers files
It has external data inputs and outputs, and control inputs and outputs from and to the control part
A data component has control signals that control its clocking and/or its functionalities
Busses have control signals that select their sources and routing of data from one data component to another

## Slide 5: DataPath Module
module DataPath (DataInput, DataOutput, Flags, Opcodes,
ControlSignals);
input [15:0] DataInputs;
output [15:0]DataOutputs;
output Flags, Status1, Status2, ...;
output Opcodes;
input ControlSignals;
//instantiation of data components
// ...
//interconnection of data components
//bussing specifications
endmodule

## Slide 6: Data Component Module
module DataComponent (DataIn, DataOut, ControlSignals);
input [7:0] DataIn;
output [7:0]DataOut;
input ControlSignals;
//Depending on ControlSignals
//operate on DataIn
//and produce DataOut
endmodule

## Slide 7: Control Part / Control Unit
Takes control inputs from the data part and external control inputs and depending on its state makes decisions as to when and what control signals to issue
Consist of one or more state machines
Keep the state of the circuit
Make decisions based on the current data and data status
Control how data is routed and what operations are performed on the data in the data part

## Slide 8: Control Unit Module
module ControlUnit (Flags, Opcodes,ExternalControls,
ControlSignals);
input Flags, Status1, Status2, ...;
input Opcodes;
input ExternalControls;
output ControlSignals;
//Based on inputs decide
//what control signals to issue
//and what next state to take
endmodule

## Slide 9: Data Components
Consist generally of
  Multiplexers for bus specifications
  Register for data storages
  Flip flops for flags
  Combinational logic units for arithmetical and/or llogic operations on data

## Slide 10: Multiplexer
//values are in ns and precision is 100 ps (0.1 ns)
‘timescale 1ns/100ps
module Mux8 (sel, data1, data0, bus1);
input [7:0] data1, data0;
input sel;
output [7:0] bus1;
//6 ns delay for all values assigned to bus1
//bus1 = data1 if sel = 1, else bus1 = data0
assign #6 bus1 = sel ? data1 : data0;
endmodule

## Slide 11: Flip Flop
//values are in ns and precision is 100 ps (0.1 ns)
‘timescale 1ns/100ps
module Flop (reset, din, clk, qout);
input reset, din, clk;
output qout;
always @ (nededge clk) begin
if (reset) qout <= #8 1’b0
else qout <= #8 din;
end
endmodule

## Slide 12: Counter (4 bits modulo 16 counter)
//values are in ns and precision is 100 ps (0.1 ns)
‘timescale 1ns/100ps
module Counter4 (reset, clk, count);
input reset, clk;
output [3:0] count;
reg [3:0] count;
always @ (nededge clk) begin
if (reset) count <= #3 4’b0000
else count <= #5 count + 1;
end
endmodule

## Slide 13: Full Adder
//values are in ns and precision is 100 ps (0.1 ns)
‘timescale 1ns/100ps
module Counter4 (a, b, sum, cout);
input a, b;
output sum, cout;
assign #5 sum = a ^ b ^ cin;
assign #3 cout = (a & b) | (a & cin) | (b & cin);
endmodule

## Slide 14: Shift Register
//values are in ns and precision is 100 ps (0.1 ns)
‘timescale 1ns/100ps
module ShiftRegister8 (sl, sr, clk, ParIn, m, ParOut);
input sl, sr, clk;
input [7:0] ParIn;
input [1:0] m;
output [7:0] ParOut;
reg [7:0] ParOut
always @ (nededge clk) begin
case (m)
0: ParOut <= ParOut;
1: ParOut <= {sl, ParOut [7:1]};
2: ParOut <= {ParOut [6:0], sr};
3: ParOut <= ParIn;
default: ParOut <= 8’bX;
endcase
end
endmodule

## Slide 15: ALU
//values are in ns and precision is 100 ps (0.1 ns)
‘timescale 1ns/100ps
module ALU8 (left, right, mode, ALUout);
input [7:0] left, right;
input [1:0] mode;
output [7:0] ALUout;
reg [7:0] ALUout
always @ (left, right, mode) begin
case (mode)
0: ALUout <= left + right;
1: ALUout <= left - right;
2: ALUout <= left & right;
3: ALUout <= left | right;
default: ALUout <= 8’bX;
endcase
end
endmodule

## Slide 16: Partial Hardware - Interconnections
ALU8 U1 (.left(Inbus), .right(Abinput),
.mode(function),
.ALUout(Outbus));
Mux8 U2 (.sel(select_source),
.data1(Aside),
.data0(Bside));
ALU8 U1 (Inbus, Abinput, function,
Outbus);
Mux8 U2 (select_source, Aside, Bside);

## Slide 17: Controllers
Wired to the data part to control its flow of data
Can be as easy as one flip-flop, handshaking handlers, or as complex as several concurrent state machines
Examples
  Synchronizer – used to synchronize incoming data with a given clock
  Sequence detector – good representation for the general class of controllers

## Slide 18: Controllers
Decisions based on inputs, outputs, state
Issue control signal
Set next state
Go to next state

## Slide 19: Synchronizer
Used to synchronize incoming data with a given clock

## Slide 20: Synchronizer
‘timescale 1ns/100ps
module Synchronizer (clk, adata, synched);
input clk, adata;
output synched;
reg synched;
always @ (posedge clk) begin
if (adata == 0) synched <= 0
else synched <= 1;
end
endmodule

## Slide 21: Sequence Detector
If 110 is detected on a, then w gets 1, else w gets 0
a
w
clk

## Slide 22: Sequence Detector
‘timescale 1ns/100ps
module Detector110 (a, clk, reset, w);
input a, clk, reset;
output w;
parameter [1:0] s0=2’b00, s1=2’b01, s2=2’b10, s3=2’b11;
reg [1:0] current
always @ (posedge clk) begin
if (reset) current = s0;
else
case (current)
s0: if (a) current<= s1; else current <= s0;
s1: if (a) current<= s2; else current <= s0;
s2: if (a) current<= s2; else current <= s3;
s3: if (a) current<= s1; else current <= s0;
endcase
end
assign w <= (current == s3) ? 1 : 0;
endmodule

## Slide 23: Sequence Detector - Testbench
‘timescale 1ns/100ps
module Detector110Tester;
reg aa, clock, rst;
wire ww;
Detector110 UUT (aa, clock, rst, ww);
initial begin
aa= 0; clock = 0; rst = 1;
end
initial repeat (44) #7 closk = ~clock;
initial repeat (15) #23 aa = ~aa;
initial begin
#31 rst = 1;
#23 rst = 0;
end
always @ (ww) if (ww == 1)
$display (“A 1 was detected on w at time = %t”, $time);
endmodule