## Slide 1: MI66B: Complementos de Geotecnia
Enrique Rubio
Gabriel Pais
Notes: This presentation is aimed at providing an overview of numerical modelling and how it applied to mine design. The objective is to set the theme for discussion that will follow.

## Slide 2: Numerical Modelling Background
    Que es el modelamiento numérico?
    Cómo funciona?
    Cuál es la diferencia entre diferentes códigos numéricos?
    Qué se puede lograr a partir del modelamiento numérico?
    Aplicación convencional de la aplicación de modelamiento numérico al diseño?
    Cómo funciona esta aproximación?
    Cuál son las limitaciones?
Notes: Here let’s try to address these issues in a cursory sense only, leaving the details until later.

## Slide 3: Que es ?
La modelación numérica es una manera de representar en forma matemática cómo el macizo rocoso responde a minería:
    Condiciones de carga
    Geometría
    Elasticidad
    Reglas de flujo
Notes: There are really 4 components to a numerical model.

## Slide 4: Condiciones de Carga y Geometría
Overburden Loads
Tectonic Forces
Geometry
Notes: Loading conditions - Prior to mining the rockmass is loaded by overburden and tectonic forces. These are commonly referred to as the far field or in situ pre-mining stresses.
Geometry - When you make excavations, these pre-existing loads are redistributed around the excavations, concentrating in abutments and pillars. The whole point of modelling is to assess the affect that your mining has on the rockmass response.

## Slide 5: Elasticidad y Deformaciones
Elasticidad
Deformaciones


Notes: Elasticity - At locations where the stresses do not exceed the strength, the rock deforms in a more or less elastic manner. This simply means that the deformations are relatively small in magnitude and are mostly recoverable.
Flow rule - At locations where the stresses are concentrated to the point where they exceed the strength, the rock will yield to these loads and deform. This means that the deformations can be relatively large in magnitude and are mostly non-recoverable.
Normally, most of your rockmass will response more or less elastically. Yielding zones will be confined to location in the immediate vicinity of your mining excavations.

## Slide 6: El Análisis de los Resultados
Todos los modelos entregan alguna idea de los esfuerzos deformaciones y desplazamientos, sin embargo la interpretación es la parte de mayor valor de estos resultados
Notes: All numerical models provide predictions of stresses, strains and displacements. While modelling by itself is reasonably straight forward, it is the interpretation of the modelling results that is the real challenge. Somehow we must relate the model predictions of stress, strain or displacement to the response we see in situ.

## Slide 7: Cómo funcionan los modelos numéricos?
Equilibrio
Continuidad
Elasticidad
Non linearidad
Notes: Numerical modelling achieves this simulation by using certain physical constraints on how the rockmass can respond.

## Slide 8: Equilibrio
    xx/x + xy/y + xz/z + X = 0
    xy/x + yy/y + yz/z + Y = 0
    xz/x + yz/y + zz/z + Z = 0
Todas las fuerzas deben balancearse en un elemento o cara
Fuerzas externas a la condición pre minería y geométrica, calor, deformaciones, sismicidad
Notes: Equilbrium – Applied forces must always balance one another at all locations in the model. If you cut out a small cube of material and examine the stresses acting on this cube these stresses must be in equilibrium.
Note that terms X, Y and Z, represent body forces that can be used to apply any sort of external field loading. External field loading can be the result of heating, fluid pressures material non-linearity etc. In addition, these can be determined from many forms of in situ monitoring including for example fluid pressures (e.g. well drawdown, dams, hydrofracturing), heating (e.g. natural heating, nuclear waste storage), deformations (e.g. monitored with extensometers), and seismic activity (e.g. definition of fault slip or material non-linearity from seismic data). It is these terms that will be used for the integration of numerical modelling with seismic monitoring.

## Slide 9: Continuidad
    2xx/y2 + 2yy/x2 = 2xy/x/y
    2yy/z2 + 2zz/y2 = 2yz/y/z
    2zz/x2 + 2xx/z2 = 2xz/x/z
    22xx/y/z = /x(  yz/x  xz/y  xy/z )
    22yy/x/z = /y( yz/x  xz/y  xy/z )
    22zz/x/y = /z( yz/x  xz/y  xy/z )
    La materia se conserva
Notes: Continuity – In the rockmass continuum, the mass of material must be maintained. You cannot have material disappearing or being created.

## Slide 10: Elasticidad
    xx = xx + E/(1+)/(1-2) [(1-) xx +  (yy + zz)]
    yy = yy + E/(1+)/(1-2) [(1-) yy +  (zz + xx)]
    zz = zz + E/(1+)/(1-2) [(1-) zz +  (xx + yy)]
    xy = xy + E/(1) xy
    yz = yz + E/(1) yx
    xz = xz + E/(1) xz
    Acá es donde la s cargas de pre-minería entran en la física ().
Notes: Elasticity - At locations where the stresses do not exceed the strength, the rock deforms in a linear elastic manner: stresses varying in direct proportion to the strains.

## Slide 11: No Linearidad
    1 = UCS + 3 tan2(45+/2)
pvol = p1 + p2 + p3 = f(p1-p2)
Resistencia depende del esfuerzo
Deformación depende del sobre esfuerzo
Notes: Non-linearity - At locations where the stresses are concentrated to the point where they exceed the strength, the rock will yield to these loads and deform: deformations are all allowed to proceed until the stresses relax down to the strength.

## Slide 12: Cómo funciona ?
Las ecuaciones de equilibrio y continuidad son ecuaciones diferenciales. Estas se integran en el macizo rocoso para obtener las condiciones de borde pre establecidas.
BEM integra analíticamente las ecuaciones y luego aproxima para obtener las condiciones de borde.
FEM FDM utilizan integración matemática sobre el macizo rocoso para obtener las condiciones de borde
Notes: There are many ways of accomplishing this. BEM integrate the equations analytically, then use a numerical approximation to satisfy the boundary conditions. FEM and FDM packages use a numerical integration scheme to integrate the differential equations.
It must be emphasized that all numerical models solve these same equations. Different methods use different methods to achieve this.

## Slide 13: Todos los modelos numéricos utilizan las ecuaciones siguientes
surface = far_field + MD BEM
P = Ku FEM or FDM
Notes: Both of these equations constitute a mathematical description of how the rockmass responds. All numerical models (Map3D, Flac, Udec, Minsim, Nastran, etc.) use some variation on this approach.
These equations need to be solved simultaneously such the boundary conditions are satisfied. By solving these equations throughout the rockmass, along with the loading conditions and geometry, you conduct a “stress analysis”.
No matter which method is used, you end up with a large set of equations that describes how various parts of the rockmass interact with one another. A typical mine wide model would have in the range of 100,000 to 1,000,000 equations depending on how much detail we build into the model, and whether we use elastic or non-linear modelling.

## Slide 14: El propósito final?
Predecir el comportamiento del macizo rocoso cuando su equilibrio es alterado por minería
Notes: We specify the loading conditions, specify the geometry (this can include dykes, faults, bedding etc.), assume that elasticity and/or non-linearity applies, then solve these equations for the stresses, strains, displacement etc. throughout the rockmass.
By examining the results from the stress analysis we can identify locations that are for example over-stressed or yielding. We can determine what locations need support and what type of support is appropriate, etc.

## Slide 15: Cual es el proposito?
Comparar diferentes layouts alternativos para la mina
Desarrollar estrategias para problemas conocidos
Evitar perdidas de producción
Apoyo al diseño y soporte de pilares, caserones y excavaciones en general
Notes: Knowing what problems to expect, and the time and location of these problems is the ultimate goal.
Compare alternative mine layouts.
Develop strategies to deal with problems.
Avoid unexpected production interruptions.
Lay down hard design numbers for support, pillar widths, stope heights, etc.

## Slide 16: Aproximación convencional al uso de modelos numericos?
Conducir estudios paramétricos de la condición pre minería de esfuerzos
Comparar diseños alternativos
Identificar los factores que afectan estabilidad
Considerar soporte vs estabilidad
Notes: Parametric studies certainly provide useful information as they allow you to develop strategies to deal with problems if and when they occur.

## Slide 17
Al final es fundamental conocer la confiabilidad de los diseños de modo de establecer el riesgo y la base de costo que permite sustentar las decisiones mineras
Notes: But if you want to use modelling to lay down hard design numbers for support requirements, specific pillar widths, acceptable stope heights and actual costs, you need to have confidence in the accuracy of your predictions.
For example, there would be no point in specifying that a pillar be made 1.2m wide based on a model prediction if you had no idea how reliable this prediction was. You would never allow personnel to walk under a brow based on modelling results that indicated the brow was safe unless you also were confident that the predictions were reliable.

## Slide 18: Confiabilidad
Uno puede saber que la confiabilidad de un determinado diseño es baja, por el contrario uno podría presentar diseños que poseen alta confiabilidad y que poseen un alto nivel de precisión los tomadores de decisión necesitan saber esto para poder hacer sus análisis de beneficio costo y riesgo de un proyecto
Sin estimación de confiabilidad el modelo no posee valor
Notes: It is worth spending a moment to reflect on this statement. I can think of no examples where predictions of unknown reliability are of any value.
Let’s ask these two questions:
If somehow you could show that your model predictions were 99% reliable (i.e. only ±1% error) why wouldn’t you use them?
If somehow you could show that your model predictions were only 1% reliable (i.e. ±99% error) why would you use them?
The real crux of the matter here is reliability. We must know the reliability of our predictions or we have nothing.

## Slide 19: Aproximación observacional al diseño Terzaghi’s
Realizar estudios parametricos con diferentes layouts
Comenzar la minería
Monitorear el comportamiento del macizo rocoso, visualmente
Re diseñar en base a las observaciones, proceso de calibración
Notes: The procedure used to establish the reliability is called “Terzaghi’s Observational Approach to Design”.

## Slide 20: Calibración
Mina
Monitoreo
Re diseño
Aproximación de Terzaghi’s al diseño de minas
Notes: Whether we use numerical modelling or not, this is the basic approach we all use to design in our mines.

## Slide 21: Que tan bien funciona?
En la medida que la minería progresa los modelos se calibran y los diseños alcanzan mejores niveles de confiabilidad
Notes: The value of this approach is that as mining progresses, you numerical model becomes better and better calibrated: you learn how reliable or unreliable your model is. Note that traditionally observations of the rockmass response are made visually and often supplemented with sparsely located instruments. By making observations of rockmass response, over time you literally get to see when the model works and when it does not. You learn what features need to be included in the model (e.g. fault planes, lithology, loading conditions etc.). You not only learn how to use the model to predict rockmass response, but also gain confidence in the predictions and recognize situations where the model predictions are suspect.

## Slide 22: Utilizando back análisis para estimar los parámetros de resistencia del macizo rocoso
Rockburst plot
Notes: To reinforce this concept let’s consider a real example. Consider several pillar bursts that occurred at Inco’s Creighton Mine over several years of mining. For each rockburst, a numerical model was run to determine the stress state at the time and location of the burst. If we plot all of these stress predictions on a set of 1 versus 3 axes we see that there is a strong correlation between the stress state at the time of each burst and a strength criterion. The coefficient of correlation of this data is 0.90.
Let’s state this in a different way. If you calculate the difference between the stress state for each pillar failure and the best fit line, then take the mean of these errors, you will find that the mean error in prediction of 1 is approximately 14 MPa. This gives a coefficient of variation of only ±7%.

## Slide 23: Errores
El coeficiente de correlación de la recta es de 0.9
Tomando la diferencia entre los valores observados y la correlación se obtiene un valor desviación medio de 14 MPa con un coeficiente de variación de 7%.

## Slide 24: Confiabilidad
(a)
(b)
(a)
(b)
Fuera de la banda de incertidumbre
Dentro de la banda de incertidumbre
Notes: It is evident that for this particular example, the stress state predicted from numerical modelling is a very reliable predictor for the the time and location of pillar bursts.
Considering the figure on the left, certainly you would not expect pillars with stress states (a) or (b) to burst at this point in the mining sequence (i.e. (a) should have burst by now, (b) should have burst yet).
This is because they are a lot more than 14 MPa (the mean error in prediction) from the best fit line. We can see the reliability of our predictions from the other back-analysis results, and it is obvious that pillars with stress states (a) or (b) are well out of the range of uncertainty.
Alternatively, considering the figure on the right, you could not say with confidence that pillars with stress states (a) or (b) would or would not burst. While pillar (a) is above the best fit line and hence should have burst by now, it is well within the range of variability: other pillars reached this stress level without bursting. Similarly, although pillar (b) is below the best fit line and hence should not burst yet, it is well within the range of variability: other pillars reached this stress level and had already burst. We can see the reliability of our predictions from the other back-analysis results, and it is obvious that pillars with stress states (a) or (b) are well within the range of uncertainty.

## Slide 25: Problemas con la metodología anterior
Se demora muchas pasadas para poder aplicar el método minería, monitoreo, re diseño. Es difícil obtener la confiabilidad
Podría tomar varios años tener estimaciones confiables.
Notes: Shortcomings is probably the wrong term to use here. It would be more appropriate to call these problems or costs associated with this approach.
This takes time, manpower and continued dedication (a lot of trips underground). Monitoring the rockmass response is no trivial task.
While I firmly believe that predictions of unknown reliability are of no value, only you can decide if the effort required to determine the reliability can be justified ( i.e. it is worth following through with this approach).

## Slide 26: Problemas con la metodología anterior
Existen discontinuidades geológicas que no pueden ser modeladas explicitamente
El no incluirlas desvalida el resultado
Notes: There are other less obvious problems here. For example, often the details of the location, shape, extent and condition of various faults are not well enough known to be included in a numerical model with any accuracy.
Through proper application of Terzaghi’s Observational Approach to Design you can establish the level of reliability in the model predictions. It could be that you find out that they are very unreliable and be left with an unpredictable situation (at least unpredictable as far as your existing model is concerned). Even in this unfortunate case we need to know this, so we can make intelligent decisions (i.e. ignore the numerical modelling results)..

## Slide 27: Problemas con la metodología anterior
Cuando la geología o los esfuerzos pre minería cambian muy bruscamente al interior de la mina los modelos generalmente no serán capaces de reproducir esta variabilidad.
Notes: There are modelling examples where practitioners (Pariseau, 19??) have mapped drives in extreme detail and assigned appropriate sets of material properties to each bit of the rock according to the mapping. The resulting stress analysis produced predictions with remarkable agreement to the observed deformations. In another example (Wiles, 1988) showed that by measuring the in situ stresses before and after pillar mining, that the stress analysis results agreed very well with these measurements. This latter case demonstrated that it was our lack of detailed knowledge of the pre-mining stress state that limited prediction accuracy, not the model itself.
Normally we do not have this type of information, and hence it is not taken into account. This shows up as large scatter in model predictions thus reducing reliability.
Wiles, T.D., “Accuracy and Applicability of Elastic Stress Analysis Methods in Mining”, 15th Canadian Rock Mechanics Symposium, Toronto, 1988.

## Slide 28: Problemas con la metodología anterior
La metodología es utilizable cuando existe minería
No se puede aplicar en estudios de factibilidad o proyectos en vías de explotación
Notes: Laboratory testing and degradation to rockmass strength should only be used as a deficient alternative when back-analysis results are not available.

## Slide 29: Cómo mejoramos la situación actual
No existe substituto para el back análisis
Notes: We must always correlate our results with observed rockmass response. This is the only way to determine how well our model is working.

## Slide 30
Cómo mejoramos
La integración de los datos micro sismicos mejora la calibración e interpretación
Map3Di
Notes: Regardless of issues surrounding rockbursting, seismic monitoring is a tool that provides a wealth of information of when, where and how the rockmass responds. There is no other tool that let’s us see how the rockmass is behaving at depth as economically as seismic monitoring.
Map3Di has been developed as part of some cooperate research between ISSI and Mine Modelling Pty Ltd. This version of Map3D allows you to apply field loading effects implied by seismicity.