## Slide 1: Interpretación de los Modelos Numéricos
Notes: This section will deal with the fundamentals behind model interpretation. I will call this the “state of the art” as this discussion will deal only with proven methods for interpretation and application of modelling.

## Slide 2: Modelos Numéricos Apoyan
Diseño de pilares
Estabilidad de techos y caserones
Diseño de soporte
Estabilidad de pozos de perforación
Estabilidad de las discontinuidades
Notes: Our objective in applying modelling to mining problems is to optimize our designs while maintaining safety. We would like to enhance recovery without unexpected production interruptions. We really want to be able to make quantitative predictions. While it is easy to use modelling to show that one situation is better or worse than another, it is not so easy to say exactly how much better or worse. But we would like to do this.
Your boss would like to here yes or no, not maybe.

## Slide 3: Aprox. de la Ingeniería Civil Medición > Predicción
3D Modelación Elástica
Medición de esfuerzos in situ
Ensayos de laboratorio
Criterio de falla de los ensayos de laboratorio
Criterio de falla a escala de la mina
Notes: The classic method for applying modelling in mine design is really borrowed from civil engineering where the ground conditions (stresses, rock quality etc.) are measured, the rock strengths (in the lab) are measured. Some rule of thumb is used to scale lab results to field conditions. Then predictions are made. Designs are finalized. Construction proceeds.
This approach is used in civil engineering since most of their projects are one off designs with little opportunity for adjustment during construction. Because of this, over design based on large safety factors is necessary. It is common to spend a full 5% to 10% of project budgets on geotechnical investigation to ensure the geology and ground conditions are well understood before hand.
This is basically how modelling has been applied to mining since its inception 40 years ago.

## Slide 4: Aprox. Observacional Retro Análisis > Predicción
3D Modelación Elástica
Retro análisis
Criterio de falla en macizo de rocoso homogéneo
Criterio de falla en macizo rocoso discontinuo
Notes: Although the civil engineering approach is often used in mining, it really should not be. We do not have the budget to ensure the geology and ground conditions are well understood before hand. For comparison, consider a typical large mining operation with a budget exceeding $1,000,000/day. 5% to 10% of this would provide nearly $36,000,000/year for ground control/rock mechanics investigations. Given that sort of budget we probably could make significant progress using the civil engineering approach.
In mining most of our designs are ongoing. There is plenty of room for adjustment as mining proceeds. Whether we use modelling or not, we are constantly reassessing stability, modifying support, trimming pillars etc. We are back-analyzing performance all the time.

## Slide 5
Span
Roca fragmentada
Roca quebrada
Roca no dañada
Notes: Let’s begin by defining the rockmass response. The idea here is that using modelling, we can define three regions:
Undamaged – undamaged rockmass.
Cracked ground – moderately damaged.
Broken ground – heavily damaged.

## Slide 6: Respuesta del Macizo Rocoso
1
Carga
1 - Deformaciones
Respuesta elástica
Resistencia Máxima
Respuesta inelástica - daño
Notes: Consider a bit of rock being loaded.

## Slide 7: Roca Sin Daño
Roca No Dañada
Span


0.1%
Notes: In the early stages of loading the rock behaves more or less elastically. This means that deformations occur without casing any damage to the rock. The rock will spring back “linearly” to its original shape when unloaded.
For hard rock we expect the strain to be on the order of 0.1%. There should be no visible damage to the rock quality.

## Slide 8: Roca Fragmentada
Roca Fragmentada
Span
0.1%


0.5%
Roca sin Daño
Notes: At some point the loads get high enough that the rock begins to crack and the deformation are no longer entirely elastic. Due to damage to the internal structure, only part of the deformation is recoverable upon unloading. This response is common called non-linear deformation.
For hard rock we expect the strain to be on the order of 0.5%. There should be visible damage to the rock quality, but not any signs of loosening or loss of integrity.

## Slide 9: Roca Quebrada
Roca Fragmentada
Roca Quebrada
Span
?
?
?
0.1%
0.5%


Roca Sin Daño
1%  10%
Notes: Finally, we expect sliding on these cracks. The cohesive fabric of the rockmass is lost.
We would expect “broken ground” to correspond to post-peak response.

## Slide 10: Cómo se definen estas zonas utilizando modelación numérica ?
Roca fragmentada
Roca Quebrada
Span
Roca sin daño

## Slide 11
Modelamiento No Lineal
1
1
Sin Daño
Fragmentado
Quebrado
1%  10%
0.1%
0.5%
Se estima el desplazamiento no recuperable de la excavación
Notes: We could run non-linear models and attempt to simulate the yielding rock! However in this section we want to address how to accomplish this using elastic modelling only.

## Slide 12
Modelamiento Elástico
1
1
Fragmentado
Quebrado
1%  10%
0.1%
0.5%
Respuesta Elástica
Sin Daño
Proyección de los esfuerzos en la zona elástica
Notes: In elastic modelling, we proceed along a linear projection above the non-linear part of the stress-strain response.

## Slide 13
Modelamiento Elástico
LSS
1
1
1%  10%
0.1%
0.5%
Respuesta Elástica
LSS, loading system stiffness
Notes: It is clear that different levels of over-stressing correspond to different levels of non-linear strain. These are related by the LSS (loading system stiffness).

## Slide 14
Equivalencia entre Sobre Esfuerzo y daño
1
3 - Confinement
1
1
Aumento deSobre Esfuerzo
1%  10%
0.1%
0.5%
Aumento del Daño
Fragmentado
Quebrado
Sin Daño
Notes: We can quantitatively define various levels of overstressing corresponding to levels of damage or non-linear strain.

## Slide 15
Equivalencia entre sobre esfuerzo y daño
Aumenta Sobre Esfuerzo
Aumenta el daño

1
3
Notes: Clearly there is a direct correspondence between overstressing and damage.

## Slide 16
Abandonar la idea de un criterio de falla y asumir varios criterios de daños!
??Resistencia de Macizo Rocoso??
Sin daño: 0.1%
Fragmentado: 0.5%
Quebrado: 1 – 10%
1
3
Notes: Here we would like to define various criteria to represent different ground conditions.

## Slide 17: El Estado del Arte en interpretación de Modelos
Respuesta elástica
Incrementar la resistencia con el confinamiento
Equivalencia entre sore esfuerzo y daño
Notes: The “state of the art” in modelling for mining is based on elastic model interpretation.
Elastic model interpretation is based on two basic assumptions:
1) rock strength increases with confinement; and,
2) there is a correspondence between overstressing and damage.

## Slide 18: La Resistencia de la Roca Aumenta con el Confinamiento
1
3 - Confinement
1
1
Notes: If you compare rocks loaded at different confinements, you will find that the stress at which “failure occurs” increases with confinement. This is generally true for all geologic type materials.
Note that it is not true for metals. Metals behave with basically zero frictional resistance, their strength is based only on cohesion.

## Slide 19: Observación de daño como función del sobre esfuerzo
Increased Damage
Increased Overstressing
Notes: The exact relationship between the amount of overstressing and the amount of damage we will see in situ is not well understood, but there is no reason we could not quantify this relationship. Overstressing is easily obtained from elastic modelling. Damage is easily obtained from underground observations (e.g. rockmass rating). We could readily collect this information and plot it up. This would provide us with an extremely powerful tool for interpreting model results.

## Slide 20: Sobre Esfuerzo
1
3
1
max = ½(1-3)
Predicción Elástica de Esfuerzo
3
1
3
?
Pérdida de confinamiento 3 falla de techo
Incremento de esfuerzo uniaxial 1, falla de pilares
Aumento de esfuerzo de corte, 
Notes: Now let’s consider how exactly we derive the amount of overstressing. This quantity is commonly called excess stress, since it is measured as the amount by which the elastic stress prediction exceeds some strength criterion.
There are of course many ways of measuring “excess stress”. This requires that we assume some stress path to failure. As the rock exceeds the strength, we must choose the path that leads to failure. Does failure occur by:
1) loss of confinement, typical of a back failure (3)?
2) increasing load, typical of a pillar failure (1)?
3) or some combination of both, typical of an abutment failure (max)?

## Slide 21: 1
Notes: Let’s have a look at some of these parameters. Load up file smn.001 and plot for example 1.
This can be done by selecting Plot > Strength Factors > 1 Excess stress. Don’t forget to set appropriate strength parameters using Plot > Strength Factors > fcmod strength parameters.

## Slide 22: Sobre Esfuerzo- Strength Factor A
1
3
1
Predicción Elástica de Esfuerzo (1,3)
SF-A = (UCS + q 3 ) / 1
SF/A = 1 / (UCS + q 3 )
1 = 1 - (UCS + q 3 )
UCS + q 3
Notes: Let’s look at some formal definitions.
For the a straight line, or Mohr-Coulomb failure criterion, the equations are fairly straight forward.
To see what the equations look like for a Hoek-Brown criterion select Help > What’s this? then select Plot > Strength Factors > 1 Excess stress.
Note that the strength factor A makes the assumption that failure will occur by increasing the load. This is representative for pillar failure.

## Slide 23
Cr-6658b
Notes: Let’s now plot SF-A, SF/A, and finally 1.
Plot > Strength Factors > SF-A
Plot > Strength Factors > SF/A
Plot > Strength Factors > 1

## Slide 24
Sobre Esfuerzo - Strength Factor B
1
3
1
Predicción Elástica de Esfuerzo (1,3)
SF-B = [UCS + (q-1)3]/(1-3 )
SF/B = (1-3 ) /[UCS + (q-1)3]
1 = 1 - (UCS + q 3 )
UCS + (q-1) 3
1=3
Utilizado para analizar el potencial de falla de un pilar, se normaliza la resistencia por el efecto confinamiento
Notes: Strength factor B also makes the assumption that failure will occur by increasing the load. This is probably more representative for pillar failure since when the load equals the confinement (i.e. 1= 3) there is no possibility of failure.
For the a straight line, or Mohr-Coulomb failure criterion, the equations are more complex but still fairly straight forward.
To see what the equations look like for a Hoek-Brown criterion select Help > What’s this? then select Plot > Strength Factors > 1 Excess stress.

## Slide 25
Sobre Esfuerzo - Strength Factor C
1
3
½(1-3)
SF-C = [UCS + ½(1+3)(q-1)] /[½(1-3)(q+1)]
½ (1-3) = [ 1 - (UCS + q 3 )] /(q+1)
Strength
1=3
Asume que la falla ocurre por pérdida de confinamiento e incremento de la carga. Más realista para analizar zonas aledañas a la excavación (abutments)
Predicción Elástica de Esfuerzo (1,3)
Notes: Strength factor C makes the assumption that failure will occur by simultaneously increasing the load while decreasing the confinement. This is a common stress path in mining and generally occurs for abutments.
Even for the a straight line, or Mohr-Coulomb failure criterion, the equations are complex.
To see what the equations look like for a Hoek-Brown criterion select Help > What’s this? then select Plot > Strength Factors > max Excess stress.

## Slide 26: Plane of Weakness
1
3
ip
ip
zz
xx
ip
ip
Notes: All of the previous considerations have assumed that the rockmass has equal strength in all directions. Of course most often rockmasses are traversed by one or more joint sets. This gives the rockmass anisotropic strength. The strength changes with orientation due to a weakness causes by the joint set.
Elastic modelling results can be used to examine this situation as well. Since the model calculates the complete stress tensor, it is a simple matter to determine the stresses acting on a plane at some given orientation.

## Slide 27: Excess Shear Stress ip
Notes: Let’s have a look at an example. Load up file smn.001 and plot for example ip.
This can be done by selecting Plot > Strength Factors > ip in-plane excess stress. Don’t forget to set appropriate strength parameters using Plot > Strength Factors > ipmod in-plane parameters.

## Slide 28
Sobre Esfuerzo - Strength Factor IP
ip
ip
ip
Predicción Elástica de Esfuerzos (ip ip)
SF-ip = [Coh + tan() ip ] / ip
SF/ip = ip / [Coh + tan() ip ]
 ip = ip - [Coh + tan() ip ]
Coh + tan() ip
La grilla se asume como el plano de debilidad o falla y calculan los esfuerzos normales y de corte al plano (ip, ip). ip se denomina Excess Shear Stress
ESS
Notes: It is assumed that the grid plane is the fault plane or joint set plane. The in-plane shear ip and normal ip stress components are determined for this plane.
The formal definition for the strength calculations are straight forward in this case.
Note that ip is actually the ESS (excess shear stress).

## Slide 29: Excess Shear Stress ub
Notes: Let’s have a look at an example. Load up file smn.001 and plot for example ub.
This can be done by selecting Plot > Strength Factors > ub ubiquitous excess stress. Don’t forget to set appropriate strength parameters using Plot > Strength Factors > ubmod ubiquitous parameters.
For this plot the Cohesion was set to zero, friction angle to 30º, dip of the ubiquitous plane 60º, and the dip direction was set to 60º.

## Slide 30: Esfuerzos en un Set Estructural
ub
ub
Joints
Grid plane
Se rotan los esfuerzos en torno a una grilla para estimar los esfuerzos en un determinado set de estructuras. Esto evita tener que modelar cada una de las estructuras de manera independiente
Notes: There is no reason why we need to restrict our consideration to the orientation of the grid plane. We could consider the stability of a joint set at some other orientation if desired. All we need to do is rotate the stress tensor around to this joint set orientation and examine the shear and normal stress components. Such a consideration is commonly called a ubiquitous shear strength criterion.

## Slide 31
Sobre Esfuerzo - Strength Factor UB
ub
ub
ub
Elastic stress prediction (ub ub)
SF-ub = [Coh + tan() ub ] / ub
SF/ub = ub / [Coh + tan() ub ]
 ub = ub - [Coh + tan() ub ]
Coh + tan() ub
Se utiliza para analizar la estabilidad y daño para una determinado set de estructuras
Notes: The formal definition for the strength calculations are straight forward in this case.

## Slide 32
Joint Set Ubiquitous planes of weakness
ub
ub
Joints
Grid plane
Notes: At this point it is worth recalling that support requirements are often dictated by the joint behaviour. Locations where the joints are active are often locations where support is critical.

## Slide 33: Análisis de Estabilidad de Dos Set Estructurales
Dip=20 Dir=90
Dip=80 Dir=90
Se despliegan el ub para análizis de estabilidad en el caso de las estruturas sub verticales se determina que no existen problemas de estabilidad en el techo. Sin embargo para el set sub vertical existen problemas en las cajas. Diseño de Soporte
Notes: In such cases we would be better of using a ubiquitous joint failure criterion.
Here we see the excess ubiquitous shear stress ub results on grid 4 of 6800sp.001for two different joint sets. Clearly the joints that are dipping at 20º will be active over the back of the drift, whereas the more steeply dipping joint set will be active in the side walls.

## Slide 34
Rockmass Response
Notes: Let’s now consider the rockmass response in more detail.

## Slide 35
Rockmass Response
1
3
1
1
Peak
Residual
Notes: How does the rock respond if we hold the confinement constant and increase the load?
First the rock will take the load, but at some point the rock will crack and loose its ability to sustain this load. As cohesion is lost through cracking, the rock strength diminishes and the amount of stress the rock can support decreases.

## Slide 36
Elastic Response
1
Load
1 - Deformation
No damage
Micro-cracking
Macro-cracking
Sliding on cracks
Notes: As stated before, early in the loading history there is no damage. As the stresses approach the peak strength, the rock first micro-cracks on grain boundaries. These cracks are too small to see with the naked eye.
As these micro-cracks coalesce into larger macro-cracks, cohesion is lost. These macro-cracks are becoming large enough to be visible.
Finally, in the later stages of deformation, most cracks have formed and deformation occurs primarily by sliding on these. These cracks would now be clearly visible as we would see offsetting and opening.

## Slide 37
Elastic Response
1
Load
1 - Deformation
No damage
Micro-cracking  < 0.5%
Macro-cracking  < 1%
Sliding on cracks  < 10%
Notes: Note that in terms of strain, the micro-cracking stage corresponds to very small deformations. 0.5% strain represents only 5mm of deformation across a 1 metre width.
As the strains approach 1% we are still talking about quite small numbers as 1% strain only corresponds to a single 1 cm wide crack in a 1 metre span, or a ten 1 mm wide cracks in a 1 metre span.
It is not until the strains approach 10% that we should expect to see any real damage. At this level of strain most support systems will be pushed to their limit. 10% strain corresponds to a ten 1 cm wide cracks in a 1 metre span. Note that mild steel rock bolts fail at 10% strain.
There is no unique stage at which we can say the rock is failed. We can only say that there is a progression of failure where the rock gets increasingly damaged to the point where it is no longer stable – unraveling begins.

## Slide 38
Strength???
1
3
1
1
Peak?
Notes: So when we say that we have observed ground failure underground, what did we really see?
Did we detect a location where the stresses reached the peak strength?
If we ran an elastic model and calculated the stresses, would we say that this stress state must fall on the strength envelope?

## Slide 39
Strength???
1
3
1
1
 < 0.5%
 < 1%
 < 10%
Peak?
seismicity begins
Notes: Just like there is no unique definition of failure, there is in fact no single unique failure criterion, but rather a range of criteria that represent different stages of damage to the rock.
So should we expect “failures” in situ to correspond to the peak strength measured from laboratory tests? From an elastic modelling point of view we should consider that when we observe failure in situ, what we really see could be elastic stress predictions at a level above the actual rock strength.

## Slide 40
Rockmass Response
1
3
1
1
Peak
Residual
Failure by creep or fatigue
Notes: Just to complicate matters further, we should also be aware that given time, rocks will fail at loads well below their peak strength. Such failures can occur simply by rock creeping under constant load. This would be accelerated by load cycling (fatigue) that would occur do to repeated blasting near by.
Hence any failure criteria we derive are sensitive to time scale as well. Given some stress state we might decide that a pillar should be stable. This might really mean that it will be stable for 1 week but not 1 month.

## Slide 41: ??Rock Strength??
Is there some unique “failure criterion” or strength envelope for our rock?
1
3
Notes: So what do we mean by rock strength anyway?
Should we expect to be able to identify some unique strength envelop for our rockmass?

## Slide 42
How do we apply this concept to quantitative mine design?
1
3
??Rock Strength??
Notes: How are we going to make sense of this and make useful quantitative mine design decisions? Let’s go back to first principles!

## Slide 43
Equivalence of overstressing and damage
1
3 - Confinement
1
1
Increased Overstressing
Increased Damage
Notes: When we began this discussion we stated that elastic model interpretation was based on two basic assumptions:
1) rock strength increases with confinement; and,

## Slide 44
Relationship between overstressing and damage
Increased overstressing
Increased damage
No damage
Support failure
Micro-cracking
Macro-cracking
Notes: 2) there is a correspondence between overstressing and damage.
It appeared as though it was going to be quite straight forward to interpret model results.

## Slide 45
??Rock Strength??
How do we apply this concept to quantitative mine design?
1
3
Increasing damage
No damage
Notes: To make progress let’s return to these basic assumptions. All we really need to consider is that stress states that tend towards the lower right represent stable, low damage conditions. By contrast, stress states that tend towards the upper left represent increasingly higher damage and loss of stability.
Let’s abandon the idea of a single unique failure criterion and consider a range of conditions instead.

## Slide 46
Quantitative mine design
Abandon the idea of a single unique failure criterion!
1
3
No damage
Support failure
Micro-cracking
Macro-cracking
Notes: We should expect something along the lines of a range of criteria dividing zones where we expect different levels of damage.
In addition, we should expect these lines to shift down and to the right with increasing time under load.

## Slide 47
Quantitative mine design
Ground stability
1
3
Undamaged
Collapse
Stable
Unstable
Notes: Suppose we categorize the rock response into 4 conditions: damaged, stable, unstable and collapsed. We observe how the rock responds in our mine over several years of mining and collect many examples of these different conditions. For each example, we run a back analysis and determine the elastic stress state. Then we plot all of these examples and draw dividing lines between the results. We should expect to see the kind of results illustrated in the figure.

## Slide 48
Quantitative mine design
Support requirements
1
3
No support
Cables
Mesh
Grouted Bolts
Notes: If we did the same exercise for ground support design we might choose the following categories: no support, mesh, grouted bolts, cables.

## Slide 49
Quantitative mine design
Blasthole stability
1
3
Undamaged
Re-drill
Spalling
Offset
Notes: If we did the same exercise for blasthole stability we might choose the following categories: undamaged, spalling, offset, re-drill.

## Slide 50
Standup time
1
3
Indefinite
6 months
1 week
None
Time under load
Notes: We might consider standup time using categories such as:indefinite, 6 months, 1 week, none.

## Slide 51: Quantitative mine design
These same concepts can be applied in terms of shear stress for stability of faults or joint sets as required.
3
1
n

Notes: For fault or joint stability we could use the same concepts except we would need to generate our plots in terms of shear stress and normal stress.

## Slide 52: Blasthole Stability
Notes: Now let’s consider an example of using this concept for blasthole stability.

## Slide 53: CR-SLOT60.001
Notes: Open the results file cr-slot60.001 and zoom in on the hangingwall side to the indicated area.

## Slide 54: CR-SLOT60.001
Notes: Hide block numbers 3, 4, 5, 6 and 23 and plot 1 with trajectories of length 0.01 on grid 1. During mining it was observe that the first ring of blastholes offset and had to be redrilled. Although the second ring spalled quite heavily, they were still usable. The third and subsequent rings exhibited no significant problems.
To hide the blocks select View > Hide > Block Colours and check 3, 4, 5, 6 and 23.
To enable trajectories check Plot > Plot Options > 3D fixed length and enter 0.01 for the length.
To select grid 1, select Plot > Grid Selection > Grid 1.
To plot 1 select Plot > Stress > 1 major principal stress.

## Slide 55: Blasthole stability
Notes: Plot the stresses at these locations on a set of 1 versus 3 axes. To get the stresses simply click on the location of interest. The stress state will be displayed across the bottom of the screen.
We really should be plotting the maximum and minimum stresses in the plane perpendicular to the blastholes for this evaluation.

## Slide 56
Blasthole stability
Notes: Now let’s divide the results by their categories. Note that there are a few outliers. Careful consideration of these points may reveal that they are categorized incorrectly, or alternatively they may not actually fit the trend. This kind of result is always expected.
This entire exercise could have been conducted in terms of time to redrilling.The lines could represent 1 week, 1 month etc.
Note that here we have used in situ observations to derive criterion in terms of stress that describes our expected rockmass response. In other words we have developed a relationship between over-stressing and damage. This is called model calibration.

## Slide 57: CR-SLOTS.001
Notes: Now let’s apply this calibration to predict the expected behaviour at a different location.
Open the result file cr-slots.001 and zoom in on the location shown.

## Slide 58: CR-SLOTS.001
Notes: Hide block numbers 12 and plot 1 with trajectories of length 0.01 on grid 1. During mining it was observe that the first ring of blastholes offset and had to be redrilled. Although the second ring spalled quite heavily, they were still usable. The third and subsequent rings exhibited no problems at all.
To hide the block 12 select View > Hide > Block Colours and check 12.
To enable trajectories check Plot > Plot Options > 3D fixed length and enter 0.01 for the length.
To select grid 1, select Plot > Grid Selection > Grid 1.
To plot 1 select Plot > Stress > 1 major principal stress.

## Slide 59
Blasthole stability
Notes: Now plot these results ring by ring to see where they lie.
It is clear that ring 1 should be expected to be completely unstable. Ring 3 and 4 should be expected to be problem free. Ring 2 is marginally near the spalling line but otherwise should not have any problems.

## Slide 60: Ground Support
Notes: Now let’s consider an application involving ground support requirements.

## Slide 61: Broken Ground Length Cracked Ground Length
Cracked ground
Broken ground
Span
Bolt length
Anchor length
Notes: Let’s first define some terminology. We will assume that the ground response can be described in two categories: broken ground and cracked ground. The broken ground defines the dead weight that our support needs to suspend, and the cracked ground defines where our anchoring begins.

## Slide 62: Cracked Ground Length
Cracked ground
Broken ground
Span
Bolt length
Anchor length
Notes: Now let’s consider the cracked ground length in mode detail. Certainly we want to ensure that our ground support extends into solid ground.

## Slide 63
1
Load
1 - Deformation
No damage
Micro-cracking  < 0.5%
Macro-cracking  < 1%
Sliding on cracks  < 10%
Seismic activity
Dilation
volumetric < 20% ?
Notes: Reconsidering rock response in more detail we see that it is during the micro-cracking stage that most of the seismicity occurs. This is accompanied by lots of dilation as these cracks coalesce into macroscopic size, and the dilation is complete when we reach our residual strength.
With this in mind let’s look at some field data.

## Slide 64
(Martin, 1997)
Notes: At AECL’s underground research laboratory, stresses were calculated at each seismic event location and plotted. It was found that these stresses could be fit by a line given by
1 - 3  60 MPa.
This is equivalent to a Mohr-Coulomb criterion with a UCS of 60 and friction angle of 0º.

## Slide 65
Notes: At Brunswick mine, stresses were calculated at each seismic event location and plotted. After removing those events that could be associated with existing structure, it was found that these stresses could be fit by a line given by
1 - 3  30 MPa.
This is equivalent to a Mohr-Coulomb criterion with a UCS of 30 and friction angle of 0º.

## Slide 66
Notes: At Kanowna Belle mine CMS surveys were used to identify unravelling of the rockmass. By calculating the stress state along the CMS profile one can develop a stress criterion corresponding to the depth of failure. Here it was found that stresses could be fit by a line given by
1 - 3  37.5 MPa.
This is equivalent to a Mohr-Coulomb criterion with a UCS of 37.5 and friction angle of 0º.

## Slide 67
Creighton Mine
Notes: Here I will refer to an area of Creighton Mine at 2Km depth. The maximum horizontal stress is approximately 100MPa and the laboratory UCS is around 240MPa.

## Slide 68
Undamaged-Cracked Criterion
Cracked ground
Broken ground
Undamaged ground
Span
1
3
Undamaged
Cracked
Broken
Not Supportable
Notes: First let’s discuss how to find the strength criterion corresponding to our undamaged-cracked interface depth. By calculating stresses inside and outside the observed cracked zone, it was found that these stresses could be fit by a line given by
1 - 3  120 MPa.
This is equivalent to a Mohr-Coulomb criterion with a UCS of 120 and friction angle of 0º.

## Slide 69
Plan and section showing observed mining induced cracking zone.
Plan
Section
Observed cracked zone
Notes: At Creighton mine, the cracking around mining was observed by examining the ground with a borehole camera.

## Slide 70: Cracked Ground
Notes: To duplicate these latter findings open results file cr-slotp60.001 The cracked zones have been identified using inactive DD elements shown here in red and blue.

## Slide 71: Cr-slotp60.001
Notes: Plot 1 on grid 2 and select several points inside and outside the cracked zone.

## Slide 72
Notes: When these results are plotted you will find that the points can be divided by a line given approximately by 1 - 3  120 MPa.

## Slide 73
Cracked-Broken Criterion
Cracked ground
Broken ground
Span
1
3
Cracked
Broken
Not Supportable
Undamaged ground
Undamaged
Notes: Now let’s discuss how to find the strength criterion corresponding to our cracked-broken interface depth.

## Slide 74: Rib-pillar failures
Notes: Let’s now have a closer look at the silling out stage (result file 6800sp).
Numerous pillars were reported to have failed during this mining.

## Slide 75
Rib-pillar failures
Notes: In fact it would seem most appropriate to use a zero tensile strength since it is most likely that joints would just open in response to tensile loading in any case.

## Slide 76
Undamaged Ground
Cracked Ground
Broken Ground
Notes: When these results are plotted you will find that the points can be divided by a line given approximately by 1 - 3  120 MPa.

## Slide 77
??Rock Strength??
Undamaged
Cracked
Broken
Cracked ground
Broken ground
Undamaged ground
1
3
Span
Notes: Here we would like to define various criteria to represent different ground conditions.

## Slide 78
Notes: Open the results file cr-6658a.001 and zoom in on the hangingwall location indicated.

## Slide 79: Cracked Ground Criterion
8m span
5m Cracked Ground
Notes: If we now plot 1-3 we see that the critical value of 120 MPa is reached at approximately 5m into the back.
To plot 1-3 select Plot > Stress > User and enter s1-s3 as the user defined plot.

## Slide 80: Broken Ground Criterion
2m Broken Ground
Notes: Let’s now plot 1 or SFA using the broken ground length criterion.
We can see that the 0 contour is located at approximately 2m into the back.

## Slide 81: Broken Ground Criterion
Notes: Now let’s look at the stress distribution in the back.

## Slide 82
Highly Stressed Location Span=8m
0.5m
1m
1.5m
2.5m
2m
3m
5m
Broken
Ground
Cracked
Ground
Notes: A close look at the stresses above the back that we are expecting real failure (not just loosening of the joints) of the ground over the back to a depth of around 2m and broken ground to a depth of 5m.

## Slide 83
8m Span
Broken Ground Criterion
2m Broken
Ground
3m Broken
Ground
6m Broken
Ground
Section from previous page

## Slide 84: Lower Stress Location
Notes: Let’s now have a closer look at the silling out stage (result file 6800sp).
Numerous pillars were reported to have failed during this mining.

## Slide 85: Cracked Ground Criterion
No Cracked Ground
8m Span

## Slide 86: Broken Ground Criterion
No Broken Ground
8m Span
Pillar Failure
Pillar Failure

## Slide 87: Broken Ground Criterion
8m Span
Pillar Failure
Pillar Failure
Notes: Now let’s look at the stress distribution in the back.

## Slide 88
1m
1.5m
2m
3m
4m
6m
Broken
Ground
Cracked
Ground
0.5m
Lower Stress Location Span=8m
Notes: A close look at the stresses above the back that we are expecting real failure (not just loosening of the joints) of the ground over the back to a depth of around 2m and broken ground to a depth of 5m.

## Slide 89
Offset
Blastholes
Spalling
Blastholes
Intact
Blastholes
Notes: Note that the lines back-calculated from the blasthole stability analysis fit in quite neatly here.

## Slide 90: Pillar failure
Notes: Let’s now consider a more classic application of pillar failure.

## Slide 91: Lab tests
Notes: Extensive lab tests were conducted to determine the strength. It was found that the best fit Mohr-Coulomb criterion gave a UCS from 231 to 237 MPa and a friction angle of 43.4 º to 48.5º. For the same data, the Hoek-Brown criterion gave a c of 225 to 229 MPa with an m in the range of 13.8 to 19.5
Subsequent tests demonstrated that the lab strength was very sensitive to the over drying procedure used. Samples that were not dried gave a UCS (or c) of only 152 to 182 MPa.
Numerous scan lines were conducted in the area and the RMR was reported to be in the range of 54 to 75.
The question now is how to determine representative field scale strength parameters?

## Slide 92
Lab tests
Notes: Taking the RMR values and using Hoek’s recommendation for field estimates of m and s we get a maximum (RMR=75) possible strength of
c = 182 MPa, m=7.98 and s=0.062
The recommend Mohr-Coulomb fit is rockmass UCS of 75.8 MPa (16.2 MPa cohesion) and 43.7 degree friction angle.
The minimum (RMR=54) strength is given by
c = 152 MPa, m=2.67 and s=0.00603
The recommend Mohr-Coulomb fit is rockmass UCS of 33.7 MPa (8.86 MPa cohesion) and 34.5 degree friction angle.
Both of these values has been determined for an ‘undamaged rockmass’.

## Slide 93
Crown Pillar Failure
Notes: Let’s now examine the predictions that these criterion provide. Stress analyses have been conducted to determine the conditions in the crown pillar as it narrows by advancing mining.

## Slide 94
Crown Pillar Failure
The crown pillar failed during this cut
66m
59m
51m
35m
27m
43m
Notes: If we now advance the mining and examine the stresses in the crown pillar for various crown pillar thicknesses we see the Hoek-Brown criterion is predicting failure of the crown without any mining at all.

## Slide 95
Crown Pillar Failure
The crown pillar failed during this cut
66m
59m
51m
35m
27m
43m
Notes: Now considering the best estimate from the Hoek-Brown criterion, we predict failure of the crown at the second cut (59 metres thick). The crown actually failed when it was 35 metres thick, well above any prediction made using the Hoek-Brown lines (note that even if we were to use the unrealistically high oven-dry c of 229 MPa, we still do not get large enough strength predictions to match observed field behaviour).

## Slide 96: Rib-pillar failures
Notes: Let’s now have a closer look at the silling out stage (result file 6800sp).
Numerous pillars were reported to have failed during this mining.

## Slide 97
Rib-pillar failures
Notes: If we back analyze each of these failures and plot the stress states at the time of failure we see that the Hoek-Brown minimum criterion underestimates the strength enormously in all cases. The Hoek-Brown maximum criterion gives reasonable predictions for the very high confinement range but clearly underestimates the strength for lower confinements.

## Slide 98: Validity of the Hoek-Brown estimates of field strength
This data shows that in the worst case, the Hoek-Brown field strength estimate can severely under-estimate the strength (by a factor of one third).
At best the field strength estimate fits higher confinement pillar failures, but still provides a severe under-estimate of the strength for low confinement cases (by as much as one half).
Notes: Clearly the Hoek-Brown criterion is providing a very poor estimate of the rock mass strength in this case.

## Slide 99: What do others say?
M. Panet - “to arrive at an economic design with an adequate level of safety ... can be achieved only by comparing the model results with the data obtained from real excavations”

## Slide 100: What do others say?
Hoek - “Since testing on a realistic scale is not practical, we have only two avenues open to us... first is to develop a better understanding... second is to use back analysis of the observed performance”

## Slide 101: What do others say?
E. Hoek - “Out approach was entirely empirical and we worked from very limited data of rather poor quality. The fact that the criterion works, more by good fortune than because of its inherent merit, is no excuse for the current lack of effort or even apparent desire to find a better way”.

## Slide 102: What do others say?
Brekke and Howard - “Rock masses are so variable in nature that the chance for ever finding a common set of parameters and a common set of constitutive equations valid for all rock masses is quite remote.”

## Slide 103
Validity of the Hoek-Brown estimates of field strength
Notes: So why doesn’t the Hoek-Brown criterion work? There are 2 reasons:
It would appear that in order to provide a realistic tensile strength, the low confinement portion of the criterion is pulled down do to the inability of the square root function to bend around in this stress range. The curve defined by a square root function simply is not flexible enough to bend around sharply enough.
The procedure for reduction from laboratory measurements to rockmass strength values is flawed.
Another question here is why would we use a curved line?

## Slide 104
Estimated Rockmass UCS |  |  |  |  |  |  | 
GSI/RMR | 75 | 50 | 30 | 75 | 65 | 24 | Cv
Hoek & Brown*1 | 64.8 | 13 | 1.7 | 43 | 8.2 | 1 | 
Ramamurthy*2 | 39.5 | 5.6 | 0.5 | 29 | 4.6 | 0.3 | 
Trueman*3 | 45 | 10 | 3 | 45 | 24.7 | 2.1 | 
Singh*4 | 57.4 | 22.7 | 10.8 | 57.4 | 39.6 | 8.7 | 
Kalamaras et al*5 | 57.4 | 18.8 | 2.4 | 42.1 | 9.7 | 1.2 | 
Sheorey*6 | 43 | 6.6 | 0.6 | 31.5 | 5.2 | 0.3 | 
Hoek*7 | 57 | 11.8 | 1.4 | 41.8 | 7.8 | 0.8 | 
Call | 18% | 49% | 123% | 23% | 92% | 145% | 75%
C3,4 | 20% | 48% | 60% | 18% | 30% | 57% | 39%
Reduction from laboratory measurements to rockmass strength
Notes: There are multiple techniques that have been proposed to achieve degraded rock mass strengths. If we take the results from these various approaches and calculate a coefficient of variation Cv this should provide some indication of the level of uncertainty inherent in this process. Results from in a recent paper by Villaescusa and Li are reproduced in the Table where each column indicates the estimated rock mass compressive strength for various rock mass qualities. Two categories of Cv have been calculated for each column of predictions: Call incorporates all 7 equations; C3,4 excludes equations *3 and *4 (because as recommended by the above authors, these do not use the measured laboratory strength). The mean has also been calculated for both categories.
Villaescusa and Li go on to state that “Comparisons of the estimated parameters using rock mass classification and those used in numerical modelling (by mine site based practitioners) … appear to estimate different rock mass compressive strengths for the same rock mass environment”. Martin and Maybee find that the Hoek-Brown empirical method over-estimates hard rock pillar strengths. Hoek states that his own degradation procedure “works, more by good fortune than because of its inherent scientific merits”, and further that “the user of the Hoek-Brown procedure or of any other equivalent procedure for estimating rock mass properties should not assume that the calculations produce unique reliable numbers”.

## Slide 105
Estimated Rockmass UCS |  |  |  |  |  |  | 
GSI/RMR | 75 | 50 | 30 | 75 | 65 | 24 | Cv
Hoek & Brown*1 | 64.8 | 13 | 1.7 | 43 | 8.2 | 1 | 
Ramamurthy*2 | 39.5 | 5.6 | 0.5 | 29 | 4.6 | 0.3 | 
Trueman*3 | 45 | 10 | 3 | 45 | 24.7 | 2.1 | 
Singh*4 | 57.4 | 22.7 | 10.8 | 57.4 | 39.6 | 8.7 | 
Kalamaras et al*5 | 57.4 | 18.8 | 2.4 | 42.1 | 9.7 | 1.2 | 
Sheorey*6 | 43 | 6.6 | 0.6 | 31.5 | 5.2 | 0.3 | 
Hoek*7 | 57 | 11.8 | 1.4 | 41.8 | 7.8 | 0.8 | 
Call | 18% | 49% | 123% | 23% | 92% | 145% | 75%
C3,4 | 20% | 48% | 60% | 18% | 30% | 57% | 39%
Reduction from laboratory measurements to rockmass strength
Notes: Degradation techniques inherently involve subjective assumptions to derive a guesstimate of in situ strength. Uncertainty occurs because of simplification of the actual complex mechanisms responsible for the degraded strength. Natural variability in the rock mass due to anisotropy, changing geology, pre-existing structure etc., is normally averaged across the mine site in an attempt to derive a single strength envelope or at best, a series of strengths associated with broadly defined lithological units.
It is apparent that there is considerable lack of agreement between various degradation procedures, theory and practice. From the results in the Table it would appear that we should assign something on the order of 39% (C3,4) coefficient of variation for the degradation procedure. The lack of agreement between alternative techniques for degradation of laboratory measurements to rock mass strength demonstrates that this is a very uncertain procedure that could invalidate modelling predictions

## Slide 106
Validity of the Hoek-Brown estimates of field strength
Cv39%
Cv48%
Notes: The actual uncertainty in our prediction accuracy is a combination of the uncertainty from several sources:
Laboratory strength measurements (20%)
Laboratory to rockmass degradation procedure (39%).
Far field stress state (20%-30%).
Appliciability of the adopted modelling procedure (?).
The combined uncertainty can be determined by taking the square root the the sum of the squares of all contributions sqrt(20^2+39^2+20^2+??^2)48++%

## Slide 107
Using back-analysis to determine field scale strength parameters
s=18MPa
Cv10%
Notes: From the back-analysis data is would seem there is little justification for choosing anything but a linear criterion. By simply cutting the Mohr-Coulomb line at any desired tensile strength we achieve a much better fit to the back-analysis results. The best fit line has a UCS of 123.6 MPa and a friction angle of 37.3°.
Note here that the standard deviation is only ±18 MPa. This gives a coefficient of variation of around ±10%, an extremely good fit to the back-analysis data. Compare this to the anticipated 39% value obtained in the previous slide.
Also note that the use of correlation coefficient in this case is totally inappropriate since we are not interested in how strongly the principal stress components are correlated, but rather how good the fit of the line is to the back-analysis data.

## Slide 108
Using back-analysis to determine field scale strength parameters
Notes: In fact it would seem most appropriate to use a zero tensile strength since it is most likely that joints would just open in response to tensile loading in any case.

## Slide 109
Crown pillar failure
The crown pillar failed during this cut
66m
59m
51m
35m
27m
43m
Notes: Let’s examine the crown pillar failure again, but now using the best fit criterion from the sill pillar back-analyses. We see that the crown is predicted to fail at exactly the cut where in fact it did fail.