## Slide 1
Anchor Systems
Notes: <number>
<footer>
<header>
<date/time>

## Slide 2
¿Qué es un Anclaje?
Un anclaje es un elemento estructural que tiene la propiedad de fijar un material a otro que hace las veces de base.
Material a fijar
Anclaje
Material base
Principios de funcionamiento......
Notes: <number>
<footer>
<header>
<date/time>

## Slide 3
Principios de Funcionamiento: Roce
KB-III
HPS
HUD
La carga tensora, N, se transfiere al material base mediante la fricción, R.
Para crear la fricción, se necesita una fuerza expansiva
Ejemplos:
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4
La carga tensora, N, está en equilibrio con las fuerzas de soporte, R, que actúa sobre el material base.
HDA
HIT HY20
Ejemplos:
Principios de Funcionamiento: Área de soporte
HLD
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5
Produce una unión adhesiva entre la varilla o barra reforzada y el adhesivo y entre el adhesivo y el material base
HIT RE 500 + Barra
HVU + HAS
Ejemplos:
HIT HY 150 + HAS
Principios de Funcionamiento: Adhesión
Formas de falla......
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6
Posibles formas de Falla
Falla del Hormigón
“cono”
Corte de la barra
Falla del Adhesivo
(con el acero)
Falla del Adhesivo
(con el hormigón)
Gama de Anclajes Hilti............
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7
Desempeño
Seguridad
Gama de Anclajes Hilti
HDI
DBZ
HVU
HSL
HDA
KB-III
HY-150
RE-500
HLC
HPS
Toggler
HLD
HIT-MM
HA 8
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8
ANCLAJES QUIMICOS
Sistema HVA
(HVU + HAS)
Descripción del Producto:
Ampolla pre-dosificada Metacrilato Uretano de Vinilo (HVU) bi-componente para anclajes en diversas aplicaciones.
Ventajas:
Desempeño de adherencia superior.
Capacitado para soportar cargas sísmicas y vibratorias.
Bajo tiempo de curado.
Gran resistencia a los ciclo de hielo y deshielo.
Gran resistencia a la temperatura.
Excelente resistencia al ataque químico y ácido
Notes: <number>
<footer>
<header>
<date/time>
Comment for the presenter:
This is a Hilti HIT-RE 500 training. Please note that there are separate Hilti HIT training available - one for Hilti HIT-HY and one for rebar applications (in preparation).
For your convenience you will always find the presenter comments below each slide.
For an effective training please bring the following along:
- a fully equipped Hit MD 2000 case as well as a BD 2000 tool
- samples of the HIT-RE 500 cartridges (all sizes available) together with the special mixer
- all brochures/ promo material available.
Welcome to the Hilti HIT-RE 500 system training

## Slide 9
ANCLAJES QUIMICOS
Sistema HVA (HVU + HAS)
Notes: <number>
<footer>
<header>
<date/time>
Comment for the presenter:
This is a Hilti HIT-RE 500 training. Please note that there are separate Hilti HIT training available - one for Hilti HIT-HY and one for rebar applications (in preparation).
For your convenience you will always find the presenter comments below each slide.
For an effective training please bring the following along:
- a fully equipped Hit MD 2000 case as well as a BD 2000 tool
- samples of the HIT-RE 500 cartridges (all sizes available) together with the special mixer
- all brochures/ promo material available.
Welcome to the Hilti HIT-RE 500 system training

## Slide 10
ANCLAJES QUIMICOS
HIT RE-500
Descripción del Producto:
Resina epóxica bi-componente para anclajes en diferentes materiales base como hormigón, piedra natural, grout, madera etc.
Ventajas:
Desempeño de adherencia superior.
Capacitado para soportar cargas sísmicas.
Pequeños diámetros de perforación.
Puede ser instalado inclusive bajo agua.
Excelente resistencia a la interperie
Notes: <number>
<footer>
<header>
<date/time>
Comment for the presenter:
This is a Hilti HIT-RE 500 training. Please note that there are separate Hilti HIT training available - one for Hilti HIT-HY and one for rebar applications (in preparation).
For your convenience you will always find the presenter comments below each slide.
For an effective training please bring the following along:
- a fully equipped Hit MD 2000 case as well as a BD 2000 tool
- samples of the HIT-RE 500 cartridges (all sizes available) together with the special mixer
- all brochures/ promo material available.
Welcome to the Hilti HIT-RE 500 system training

## Slide 11
ANCLAJES QUIMICOS
HIT RE-500
Notes: <number>
<footer>
<header>
<date/time>
Comment for the presenter:
This is a Hilti HIT-RE 500 training. Please note that there are separate Hilti HIT training available - one for Hilti HIT-HY and one for rebar applications (in preparation).
For your convenience you will always find the presenter comments below each slide.
For an effective training please bring the following along:
- a fully equipped Hit MD 2000 case as well as a BD 2000 tool
- samples of the HIT-RE 500 cartridges (all sizes available) together with the special mixer
- all brochures/ promo material available.
Welcome to the Hilti HIT-RE 500 system training

## Slide 12
HIT HY-150
ANCLAJES QUIMICOS
Descripción del Producto:
Resina Hibrida (metacrilato-cemento) bi-componente para anclajes en diferentes materiales base como hormigón, piedra natural y grout.
Ventajas:
Desempeño de adherencia superior.
Capacitado para soportar cargas sísmicas.
Bajo tiempo de curado.
Gran resistencia a la temperatura (soldadura).
Buena resistencia al ataque químico y ácido.
Notes: <number>
<footer>
<header>
<date/time>
Comment for the presenter:
This is a Hilti HIT-RE 500 training. Please note that there are separate Hilti HIT training available - one for Hilti HIT-HY and one for rebar applications (in preparation).
For your convenience you will always find the presenter comments below each slide.
For an effective training please bring the following along:
- a fully equipped Hit MD 2000 case as well as a BD 2000 tool
- samples of the HIT-RE 500 cartridges (all sizes available) together with the special mixer
- all brochures/ promo material available.
Welcome to the Hilti HIT-RE 500 system training

## Slide 13
HIT HY-150
ANCLAJES QUIMICOS
Notes: <number>
<footer>
<header>
<date/time>
Comment for the presenter:
This is a Hilti HIT-RE 500 training. Please note that there are separate Hilti HIT training available - one for Hilti HIT-HY and one for rebar applications (in preparation).
For your convenience you will always find the presenter comments below each slide.
For an effective training please bring the following along:
- a fully equipped Hit MD 2000 case as well as a BD 2000 tool
- samples of the HIT-RE 500 cartridges (all sizes available) together with the special mixer
- all brochures/ promo material available.
Welcome to the Hilti HIT-RE 500 system training

## Slide 14
ANCLAJES MECANICOS
HSL
Descripción del Producto:
Anclaje de expansión extra-fuerte, especialmente diseñado para cargas dinámicas y pesadas.
Ventajas:
Extraordinaria capacidad de carga.
Capacitado para soportar cargas sísmicas, vibratorias e impacto.
Camisa metálica que otorga capacidad al corte adicional.
Apropiado para ser instalado en hormigón fisurado.
Fuerza de expansión controlada.
Notes: <number>
<footer>
<header>
<date/time>
Comment for the presenter:
This is a Hilti HIT-RE 500 training. Please note that there are separate Hilti HIT training available - one for Hilti HIT-HY and one for rebar applications (in preparation).
For your convenience you will always find the presenter comments below each slide.
For an effective training please bring the following along:
- a fully equipped Hit MD 2000 case as well as a BD 2000 tool
- samples of the HIT-RE 500 cartridges (all sizes available) together with the special mixer
- all brochures/ promo material available.
Welcome to the Hilti HIT-RE 500 system training

## Slide 15
ANCLAJES MECANICOS
HSL
Notes: <number>
<footer>
<header>
<date/time>
Comment for the presenter:
This is a Hilti HIT-RE 500 training. Please note that there are separate Hilti HIT training available - one for Hilti HIT-HY and one for rebar applications (in preparation).
For your convenience you will always find the presenter comments below each slide.
For an effective training please bring the following along:
- a fully equipped Hit MD 2000 case as well as a BD 2000 tool
- samples of the HIT-RE 500 cartridges (all sizes available) together with the special mixer
- all brochures/ promo material available.
Welcome to the Hilti HIT-RE 500 system training

## Slide 16
ANCLAJES MECANICOS
KB - III
Descripción del Producto:
Anclaje de expansión de una sola cuña que actúa como tres independientes que proporcionas resistencias medianas a fuertes .
Ventajas:
Buena capacidad de carga.
Capacitado para soportar cargas estáticas.
Puede ser instalado en agujeros sin fondo.
Identificación de longitudes.
Buen rendimiento en perforaciones diamantadas.
Notes: <number>
<footer>
<header>
<date/time>
Comment for the presenter:
This is a Hilti HIT-RE 500 training. Please note that there are separate Hilti HIT training available - one for Hilti HIT-HY and one for rebar applications (in preparation).
For your convenience you will always find the presenter comments below each slide.
For an effective training please bring the following along:
- a fully equipped Hit MD 2000 case as well as a BD 2000 tool
- samples of the HIT-RE 500 cartridges (all sizes available) together with the special mixer
- all brochures/ promo material available.
Welcome to the Hilti HIT-RE 500 system training

## Slide 17
ANCLAJES MECANICOS
HDI
Descripción del Producto:
Anclaje de rosca interna con cono de expansión para ser instalado en hormigón.
Ventajas:
Capacidad de carga mediana.
Capacitado para soportar cargas estáticas.
Poca profundidad de empotramiento.
Instalación al ras para insertar varillas roscadas.
Ideal para instalaciones repetitivas.
Notes: <number>
<footer>
<header>
<date/time>
Comment for the presenter:
This is a Hilti HIT-RE 500 training. Please note that there are separate Hilti HIT training available - one for Hilti HIT-HY and one for rebar applications (in preparation).
For your convenience you will always find the presenter comments below each slide.
For an effective training please bring the following along:
- a fully equipped Hit MD 2000 case as well as a BD 2000 tool
- samples of the HIT-RE 500 cartridges (all sizes available) together with the special mixer
- all brochures/ promo material available.
Welcome to the Hilti HIT-RE 500 system training

## Slide 18
RESUMEN DE SELECCIÓN DE ANCLAJES
Notes: <number>
<footer>
<header>
<date/time>
Comment for the presenter:
This is a Hilti HIT-RE 500 training. Please note that there are separate Hilti HIT training available - one for Hilti HIT-HY and one for rebar applications (in preparation).
For your convenience you will always find the presenter comments below each slide.
For an effective training please bring the following along:
- a fully equipped Hit MD 2000 case as well as a BD 2000 tool
- samples of the HIT-RE 500 cartridges (all sizes available) together with the special mixer
- all brochures/ promo material available.
Welcome to the Hilti HIT-RE 500 system training

## Slide 19
TEORIA DE DISEÑO DE ANCLAJES
Notes: <number>
<footer>
<header>
<date/time>

## Slide 20
Método de diseño tradicional.
  Actualmente, los datos obtenidos por los anclajes HILTI, se ajustan a la norma ETAG (anexo C) y el ACI 318 (apéndice D) para CC method.
Método Clásico
Tensiones admisibles
Resultados conservadores
Sin información del comportamiento en la falla
Estado de arte actual
Capacidad del hormigón
Tensiones de rotura
Resultados bastante reales
Diferenciación entre modos de falla
Diferenciación de coeficientes de
seguridad para tipo de carga

## Slide 21
Ejemplo, Condiciones de diseño
Anclar soporte tipo bracket para suportación de tubería de 6” a pilar de hormigón en planta de procesos industriales.
Requerimientos del lugar de instalación (preselección del anclaje adecuado):
  Resistencia a vibraciones (tubería flujo a presión)
  Resistencia cargas dinámicas.
  Posible soldadura cerca de la placa.
Antes de determinar mediante calculo, secciones tipo de acero y empotramientos se debe seleccionar el sistema adecuado.

## Slide 22
Datos Iniciales:
  Separación entre soportes 4 mts.
  Peso de la tubería 50 kgf/mt.
  Pilar de sección 50 x 50 cm.
  Hormigón H30 (4000psi)

## Slide 23
V, dis= 103,5 kgf
T,dis = 287 kgf

## Slide 24
Selección anclaje adecuado
Debemos seleccionar un anclaje según la condición requerida:
resistencia a vibraciones (tubería flujo a presión)
resistencia cargas dinámicas.
Posible soldadura cerca de la placa.
SISTEMA HVA

## Slide 25
Se propone analizar para un anclaje del tipo:
HVU + HAS – E Estandar 3/8” x 6.1/2” (EMP = 5 ¼”)
ADHERENCIA

## Slide 26
RESUMEN DE SELECCIÓN DE ANCLAJES
Notes: <number>
<footer>
<header>
<date/time>
Comment for the presenter:
This is a Hilti HIT-RE 500 training. Please note that there are separate Hilti HIT training available - one for Hilti HIT-HY and one for rebar applications (in preparation).
For your convenience you will always find the presenter comments below each slide.
For an effective training please bring the following along:
- a fully equipped Hit MD 2000 case as well as a BD 2000 tool
- samples of the HIT-RE 500 cartridges (all sizes available) together with the special mixer
- all brochures/ promo material available.
Welcome to the Hilti HIT-RE 500 system training

## Slide 27
Anchor Systems Departamento de Ingenieria, Tel 6553043; 6553015
Notes: <number>
<footer>
<header>
<date/time>