## Slide 1
Notes: <number>
<footer>
<header>
<date/time>

## Slide 2
Notes: <number>
<footer>
<header>
<date/time>

## Slide 3
Vh = Fc1
Shear Connection in Composite Beams
Notes: <number>
<footer>
<header>
<date/time>
Shear connectors in the form of headed studs (Nelson studs) are commonly used in floor construction. They have the purpose of connecting the concrete slab to the steel beam so that the two can work together as one structural unit.
  If the studs are not welded together with the decking (as shown here), the decking fastenings will have to provide lateral support for the beams. (The decking installer (Richard Lees) used ENP2 instead of DAK16 because the greater shear strength of the ENP2 fastening could be utilized.
  The embossments on the web of the decking profile are provided for the purpose of providing and interlocking of the decking profile and the concrete. In other words, the embossments work as “shear connectors” between the decking and the concrete.
next slide

## Slide 4
The X-HVB is an alternative to the headed stud shear connector
Relevant disadvantages:
Large bulky placing equipment
Installed quality sensitive to:
  Weather
  Coatings on beam and decking
  Operator skill, training and experience
Notes: <number>
<footer>
<header>
<date/time>
Shear connectors in the form of headed studs (Nelson studs) are commonly used in floor construction. They have the purpose of connecting the concrete slab to the steel beam so that the two can work together as one structural unit.
  If the studs are not welded together with the decking (as shown here), the decking fastenings will have to provide lateral support for the beams. (The decking installer (Richard Lees) used ENP2 instead of DAK16 because the greater shear strength of the ENP2 fastening could be utilized.
  The embossments on the web of the decking profile are provided for the purpose of providing and interlocking of the decking profile and the concrete. In other words, the embossments work as “shear connectors” between the decking and the concrete.
next slide

## Slide 5
Cartridge 6.8/18M
ENPH2-21
X-HVB50
X-HVB80
X-HVB95
X-HVB110
X-HVB125
X-HVB140
The X-HVB System
DX 76 with 76/HVB equipment
Notes: <number>
<footer>
<header>
<date/time>
Shear connectors in the form of headed studs (Nelson studs) are commonly used in floor construction. They have the purpose of connecting the concrete slab to the steel beam so that the two can work together as one structural unit.
  If the studs are not welded together with the decking (as shown here), the decking fastenings will have to provide lateral support for the beams. (The decking installer (Richard Lees) used ENP2 instead of DAK16 because the greater shear strength of the ENP2 fastening could be utilized.
  The embossments on the web of the decking profile are provided for the purpose of providing and interlocking of the decking profile and the concrete. In other words, the embossments work as “shear connectors” between the decking and the concrete.
next slide

## Slide 6
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8
Nail shank :
HRC58 ± 1, fu = 2100 MPa
Knurled for anchorage in steel
Forged point
Zinc plated, 8 - 16 m
Steel washers :
Made from ST2K40 RP steel (cold rolled, unalloyed mild steel)
Zinc plated, 10 - 20 mm
ENP2-21 L15 Nails
Especificación Materiales
Notes: <number>
<footer>
<header>
<date/time>

## Slide 9
Datos Tecnicos
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10
Disposicion general de los conectores
Paralelo a la viga
Transversal a la viga
La disposición de los conectores independiente de su orientación deben situarse en forma alternada uno respecto al otro.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11
Placa colaborante paralela a la viga
General
Espaciamiento entre alas verticales de los conectores
>= 100 mm
<= 4 * hc
<= 600 mm (a menos que el espesor de la placa metálica provea la resistencia adecuada)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12
Un conector por valle
Alternar la dirección de los X-HVB entre uno y otro.
Los X-HVB pueden ser instalados sobre el alma, o alternados izquierda o derecha para asegurar simetría.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13
Dos o tres conectores por valle
Alternar la dirección de los X-HVB en el valle
Mínimo 50 mm de espaciamiento transversal entre conectores
.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14
Placa colaborante perpendicular a la viga
General
Esta es la solución más común.
Es la solución donde los errores son más serios.
Espaciamiento de valles con presencia de conectores:
>= 100 mm
<= 4 * hc
<= 600 mm (a menos que el espesor de la placa metálica provea la resistencia adecuada)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15
Un conector por valle
Alternar la dirección de los X-HVB 95 entre valle y valle (nervio y nervio).
Dos o tres conectores por valle
Centre los X-HVB 95 en el nervio o altérnelos alrededor del centro del nervio.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16
En aquellos casos en que los valles son demasiado estrechos para la orientación longitudinal, use la orientación transversal a la viga.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 17
Valles Transversales a la viga
3 Conectores X-HVB por valle
Elemplos disposicion conectores
Notes: <number>
<footer>
<header>
<date/time>

## Slide 18
Valles Transversales a la viga
2 Conectores X-HVB por valle
Notes: <number>
<footer>
<header>
<date/time>

## Slide 19
Valles Paralelos a la viga
2 Conectores X-HVB por valle
Notes: <number>
<footer>
<header>
<date/time>