## Slide 1: Step by Step Construction of Numerical Models in MAP3D

## Slide 2: MAP3D File Types
*.INP
*.PNT
*.001, *.002
File to build and save excavations
File to build and save construction lines
File with step results, analysis
(After run *.inp file)
Export grid stress display

## Slide 3: Model Construction
3D Elements
2D Elements
2D Grids
1D Grids
Construction
Lines

## Slide 4: Drifting
Blue means selected

## Slide 5: Build Snapping Modes
Start/Close the building line in any part of a line
Start/Close the building line in corners and points
Start/Close the building line in the middle of any line
Create a squere reference system like with points inside it

## Slide 6: Drifting
Selected (blue)
To build a tunnel, first it is necessary to create a reference system like in the figure (above) and then set the location of the reference system as shown below
Origin of the center of the grid
Horizonal grid
Vertical grid
Move the center of the grid with the mouse
you can also change the spacing an number of intervals, depending of the size of your excavation
Spacing of points
Size of grid

## Slide 7: Base of a Tunnel
The figure on the left shows the unclosed base of a tunnel of 4[m] wide

## Slide 8: Base of a Tunnel
The base of the tunnel is closed when you click where you started and the red message displays

## Slide 9: Base of a Tunnel
Click the extrude button.
In the Offset Vector Windows put the amount of the extrude. In this case the direction is Z.
Click OK

## Slide 10: Base of a Tunnel
Set the FF block properties
Inactive features that are not considered when solving equilibrium
Name (all the excavations can have the same name)
Fictitious Force (FF) to represent a 3D excavation
Discrete discontinuity (DD) to represent a 2D feature that may yield as a result of over stress applied as Excess shear stress

## Slide 11: Base of a Tunnel
Mining step means when the feature will be excavated as 0. If a different material is used as backfill then enter the number of the material
0 means always air
Click Build
Unselect to create a single block

## Slide 12: Base of a Tunnel
If there is a problem in the excavation properties, it is possible to change those following the steps above
Colors must be chosen carefully in order to make most of the features different and being able to select them as per color property. There are 10 colors that can be used in double digits to identify different blocks. Ie an excavation could be 3 and the rib pillar could be 33

## Slide 13: Copying Features
To create another tunnel perpendicular and above the first one (10[m]), it will be copied

## Slide 14: Rotate a Feature
Both excavations have the same properties because one is a copy of the other.

## Slide 15: Build a 2D Grid
Grid plane (where stress will be calculated)
The grid will be put horizontal and in the red line

## Slide 16: Hide a Block
To hide the upper block

## Slide 17: Draw a 2D Grid
Stresses will be calculated in the grid
Display all the hidden excavations

## Slide 18: Edit a 2D Grid
The grid will be scaled, because it is little.
From the centroid of the grid, it will be scaled 3 times in x and 2 times in y

## Slide 19: Grid Construction
To click in the middle of a line

## Slide 20: Grid Construction
To click in the middle of a line

## Slide 21: Material properties
Material properties for Freeport are shown below.

## Slide 22: Building a Diorite Block

## Slide 23
Build the base
Extrude
Geology will be modeled like an excavation with a material inside it (non zero)
Building a Diorite Block

## Slide 24
>1, (1 = Universe Material)
Building a Diorite Block

## Slide 25: Seting Rock Properties
Always “1” is the number material of the universe
Linear models only use Young’s Modulus and Poisson’s Ratio
Given by Freeport Geotechnical engineers

## Slide 26
Always check Elastic only
Skarn
Diorite
Air
Seting Rock Properties

## Slide 27: DATUM + Aplicación

## Slide 28: Ecuaciones
    xx = xx + E/(1+)/(1-2) [(1-) xx +  (yy + zz)]
    yy = yy + E/(1+)/(1-2) [(1-) yy +  (zz + xx)]
    zz = zz + E/(1+)/(1-2) [(1-) zz +  (xx + yy)]
    xy = xy + E/(1) xy
    yz = yz + E/(1) yx
    xz = xz + E/(1) xz
MAP3D resuelve ecuaciones diferenciales que definen la continuidad, elasticidad (MAP3D-SV) y no linealidad (MAP3D-NL). Como se mencionó en la clase pasada, ahora sólo veremos el caso elástico.
El caso elástico supone que la roca se deforma linealmente hasta que encuentra su situación de stress máximo…..Una vez alcanzada ésta, la deformación es no-lineal….
Ecuaciones elásticas
Notar que las ecuaciones que describen la elasticidad dependen sólo del módulo de Young y de Poisson, es decir sólo dos parámetros.

## Slide 29: DATUM
En el método numérico de elementos de borde, sólo es necesario conocer el stress completamente en un sólo punto o datum (sigma0, ver ecuaciones lámina anterior).
Sin embargo, dicho stress debe ser “pre-minería”, lo que en la práctica significa que es el stress del “medio infinito” en una posición lo suficientemente lejana, de tal manera que no se vea influenciado por ninguna excavación o tipo de roca ajena a éste (recordar que los tipos de roca los definimos como una excavación relleno con un material que no es aire).

## Slide 30: DATUM
La figura de la derecha significa que en el medio infinito se tiene un DATUM que se encuentra en la cota (eje Z) 3193 [m]. TODA esa cota de ese medio tiene un S1 de 23[mpa], S2 de 15[mpa] y S3 de 5.5 [mpa] respectivamente
Asimismo, el esfuerzo en cualquier cota puede calcularse directamente sabiendo que las variaciones de los esfuerzos principales son -0.034 [mpa/m], -0.023[mpa/m] y -0.008 [mpa/m] para S1, S2 y S3 respectivamente.
Finalmente la orientación de los esfuerzos principales siempre queda determinada por un rumbo de 290 grados, un manteo de 80 grados, ambos para S1 y un rumbo de 99 grados para S3.
Los últimos 2 factores son para definir gradientes de temperatura, pero éstos no van a ser ocupados.
Analysis->Materials ->stress state