## Slide 1
Superintendencia Geología GRMD El Teniente Octubre 2008
Modelamiento Geológico Estructural en 3D (DFN) y sus aplicaciones en problemas de Mecánica de Rocas para la Minería
Miércoles 26 Octubre
Universidad de Chile, Departamento de Minas (sala por definir) entre 9:00am y 11:00am (en Español e Ingles).

## Slide 2
Superintendencia Geologia GRMD El Teniente Octubre 2008
Using the commercial FracMan software package, discrete fracture model (DFN) of the geological stockwork veins has been built at the El Teniente mine that honoured data collected in drill cores and mine drives. DFN models explicitly represent key vein structures in 3D and require as a minimum data, the orientation, the size and the intensity of the veins to be defined. The orientations of the structural data observed in oriented cores were used to bootstraps veins orientations within the modelled volume. The correlation between observed and simulated orientation data sets was evaluated by applying Chi-Square tests and the results were outstanding. Vein size was assessed through applying the simulated sampling technique to match the observed trace length measurements collected in wall mine drives. The results showed the stockwork veins as having small size with a mean around 1.0m for both lognormal and exponential size distributions. Discontinuity intensity was determined by conditioning linear vein frequency of the three different core measurements using vein orientation and size properties determined in previous modelling steps. Veins intensity, measured as the area of fracturing in a unit volume, was estimated as 46m2/m3, but for veins that control fragmentation and caving propagation, intensity values were estimated between 1m2/m3 and 5m2/m3
Dr. Andres Brzovic
Geologo Especialista (PhD Rock Mechanics) Codelco Chile Division El Teninte
Assessing Geological vein Size and Intensity using Discrete Fracture Network Modelling at the El Teniente Mine, Chile.

## Slide 3
Superintendencia Geologia GRMD El Teniente Octubre 2008
This presentation reviews brittle rock fracture simulations for rock engineering problems and discuss the approaches adopted to-date. Particular emphasis is given to the application of a hybrid finite-discrete element code incorporating fracture mechanics criteria to simulate a variety of engineering problems, including rock slope stability, cave mining mechanisms and fragmentation processes. The proposed numerical modeling approach has also been applied to the characterisation of rock mass strength at different scale under different loading conditions, including compression, shear and tensile loading. The strength of the approach is that the anisotropic, inhomogeneous spatial distribution and influence of the jointing can be fully accounted for and the resulting deformation and failure mechanisms simulated in a more realistic way. To be effective, the proposed approach has to ensure a correct balance of engineering judgment, the integration of characterised field data, and numerical modeling. This is particularly true when engineering design and artistic intent have to work together, as demonstrated by the application of the proposed integrated modelling technique to characterise rock mass properties for a mountain carving project
Dr. Davide Elmo
Rock Mechanics Specialist (Golder Associates, Vancouver, Canada)
Adjunct Professor (Simon Fraser University, Vancouver, Canada)
Integrated Finite/Discrete Element Modelling and Applications to Rock Engineering Problems