## Slide 1: Entendiendo mapas geológicos I Clase Auxiliar n°2
Diego Zamorano – Estefanía Avendaño
19 de marzo 2020
GL6101 Geología de Campo II 2019, Otoño

## Slide 2: CONTENIDO
1) Curvas de nivel
2) Reglas de las V
3) Perfil topográfico
3) Rumbo y manteo de un estrato en el mapa

## Slide 3: 1. CURVAS DE NIVEL
Líneas formadas por los puntos de de un mapa que tienen igual altura

## Slide 4: 1. CURVAS DE NIVEL
Permiten reconstruir perfiles topográficos
Pasar de 2D a 3D

## Slide 5: 1. CURVAS DE NIVEL
Para poder imaginar un mapa con solo curvas de nivel (incluso sin la cota, se puede seguir el siguiente método.
  Identificar los huevos fritos
  Identificar las quebradas y cuchillas
  Identificar los valles
(Forma de huevo frito)

## Slide 6: 1. CURVAS DE NIVEL
¿Qué ves?
En teoría, la forma de huevo frito puede ser un relieve positivo (cerro) o negativo (cuenca)
Una cuenca con forma de cerro invertido es MUY improbable (¿un cráter?)
Los huevos fritos son 99% cerros!
Notes: Mostrar ejercicio en pizarra y luego en arcgis

## Slide 7: Cuchillas y quebradas
Cuchilla
Quebrada
Cuchilla
Quebrada
Huevo Frito
Las quebradas apuntan hacia el cerro (huevo frito)
Las cuchillas apuntan hacia fuera del cerro

## Slide 8: EJERCICIO N°1 – Curvas de Nivel
EJERCICIO N°1 (En clase)
La siguiente imagen muestra un mapa de curvas de nivel cada 100 m en el sector “Chacay”
en Río Hurtado.
Señale los principales rasgos morfológicos de la zona (cerros, quebradas, cuchillas, valles
∆T = 5 minutos

## Slide 9: EJERCICIO N°1 – Solución
EJERCICIO N°1 (En clase)
La siguiente imagen muestra un mapa de curvas de nivel cada 100 m en el sector “Chacay”
en Río Hurtado.
Señale los principales rasgos morfológicos de la zona (cerros, quebradas, cuchillas, valles

## Slide 10: 2. REGLA DE LAS Vs
Permiten a simple vista concluir la dirección de inclinación, el rumbo y estimar el manteo del estrato o de la falla

## Slide 11: 2. REGLA DE LAS Vs
Capas verticales

## Slide 12: 2. REGLA DE LAS Vs
Capas horizontales

## Slide 13: 2. REGLA DE LAS Vs
Capas que mantean suavemente a favor de la pendiente

## Slide 14: 2. REGLA DE LAS Vs
Capas que mantean similar a la pendiente

## Slide 15: 2. REGLA DE LAS Vs
Capas que mantean en sentido opuesto a la pendiente

## Slide 16: REGLA DE LAS Vs
Capas que tienen mayor manteo que la pendiente
Notes: Hablar nomenclatura

## Slide 17: Opción 1) SI VA = A, SI VIENE = V Opción 2) SI se Aleja = A, SI VIENE = V
A
V
Nemotecnia
Notes: Hablar nomenclatura

## Slide 18
Capas horizontales
Capas verticales
Capas con suave manteo menor a la pendiente
Capas con manteo opuesto a la pendiente
Capas con manteo similar a la pendiente
Capas con mayor manteo que la pendiente

## Slide 19: EJERCICIO N° 2 – Regla de las V
∆T = 20 minutos

## Slide 20: 3. CONSTRUCCIÓN PERFIL TOPOGRÁFICO

## Slide 21
School of Earth and Environment
Constructing a cross section: Example
Step 1 :
First determine the line along which you are going to draw the section, it should:
      Be representative of the study area.
      Cross all major structural features (e.g. faults and folds)
      have appropriate data on the map or well logs to draw a complete section.
      Often be drawn perpendicular to major structural features.
Here is our original map. Fill in the example on exercise sheet 3 as we run through it.

## Slide 22
School of Earth and Environment
Constructing a cross section: Example
Step 2:
Now on some graph paper draw an x axis with the same scale and length as the line of the
cross section.
Then add y axes to both ends, that have a relevant scale to the topographic contours.
So that it looks something like this:

## Slide 23
School of Earth and Environment
Constructing a cross section: Example
Step 3 :
Using a scrap piece of paper, mark on where structure contours intercept your cross sectional line.

## Slide 24
School of Earth and Environment
Constructing a cross section: Example
Step 4 :
Now, overlay your scrap piece of paper with your cross section and mark on the different topographical contour points.

## Slide 25
School of Earth and Environment
Constructing a cross section: Example
Step 5 :
If you join these dots up, you should end up with an accurate scaled topographic cross section that looks something like the one below.

## Slide 26
School of Earth and Environment
Constructing a cross section: Example
Step 6 :
Now, with your scrap piece of paper add in where the lithological boundaries intercept your cross sectional line

## Slide 27
School of Earth and Environment
Step 7 :
Now, overlay your scrap piece of paper with your cross section and mark on the different lithological boundaries.
Constructing a cross section: Example

## Slide 28
School of Earth and Environment
Constructing a cross section: Example
Step 8 :
Now, extrapolate from these points the bed boundaries; If they dip, then draw the lines at the correct angle of dip for each bed.
However for this example, as the unit boundaries followed the contours, they are evidently horizontal (remember The Law of “V’s”)
Now you have drawn an accurate, to scale, cross section.

## Slide 29: 3. RUMBO Y MANTEO DE UN ESTRATO EN MAPA GEOLÓGICO
Método de los 2 puntos
500
600
D
D
100
r
m
r
r
m
= Rumbo
= Manteo